## Slide 1: 31-1-22: 2nd lecture in fluid mechanics
Hydrostatic pressure
Without flow (EFM 3.1-3.2)
Credit: Creative Commons
Cavitation is flowing systems
Pressure due to to flow (EFM 2.7)
Surface tension
EFM 2.6
Credit: USGS.gov
Pressure?

## Slide 2: Manifestations of surface tension (EFM 2.6) Surface tension controls wetting phenomena
All images from Creative Commons. Licensed under CC BY-SA-NC
Capillary rise
Floating objects
Surface tension controls size and shape of raindrops
Surface tension controls
jetting-dripping transition
Notes: Surface tension minimizes surface area

## Slide 3: Surface tension makes a liquid surface behave like a stretched membrane
tension
All images from Creative Commons. Licensed under CC BY-SA-NC
Weight of man equals tension
Notes: Like barn leker best/likt løser likt, så vannmolekylene tiltrekker seg andre vannmolekyler. Inni væsken trekker et vannmolekyl like mye I alle retninger, men et vannmolekyl på overflaten har ingen vannmolekyler over seg å trekke på; dermed trekker den hardere på molekylene på siden av seg og danner såkalte hydrogenbindinger, som er det som gir overflatespenningen.

## Slide 4: Surface tension makes a liquid surface behave like a stretched membrane
tension
Cohesive force
Cohesive force = attraction force between like molecules
(tiltrekningskraft mellom like molekyler)
All images from Creative Commons. Licensed under CC BY-SA-NC
Weight of man equals tension
Notes: Like barn leker best/likt løser likt, så vannmolekylene tiltrekker seg andre vannmolekyler. Inni væsken trekker et vannmolekyl like mye I alle retninger, men et vannmolekyl på overflaten har ingen vannmolekyler over seg å trekke på; dermed trekker den hardere på molekylene på siden av seg og danner såkalte hydrogenbindinger, som er det som gir overflatespenningen.

## Slide 5: Surface tension is a force along a fluid surface
surface tension ( =
All images from Creative Commons. Licensed under CC BY-SA-NC
Notes: Definition of surface tension

## Slide 6: Individual Exercise (5 min): Will it float? Paper clips on water
surface tension ( =
All images from Creative Commons. Licensed under CC BY-SA-NC
Small clips: mA=0.23 grams, wA=9 cm long
Large clips: mB=1.10 grams, wB=16 cm long
water-air): 73 mN/m
Gravity : g=9.8 m/s2
Calculate A: Will the small clip float?
Calculate B: Will the large clip float?
Notes: Next: Discuss with partner (2 min)

## Slide 7: Discuss with partner (2 min): Will it float? Paper clips on water
surface tension ( =
All images from Creative Commons. Licensed under CC BY-SA-NC
Small clips: mA=0.23 grams, wA=9 cm long
Large clips: mB=1.10 grams, wB=16 cm long
water-air): 73 mN/m
Gravity : 9.8 m/s2
Calculate/predict A: Will the small clip float?
Calculate/predict B: Will the large clip float?

## Slide 8: Poll A: Will the small clip float?
surface tension ( =
All images from Creative Commons. Licensed under CC BY-SA-NC
Small clips: mA=0.23 grams, wA=9 cm long
Large clips: mB=1.10 grams, wB=16 cm long
water-air): 73 mN/m
Gravity : g=9.8 m/s2
Calculate A: Will the small clip float? Hypothesis A
Calculate B: Will the large clip float? Hypothesis B

## Slide 9: Poll B: Will the large clip float?
surface tension ( =
All images from Creative Commons. Licensed under CC BY-SA-NC
Small clips: mA=0.23 grams, wA=9 cm long
Large clips: mB=1.10 grams, wB=16 cm long
water-air): 73 mN/m
Gravity : g=9.8 m/s2
Calculate/predict A: Will the small clip float?
Calculate/predict B: Will the large clip float?

## Slide 10: Calculation: Force balance on a paper clip floating on water
surface tension ( =
All images from Creative Commons. Licensed under CC BY-SA-NC
Input parameters:
Small clips: mA=0.23 grams, wA=9 cm long
Large clips: mB=1.10 grams, wB=16 cm long
water-air): 73 mN/m
Gravity : g=9.8 m/s2
Calculation A (small clip):
Require: Fg,A / wA < (weight < surface tension)
mA g/wA = 25 mN/m < 73 mN/m (it should float!)
Calculation B (big clip):
Require: Fg,B / wB < (weight < surface tension)
mA g/wA = 67 mN/m < 73 mN/m (it should also float!)

## Slide 11: In-class experiment (2 min): Pair with partner. Grab a large or a small clip
surface tension ( =
All images from Creative Commons. Licensed under CC BY-SA-NC
Small clips: 0.23 grams, 9 cm long
Large clips: 1.10 grams, 16 cm long
water-air): 73 mN/m
Gravity : 9.8 m/s2
Test hypothesis A: Did the small clip float?
Test hypothesis B: Did the large clip float?

## Slide 12: In-class discussion: Did your experiment confirm your hypothesis?
surface tension ( =
All images from Creative Commons. Licensed under CC BY-SA-NC
Small clips: 0.23 grams, 9 cm long
Large clips: 1.10 grams, 16 cm long
water-air): 73 mN/m
Gravity : 9.8 m/s2
Experiment A: How did theory and experiment
compare?
Experiment B: How did theory and experiment
compare?
Notes: At-home exercise: Add a drop of soap to see what happens

## Slide 13: Pressure is a force per unit area (EFM 2.7,3.1-3.2) Pressure [=] N/m2
All images from Creative Commons. Licensed under CC BY-SA-NC
Capillary pressure
Pressure inside a bubble is higher than pressure outside (Ex. 2.3, EFM 2.7)
Static pressure (no flow)
Pascal’s exploding bucket
Vapor pressure = damptrykk
Flow can induce cavitation by bringing pressure below vapor pressure
Notes: Siste før pausen: Labassistentene informerer!
Etter pausen: trykk! Trykk en en normalkraft fordelt på et areal. Tegnestift (same kraft, ulikt areal). Barometer: 1 bar = 100kPa (1 atm = 1.01 bar = weight of the atmosphere at sea level at 25 oC ). Hydrostatisk trykk: p = rho(T)*g*h (Pascals prinsipp. Experiment: Pascal’s barrel).
Strømning:
Undertrykk (vacuum pressure) = differansen mellom et referansetrykk og et lavere trykk i systemet : prinsippet for vacuumpumper, seiling (mot vinden), helikoptere?, …
Differensialtrykk p(differential pressure): pA – pB > 0. Damptrykk:
We live submerged at the bottom of an ocean of the element air, which by unquestioned experiments is known to have weight. (Evangelista Torricelli, 1608-1647)
In Aerodynamics, L.J. Clancy[7] writes: "To distinguish it from the total and dynamic pressures, the actual pressure of the fluid, which is associated not with its motion but with its state, is often referred to as the static pressure, but where the term pressure alone is used it refers to this static pressure."
Siste før pausen: Labassistentene informerer!
Etter pausen: trykk! Trykk en en normalkraft fordelt på et areal. Tegnestift (same kraft, ulikt areal). Barometer: 1 bar = 100kPa (1 atm = 1.01 bar = weight of the atmosphere at sea level at 25 oC ). Hydrostatisk trykk: p = rho(T)*g*h (Pascals prinsipp. Experiment: Pascal’s barrel).
Strømning:
Undertrykk (vacuum pressure) = differansen mellom et referansetrykk og et lavere trykk i systemet : prinsippet for vacuumpumper, seiling (mot vinden), helikoptere?, …
Differensialtrykk Δ p(differential pressure): pA – pB > 0. Damptrykk:
We live submerged at the bottom of an ocean of the element air, which by unquestioned experiments is known to have weight. (Evangelista Torricelli, 1608-1647)
In Aerodynamics, L.J. Clancy[7] writes: "To distinguish it from the total and dynamic pressures, the actual pressure of the fluid, which is associated not with its motion but with its state, is often referred to as the static pressure, but where the term pressure alone is used it refers to this static pressure."

## Slide 14: Four main types of static pressures: Capillary, hydrostatic, gauge, and absolute pressure (EFM 2.7, 3.1-3.2)
All images from Creative Commons. Licensed under CC BY-SA-NC
Hydrostatic pressure
Pressure due to the weight of a column of fluid
Vapor pressure = damptrykk
Pressure?
Notes: Siste før pausen: Labassistentene informerer!
Etter pausen: trykk! Trykk en en normalkraft fordelt på et areal. Tegnestift (same kraft, ulikt areal). Barometer: 1 bar = 100kPa (1 atm = 1.01 bar = weight of the atmosphere at sea level at 25 oC ). Hydrostatisk trykk: p = rho(T)*g*h (Pascals prinsipp. Experiment: Pascal’s barrel).
Strømning:
Undertrykk (vacuum pressure) = differansen mellom et referansetrykk og et lavere trykk i systemet : prinsippet for vacuumpumper, seiling (mot vinden), helikoptere?, …
Differensialtrykk p(differential pressure): pA – pB > 0. Damptrykk:
We live submerged at the bottom of an ocean of the element air, which by unquestioned experiments is known to have weight. (Evangelista Torricelli, 1608-1647)
In Aerodynamics, L.J. Clancy[7] writes: "To distinguish it from the total and dynamic pressures, the actual pressure of the fluid, which is associated not with its motion but with its state, is often referred to as the static pressure, but where the term pressure alone is used it refers to this static pressure."
Siste før pausen: Labassistentene informerer!
Etter pausen: trykk! Trykk en en normalkraft fordelt på et areal. Tegnestift (same kraft, ulikt areal). Barometer: 1 bar = 100kPa (1 atm = 1.01 bar = weight of the atmosphere at sea level at 25 oC ). Hydrostatisk trykk: p = rho(T)*g*h (Pascals prinsipp. Experiment: Pascal’s barrel).
Strømning:
Undertrykk (vacuum pressure) = differansen mellom et referansetrykk og et lavere trykk i systemet : prinsippet for vacuumpumper, seiling (mot vinden), helikoptere?, …
Differensialtrykk Δ p(differential pressure): pA – pB > 0. Damptrykk:
We live submerged at the bottom of an ocean of the element air, which by unquestioned experiments is known to have weight. (Evangelista Torricelli, 1608-1647)
In Aerodynamics, L.J. Clancy[7] writes: "To distinguish it from the total and dynamic pressures, the actual pressure of the fluid, which is associated not with its motion but with its state, is often referred to as the static pressure, but where the term pressure alone is used it refers to this static pressure."

## Slide 15: Static pressures: Hydrostatic pressure is the pressure due to the weight of a column of fluid (EFM 3.1-3.2)
All images from Creative Commons. Licensed under CC BY-SA-NC
Hydrostatic pressure
Pressure due to the weight of a column of fluid
Vapor pressure = damptrykk
Pressure?
Notes: Siste før pausen: Labassistentene informerer!
Etter pausen: trykk! Trykk en en normalkraft fordelt på et areal. Tegnestift (same kraft, ulikt areal). Barometer: 1 bar = 100kPa (1 atm = 1.01 bar = weight of the atmosphere at sea level at 25 oC ). Hydrostatisk trykk: p = rho(T)*g*h (Pascals prinsipp. Experiment: Pascal’s barrel).
Strømning:
Undertrykk (vacuum pressure) = differansen mellom et referansetrykk og et lavere trykk i systemet : prinsippet for vacuumpumper, seiling (mot vinden), helikoptere?, …
Differensialtrykk p(differential pressure): pA – pB > 0. Damptrykk:
We live submerged at the bottom of an ocean of the element air, which by unquestioned experiments is known to have weight. (Evangelista Torricelli, 1608-1647)
In Aerodynamics, L.J. Clancy[7] writes: "To distinguish it from the total and dynamic pressures, the actual pressure of the fluid, which is associated not with its motion but with its state, is often referred to as the static pressure, but where the term pressure alone is used it refers to this static pressure."
Siste før pausen: Labassistentene informerer!
Etter pausen: trykk! Trykk en en normalkraft fordelt på et areal. Tegnestift (same kraft, ulikt areal). Barometer: 1 bar = 100kPa (1 atm = 1.01 bar = weight of the atmosphere at sea level at 25 oC ). Hydrostatisk trykk: p = rho(T)*g*h (Pascals prinsipp. Experiment: Pascal’s barrel).
Strømning:
Undertrykk (vacuum pressure) = differansen mellom et referansetrykk og et lavere trykk i systemet : prinsippet for vacuumpumper, seiling (mot vinden), helikoptere?, …
Differensialtrykk Δ p(differential pressure): pA – pB > 0. Damptrykk:
We live submerged at the bottom of an ocean of the element air, which by unquestioned experiments is known to have weight. (Evangelista Torricelli, 1608-1647)
In Aerodynamics, L.J. Clancy[7] writes: "To distinguish it from the total and dynamic pressures, the actual pressure of the fluid, which is associated not with its motion but with its state, is often referred to as the static pressure, but where the term pressure alone is used it refers to this static pressure."

## Slide 16: Static pressures: Hydrostatic pressure is the pressure due to the weight of a column of fluid (EFM 3.1-3.2)
All images from Creative Commons. Licensed under CC BY-SA-NC
Hydrostatic pressure
Pressure due to the weight of a column of fluid
Vapor pressure = damptrykk
Pressure?
Notes: Siste før pausen: Labassistentene informerer!
Etter pausen: trykk! Trykk en en normalkraft fordelt på et areal. Tegnestift (same kraft, ulikt areal). Barometer: 1 bar = 100kPa (1 atm = 1.01 bar = weight of the atmosphere at sea level at 25 oC ). Hydrostatisk trykk: p = rho(T)*g*h (Pascals prinsipp. Experiment: Pascal’s barrel).
Strømning:
Undertrykk (vacuum pressure) = differansen mellom et referansetrykk og et lavere trykk i systemet : prinsippet for vacuumpumper, seiling (mot vinden), helikoptere?, …
Differensialtrykk p(differential pressure): pA – pB > 0. Damptrykk:
We live submerged at the bottom of an ocean of the element air, which by unquestioned experiments is known to have weight. (Evangelista Torricelli, 1608-1647)
In Aerodynamics, L.J. Clancy[7] writes: "To distinguish it from the total and dynamic pressures, the actual pressure of the fluid, which is associated not with its motion but with its state, is often referred to as the static pressure, but where the term pressure alone is used it refers to this static pressure."
Siste før pausen: Labassistentene informerer!
Etter pausen: trykk! Trykk en en normalkraft fordelt på et areal. Tegnestift (same kraft, ulikt areal). Barometer: 1 bar = 100kPa (1 atm = 1.01 bar = weight of the atmosphere at sea level at 25 oC ). Hydrostatisk trykk: p = rho(T)*g*h (Pascals prinsipp. Experiment: Pascal’s barrel).
Strømning:
Undertrykk (vacuum pressure) = differansen mellom et referansetrykk og et lavere trykk i systemet : prinsippet for vacuumpumper, seiling (mot vinden), helikoptere?, …
Differensialtrykk Δ p(differential pressure): pA – pB > 0. Damptrykk:
We live submerged at the bottom of an ocean of the element air, which by unquestioned experiments is known to have weight. (Evangelista Torricelli, 1608-1647)
In Aerodynamics, L.J. Clancy[7] writes: "To distinguish it from the total and dynamic pressures, the actual pressure of the fluid, which is associated not with its motion but with its state, is often referred to as the static pressure, but where the term pressure alone is used it refers to this static pressure."

## Slide 17: Excercise: Individual (2 min) + pair wise (1 min): What is the hydrostatic pressure 10 meters below sea level in bars?
All images from Creative Commons. Licensed under CC BY-SA-NC
Hydrostatic pressure
Pressure due to the weight of a column of fluid
Pressure?
Useful info:
1 bar = 100 kPa
Seawater is heavier than
freshwater due to dissolved salt ions

## Slide 18: Static pressures: Gauge pressure is the pressure relative to the ambient atmospheric pressure
All images from Creative Commons. Licensed under CC BY-SA-NC
The tire pressure is a gauge pressure and is measured relative to the atmospheric pressure
The absolute pressure is the actual pressure inside the tire
Gauge pressure = overtrykk

## Slide 19: Fluid flow leads to a pressure reduction which can induce boiling. This, in turn, leads to cavitation and water hammers
All images from Creative Commons. Licensed under CC BY-SA-NC
Cavitation in rotating machinery
Implosion induced by a
water hammer

## Slide 20: Energy balance is conserved in dynamic systems: (Etot = Etot,1 –Etot,2 = 0)
All images from Creative Commons. Licensed under CC BY-SA-NC
Potential energy (1) is converted to kinetic energy (2) in a rollercoaster.
Etot = 0
(1): Epotential = mgh
(2): Ekinetic=1/2mu2
h

## Slide 21: Energy can also be stored as pressure: pressure volume = p1V1 (
All images from Creative Commons. Licensed under CC BY-SA-NC
Potential energy (1) is converted to kinetic energy (2) in a rollercoaster
(2): Ekinetic=1/2mu2
p
p1
(1): Epotential = mgh
h
Pressure p1 inside a close container with volume V1
Kinetic energy is zero
pref = 0

## Slide 22: Energy can also be stored as pressure: pressure volume = p1V1 (
All images from Creative Commons. Licensed under CC BY-SA-NC
Potential energy (1) is converted to kinetic energy (2) in a rollercoaster
(2): Ekinetic=1/2mu2
p
p1
(1): Epotential = mgh
h
Pressure p1 inside a close container with volume V1
Kinetic energy is zero
pref = 0
What is we punch a hole in the wall between the containers?

## Slide 23: Potential energy is converted to kinetic energy upon pressure release: +
All images from Creative Commons. Licensed under CC BY-SA-NC
Potential energy (1) is converted to kinetic energy (2) in a rollercoaster
(2): Ekinetic=1/2mu2
p
p2< p1
(1): Epotential = mgh
h
Kinetic flow energy: 1/2mu2
p2< p1

## Slide 24: The energy equation yields: + = +
All images from Creative Commons. Licensed under CC BY-SA-NC
Potential energy (1) is converted to kinetic energy (2) in a rollercoaster
(2): Ekinetic=1/2mu2
(1): Epotential = mgh
h
p
p2< p1
Kinetic flow energy: 1/2mu2
p2< p1

## Slide 25: We divide by volume to get the total energy expressed in pressure units [N/m2]: + = +
All images from Creative Commons. Licensed under CC BY-SA-NC
Potential energy (1) is converted to kinetic energy (2) in a rollercoaster
(2): Ekinetic=1/2mu2
(1): Epotential = mgh
h
p
p2< p1
Kinetic flow energy: 1/2mu2
p2< p1

## Slide 26: We divide by volume to get the total energy expressed in pressure units [N/m2]: + = +
All images from Creative Commons. Licensed under CC BY-SA-NC
Potential energy (1) is converted to kinetic energy (2) in a rollercoaster
(2): Ekinetic=1/2mu2
p
p2
(1): Epotential = mgh
h
Flow energy: 1/2mu2
In words: When the velocity goes up,
the pressure goes down (and vice-versa).

## Slide 27: EFM 2.7: Vapor pressure is the pressure at which the liquid and vapor phase are in thermal equilibrium
All images from Creative Commons. Licensed under CC BY-SA-NC
Cavitation: Boiling at low pressure
Pressure < vapor pressure
Phase diagram for water
What’s the phase for a given T, p?
Vapor pressure = damptrykk
Notes: Siste før pausen! Summen av statisk og dynamisk trykk er konstant (langs en strømlinje) i en tapsfri strømning (dvs. hvor vi kan se bort fra friksjon, i.e. høye Re). Means: The vapor and liquid phase coexist at a fixed temperature (there is no exchange of energy within the system).