## Slide 1: Operating Systems: Storage: Disks & File Systems
IN2140: Introduction to Operating Systems and Data Communication

## Slide 2: Overview
(Mechanical) Disks
Disk scheduling
Memory/buffer caching
File systems
Some trends and “new” technologies …

## Slide 3: Disks
Disks ...
  are used to have a persistent system
  are cheaper compared to main memory
  have more capacity
  are orders of magnitude slower
Two resources of importance
  storage space
  I/O bandwidth
We must look closer on how to manage disks, because...
  ...there is a large speed-mismatch (ms vs. ns) compared to main memory
  ...disk I/O is often the main performance bottleneck
cache(s)
main memory
tertiary storage (tapes)
secondary storage (disks)

## Slide 4: Why spend a lecture talking about HDDs?
SSDs are persistent and
  “almost like memory” (no mechanical parts)
  much faster (ms vs µs)
  but, more expensive (price per byte, but also shorter lifetime)
Many devices:
  Google 2012
  417,600 servers - Douglas County, USA
  204,160 servers - The Dalles, USA
  241,280 servers - Council Bluffs, USA
  139,200 servers – Lenoir, USA
  250,560 servers - Moncks Corner, USA
  296,960 servers - St. Ghislain, Belgium
  116,000 servers - Hamina, Finland
  125,280 servers - Mayes County, USA
  Google Early 2013
  46,400 servers - Profile Park, Dublin, Ireland
  200,000 servers - Jurong West, Singapore (projected estimate)
  200,000 servers - Kowloon, Hong Kong (projected estimate)
  139,200 servers - Mayes County, USA
  Estimated grand total: 2,376,640 (early 2013 – 3 more centers in 2019)
  one 0.5 TB SSD in each
    Seagate HDD at Komplett: 1.4 billion NOK
    Intel P3700 SSD: 17.7 billion NOK
  one 4 TB in each
    Seagate HDD at Komplett: 4.1 billion NOK
    Samsung SSD at komplett: 17.8 billion NOK (2 TB)
    Intel P3608 SSD: 160 billion NOK
Google data center locations (2019):
Mechanical HDDs will exist for a long time….!
~10x price
Notes: HDD Komplett 0.5 TB (2015) = 579 NOK
4 TB (2015) = 1749 NOK
The highest endurance Intel P3700 drive is priced at around $3/GB (2014)  17.7 miliarder NOK hvis hver bare har 1 disk ++ alt arbeidet
Komplett 2015: Samsung 850 EVO 2TB SSD  7500 NOK  17,8 milliarder NOK
The intel P3608, 4 TB : $8,759  20 milliarder DOLLAR = 160 B NOK
Picture is from MAYES COUNTY, OKLAHOMA
https://www.google.com/about/datacenters/inside/locations/index.html
In 2011, Google had 1 Mill servers
In 2013: Microsoft had 1 Mill servers

## Slide 5: Mechanics of Disks

## Slide 6: Mechanics of Disks
Platters circular platters covered with magnetic material to provide nonvolatile storage of bits
Tracks concentric circles on a single platter
Sectors segment of the track circle – usually each contains 512 bytes – separated by non-magnetic gaps. The gaps are often used to identify beginning of a sector
Cylinders corresponding tracks on the different platters are said to form a cylinder
Spindle of which the platters rotate around
Disk heads read or alter the magnetism (bits) passing under it. The heads are attached to an arm enabling it to move across the platter surface
Notes: Some new drives have sectors of 4096

## Slide 7: Disk Capacity
The size (storage space) of the disk is dependent on
  the number of platters
  whether the platters use one or both sides
  number of tracks per surface
  (average) number of sectors per track
  number of bytes per sector
Example (Cheetah X15.1):
  4 platters using both sides: 8 surfaces
  18497 tracks per surface
  617 sectors per track (average)
  512 bytes per sector
  Total capacity = 8 x 18497 x 617 x 512  4.6 x 1010 = 42.8 GB
  Formatted capacity = 36.7 GB
Note: there is a difference between formatted and total capacity. Some of the capacity is used for storing checksums, spare tracks, etc.
Notes: Some new drives have sectors of 4096 B

## Slide 8: Disk Access Time
How do we retrieve data from disk?
  position head over the cylinder (track) on which the block (consisting of one or more sectors) is located
  read (or write) the data block as the sectors are moved under the head when the platters rotate
The time between the moment issuing a disk request and the time the block is resident in memory is called disk latency or disk access time

## Slide 9: Disk Access Time
+ Rotational delay
+ Transfer time
Seek time
Disk access time =
+ Other delays
Disk platter
Disk arm
Disk head
block x
in memory
I want
block X

## Slide 10: Disk Access Time: Seek Time
Seek time is the time to position the head
  time is used for actually moving the head – roughly proportional to the number of cylinders traveled
  time to start and stop moving the head
  time to move head:
~ 10x - 20x
x
1
N
Cylinders Traveled
Time
“Typical” average: 10 ms  40 ms (old) 7.4 ms (Barracuda 180) 5.7 ms (Cheetah 36) 3.6 ms (Cheetah X15)
number of tracks
seek time constant
fixed overhead

## Slide 11: Disk Access Time: Rotational Delay
Time for the disk platters to rotate so the first of the required sectors are under the disk head
head here
block I want
Average delay is 1/2 revolution “Typical” average: 8.33 ms (3.600 RPM) 5.56 ms (5.400 RPM) 4.17 ms (7.200 RPM) 3.00 ms (10.000 RPM) 2.00 ms (15.000 RPM)
Notes: 15.000 RPM = 250 RPS = 4 ms per rotasjon  2 ms gjennomsnittlig rotasjonsforsinkelse

## Slide 12: Disk Access Time: Transfer Time
Time for data to be read by the disk head, i.e., time it takes the sectors of the requested block to rotate under the head
Transfer time is dependent on data density and rotation speed
Transfer rate =
Transfer time = =
Transfer rate example
  Barracuda 180: 406 KB per track x 7.200 RPM  47.58 MB/s
  Cheetah X15: 306 KB per track x 15.000 RPM  77.15 MB/s
If we have to change track, time must also be added for moving the head
amount of data per track time per rotation
Note: one might achieve these transfer rates reading continuously on disk, but time must be added for seeks, etc.
amount of data to read * time per rotation
amount of data per track
amount of data to read
transfer rate

## Slide 13: Disk Access Time: Other Delays
There are several other factors which might introduce additional delays:
  CPU time to issue and process I/O
  contention for controller, bus, memory
  verifying block correctness with checksums (retransmissions)
  waiting in scheduling queue
  ...
Typical values: “0” (maybe except from waiting in the scheduling queue)

## Slide 14: Disk Specifications
Some existing (Seagate) disks:
Note 1: disk manufacturers usually
denote GB as 109 whereas computer quantities often are powers of 2, i.e., GB is 230
Note 3: there is usually a trade off between speed and capacity
Note 2: there is a difference between internal and formatted transfer rate. Internal is only between platter. Formatted is after the signals interfere with the electronics (cabling loss, interference, retransmissions, checksums, etc.)
 | Barracuda 180 | Cheetah 36 | Cheetah X15.3
Capacity (GB) | 181.6 | 36.4 | 73.4
Spindle speed (RPM) | 7200 | 10.000 | 15.000
#cylinders | 24.247 | 9.772 | 18.479
average seek time (ms) | 7.4 | 5.7 | 3.6
min (track-to-track) seek (ms) | 0.8 | 0.6 | 0.2
max (full stroke) seek (ms) | 16 | 12 | 7
average latency (ms) | 4.17 | 3 | 2
internal transfer rate (Mbps) | 282 – 508 | 520 – 682 | 609 – 891
Notes: http://www.seagate.com/files/docs/pdf/datasheet/disc/cheetah-15k.7-ds1677.3-1007us.pdf :
X15.7 has more capasity and higher transfer rates, but almost the same seek/rotation latencies (3.4 / 0.2 / 2)

## Slide 15: Writing and Modifying Blocks
A write operation is analogous to read operations
  must potentially add time for block allocation
  a complication occurs if the write operation has to be verified – must usually wait another rotation and then read the block again
  Total write time  read time (+ time for one rotation)
A modification operation is similar to read and write operations
  cannot modify a block directly:
    read block into main memory
    modify the block
    write new content back to disk
  Total modify time  read time (+ time to modify) + write time

## Slide 16: Disk Controllers
To manage the different parts of the disk, we use a disk controller, which is a small processor capable of:
  controlling the actuator moving the head to the desired track
  selecting which head (platter and surface) to use
  knowing when the right sector is under the head
  transferring data between main memory and disk

## Slide 17: Efficient Secondary Storage Usage
Must take into account the use of secondary storage
  large gaps in access times between disks and memory, i.e., a disk access will probably dominate the total execution time
  huge performance improvements if we reduce the number of disk accesses
  a “slow” algorithm with few disk accesses will probably outperform a “fast” algorithm with many disk accesses
Several ways to optimize .....
  block size - 4 KB
  disk scheduling - SCAN derivate
  file management / data placement - various
  memory caching / replacement algorithms - LRU variant
  prefetching - read-ahead
  multiple disks - a specific RAID level
  …

## Slide 18: Disk Scheduling

## Slide 19: Disk Scheduling
How to most efficiently fetch the parcels I want?
Notes: Indiana Jones – Hangar 51

## Slide 20: Disk Scheduling
Seek time is the dominant factor of the total disk I/O time
IDEA: Let the operating system or disk controller choose which request to serve next depending on the head’s current position and requested block’s position on disk (disk scheduling)
Note that disk scheduling  CPU scheduling
  a mechanical device – hard to determine (accurate) access times
  disk accesses can/should not be preempted – run until they finish
General goals
  short response time
  high overall throughput
  fairness (equal probability for all blocks to be accessed in the same time)
Tradeoff: seek efficiency vs. maximum response time

## Slide 21: Disk Scheduling
Several traditional algorithms
  First-Come-First-Serve (FCFS)
  Shortest Seek Time First (SSTF)
  SCAN (and variations)
  Look (and variations)
  …
A LOT of different algorithms exist depending on expected access pattern

## Slide 22: First–Come–First–Serve (FCFS)
FCFS (FIFO) serves the first arriving request first:
Long seeks
“Short” response time for all
time
cylinder number
1
5
10
15
20
25
12
incoming requests (in order of arrival, denoted by cylinder number):
14
2
7
21
8
24
scheduling
queue
24
8
21
7
2
14
12

## Slide 23: Shortest Seek Time First (SSTF)
SSTF serves closest request first:
short seek times
longer maximum response times – may even lead to starvation
time
cylinder number
1
5
10
15
20
25
12
incoming requests (in order of arrival):
14
2
7
21
8
24
scheduling
queue
24
8
21
7
2
14
12
arrived first, served last
Notes: køen går av seg selv fra og med 7

## Slide 24: SCAN
SCAN (elevator) moves head edge to edge and serves requests on the way:
bi-directional
compromise between response time and seek time optimizations
time
cylinder number
1
5
10
15
20
25
12
incoming requests (in order of arrival):
14
2
7
21
8
24
scheduling
queue
24
8
21
7
2
14
12

## Slide 25: SCAN vs. FCFS
Disk scheduling makes a difference!
In this case, we see that SCAN requires much less head movement compared to FCFS
  here 37 vs. 75 tracks
  imagine having
    20.000++ tracks
    many users
    many files
    …
cylinder number
1
5
10
15
20
25
time
time
12
incoming requests (in order of arrival):
14
2
7
21
8
24
FCFS
SCAN

## Slide 26: C–SCAN
Circular-SCAN moves head from edge to edge
optimization of SCAN
serves requests on one way – uni-directional
improves response time (fairness)
time
cylinder number
1
5
10
15
20
25
12
incoming requests (in order of arrival):
14
2
7
21
8
24
scheduling
queue
24
8
21
7
2
14
12

## Slide 27: SCAN vs. C–SCAN
Why is C-SCAN in average better in reality than SCAN when both service the same number of requests in two passes?
  modern disks must accelerate (speed up and down) when seeking
  head movement formula:
SCAN | C-SCAN
bi-directional | uni-directional
requests: n avg. dist: 2x (spread over both directions) total cost: | requests: n avg. dist: x (over one direction only + one full pass) total cost:
cylinders traveled
time
number of cylinders
seek time constant
fixed overhead
if n is large:

## Slide 28: LOOK and C–LOOK
LOOK (C-LOOK) is a variation of SCAN (C-SCAN):
same schedule as SCAN
does not run to the edges
stops and returns at outer- and innermost requests
increased efficiency
SCAN vs. LOOK example:
time
cylinder number
1
5
10
15
20
25
12
incoming requests (in order of arrival):
14
2
7
21
8
24
scheduling
queue
24
8
21
7
2
14
12

## Slide 29: V–SCAN(R)
V-SCAN(R) combines SCAN (or LOOK) and SSTF
  define an R-sized unidirectional SCAN window, i.e., C-SCAN, and use SSTF outside the window
  Example: V-SCAN(0.6)
    makes a C-SCAN window over 60 % of the cylinders
    uses SSTF for requests outside the window
  V-SCAN(0.0) equivalent with SSTF
  V-SCAN(1.0) equivalent with C-SCAN
  V-SCAN(0.2) is supposed to be an appropriate configuration
cylinder number
1
5
10
15
20
25

## Slide 30: Modern Disk Scheduling
Disk used to be simple devices and disk scheduling used to be performed by OS (file system or device driver) only…
… but, new disks are more complex
  hide their true layout, e.g.,
    only logical block numbers
    different number of surfaces, cylinders, sectors, etc.
OS view
real view

## Slide 31: Modern Disk Scheduling
Disk used to be simple devices and disk scheduling used to be performed by OS (file system or device driver) only…
… but, new disks are more complex
  hide their true layout
  transparently move blocks to spare cylinders
    e.g., due to bad disk blocks
OS view
real view

## Slide 32: Modern Disk Scheduling
Constant angular velocity (CAV) disks
  constant rotation speed
  equal amount of data in each track
  thus, constant transfer time
OS view
real view
Disk used to be simple devices and disk scheduling used to be performed by OS (file system or device driver) only…
… but, new disks are more complex
  hide their true layout
  transparently move blocks to spare cylinders
  have different zones
Zoned CAV disks
  constant rotation speed
  zones are ranges of tracks
  typical few zones
  the different zones have different amount of data, i.e., more better on outer tracks
  thus, variable transfer time
Zone | Cylinders per Zone | Sectors per Track | Zone Transfer Rate (MBps) | Sectors per Zone | Efficiency | Formatted Capacity (MB)
1 | 3544 | 672 | 890,98 | 19014912 | 77,2% | 9735,635
2 | 3382 | 652 | 878,43 | 17604000 | 76,0% | 9013,248
3 | 3079 | 624 | 835,76 | 15340416 | 76,5% | 7854,293
4 | 2939 | 595 | 801,88 | 13961080 | 76,0% | 7148,073
5 | 2805 | 576 | 755,29 | 12897792 | 78,1% | 6603,669
6 | 2676 | 537 | 728,47 | 11474616 | 75,5% | 5875,003
7 | 2554 | 512 | 687,05 | 10440704 | 76,3% | 5345,641
8 | 2437 | 480 | 649,41 | 9338880 | 75,7% | 4781,506
9 | 2325 | 466 | 632,47 | 8648960 | 75,5% | 4428,268
10 | 2342 | 438 | 596,07 | 8188848 | 75,3% | 4192,690
Seagate X15.3:

## Slide 33: Modern Disk Scheduling
Constant angular velocity (CAV) disks
  constant rotation speed
  equal amount of data in each track
  thus, constant transfer time
OS view
real view
Disk used to be simple devices and disk scheduling used to be performed by OS (file system or device driver) only…
… but, new disks are more complex
  hide their true layout
  transparently move blocks to spare cylinders
  have different zones
Zoned CAV disks
  constant rotation speed
  zones are ranges of tracks
  typical few zones
  the different zones have different amount of data, i.e., more better on outer tracks
  thus, variable transfer time
For handouts

## Slide 34: Modern Disk Scheduling
Disk used to be simple devices and disk scheduling used to be performed by OS (file system or device driver) only…
… but, new disks are more complex
  hide their true layout
  transparently move blocks to spare cylinders
  have different zones
  head accelerates – most algorithms assume linear movement overhead
~ 10x - 20x
x
1
N
Cylinders Traveled
Time

## Slide 35: Modern Disk Scheduling
Disk used to be simple devices and disk scheduling used to be performed by OS (file system or device driver) only…
… but, new disks are more complex
  hide their true layout
  transparently move blocks to spare cylinders
  have different zones
  head accelerates – most algorithms assume linear movement overhead
  on device buffer caches may use read-ahead prefetching
disk
buffer
disk

## Slide 36: Modern Disk Scheduling
Disk used to be simple devices and disk scheduling used to be performed by OS (file system or device driver) only…
… but, new disks are more complex
  hide their true layout
  transparently move blocks to spare cylinders
  have different zones
  head accelerates – most algorithms assume linear movement overhead
  on device buffer caches may use read-ahead prefetching
  “smart” with build-in low-level scheduler (usually SCAN-derivate)
  we cannot fully control the device (black box)
OS could (should?) focus on high level scheduling only!??

## Slide 37: Schedulers today (Linux)?
Elevator – SCAN
NOOP
  FCFS with request merging
Deadline I/O
  C-SCAN based
  3 queues: 1 sorted (elevator) queue, and 2 deadline queues (one for read and one for write)
Anticipatory
  same queues as in Deadline I/O
  delays decisions to be able to merge more requests
Completely Fair Queuing (CFQ)
  1 queue per process (periodic access, but period length depends on load)
  gives time slices and ordering according to priority level (real-time, best-effort, idle)
  selects requests from queues in RR for the final elevator sorting
  work-conserving
$> more /sys/block/sda/queue/scheduler
noop deadline [cfq]
Notes: Deadline:
read priority over write,
respective deadlines are 0.5 and 5 seconds
if no deadlines have expired, select a batch from SCAN
Anticipatory;
http://www.linux-mag.com/id/7724/ :
It has been observed that the Apache web server may achieve up to 71% more throughput using the anticipatory IO scheduler. On the other hand, it has been observed that the anticipatory scheduler has caused up to a 15% slowdown on a database run.
The anticipatory IO schduler was a mixed bag overall, helping some workloads and hurting others. In the 2.6.33 kernel, Linus decided that the CFQ (Completely Fair Queue) Scheduler had a broad range of capabilities beyond the desktop to include servers, so the anticipatory scheduler was removed from the 2.6.33 kernel.

## Slide 38: Schedulers today (Windows)?
Well, a bit hard to say, but…
I/O priorities
  individual I/O operations
    FIFO within each queue
    to avoid low-priority starvation, a timer enforce ONE I/O per time unit (.5 sec)
  reservations
  many special functions: fast I/O, I/O boosts and bumps, …
https://www.microsoftpressstore.com/articles/article.aspx?p=2201309&seqNum=3
Notes: https://www.microsoftpressstore.com/articles/article.aspx?p=2201309&seqNum=3
Without I/O priority, background activities like search indexing, virus scanning, and disk defragmenting can severely impact the responsiveness of foreground operations. A user launching an application or opening a document while another process is performing disk I/O, for example, experiences delays as the foreground task waits for disk access. The same interference also affects the streaming playback of multimedia content like music from a disk.
Windows includes two types of I/O prioritization to help foreground I/O operations get preference: priority on individual I/O operations and I/O bandwidth reservations.
5 levels of priorities supported, 3 used. As each application generates I/Os, I/O request packets (IRPs) are put on different I/O queues based on their priority, and the hierarchy strategy decides the ordering of the operations.
FIFO queue for each.
Windows I/O bandwidth reservation support is useful for applications that desire consistent I/O throughput. Using the SetFileBandwidthReservation call, a media player application asks the I/O system to guarantee it the ability to read data from a device at a specified rate. The I/O system won’t service other I/Os unless it can satisfy the requirements of applications that have made reservations on the target storage device.
A few other subtle modifications to normal I/O paths are used by Windows to avoid starvation, inversion, or otherwise unwanted scenarios when I/O priority is being used. Typically, these modifications are done by boosting I/O priority when needed.

## Slide 39: Cooperative user-kernel space scheduling
Some times the kernel does not have enough information to make an efficient schedule
File tree traversals
  processing one file after another
  tar, zip, …
  recursive copy (cp -r)
  search (find)
  …
Only application knows access pattern
  use ioctl FIEMAP (FIBMAP) to retrieve extent/block locations
  sort in user space
  send I/O request according to sorted list
GNU/BSD Tar vs. QTAR

## Slide 40: Cooperative user-kernel space scheduling
Some times the kernel does not have enough information to make an efficient schedule
File tree traversals
  processing one file after another
  tar, zip, …
  recursive copy (cp -r)
  search (find)
  …
Only application knows access pattern
  use ioctl FIEMAP (FIBMAP) to retrieve extent/block locations
  sort in user space
  send I/O request according to sorted list
GNU/BSD Tar vs. QTAR
So, schedule your disk requests wisely….!
 it does matter

## Slide 41: Cooperative user-kernel space scheduling
Some times the kernel does not have enough information to make an efficient schedule
File tree traversals
  processing one file after another
  tar, zip, …
  recursive copy (cp -r)
  search (find)
  …
Only application knows access pattern
  use ioctl FIEMAP (FIBMAP) to retrieve extent/block locations
  sort in user space
  send I/O request according to sorted list
GNU/BSD Tar vs. QTAR
For handouts

## Slide 42: Data Placement

## Slide 43: Data Placement on Disk
Interleaved placement tries to store blocks from a file with a fixed number of other blocks in-between each block
  minimal disk arm movement reading the files A, B and C (starting at the same time)
  fine for predictable workloads reading multiple files
  no gain if we have unpredictable disk accesses
Non-interleaved (or even random) placement can be used for highly unpredictable workloads
file A
file B
file C

## Slide 44: Data Placement on Disk
Contiguous placement stores disk blocks contiguously on disk
  minimal disk arm movement reading the whole file (no intra-file seeks)
  pros/cons
    within a file, head must not move between reads - no seeks / rotational delays
    can approach theoretical transfer rate
    but usually we read other files as well (giving possible large inter-file seeks)
  real advantage
    whatever amount to read, at most track-to-track seeks are performed within one request
  no inter-operation gain if we have unpredictable disk accesses (but still not worse than random placement)
file A
file B
file C

## Slide 45: Data Placement on Disk
Organ-pipe placement consider the ‘average’ disk head position
  place most popular data where head is most often
  center of the disk is in average “closest” to the head
  but, a bit outward for zoned disks (modified organ-pipe)
disk:
innermost
outermost
head
block access probability
cylinder number
block access probability
cylinder number
organ-pipe:
modified organ-pipe:
Note: skew dependent on tradeoff between zoned transfer time and storage capacity vs. seek time

## Slide 46: Memory Caching

## Slide 47: Data Path (Intel Hub Architecture)
Pentium 4
Processor
registers
cache(s)
I/O
controller
hub
memory
controller
hub
RDRAM
RDRAM
RDRAM
RDRAM
PCI slots
PCI slots
PCI slots
disk
file system
application
file system
communication
system
application
disk
network card

## Slide 48: Buffer Caching
communication
system
application
disk
network card
expensive
file system
cache
caching possible
How do we manage a cache?
how much memory to use?
how much data to prefetch?
which data item to replace?
how to do lookups quickly?
…

## Slide 49: Buffer Caching: Windows (XP ++)
An I/O manager performs caching
  centralized facility to all components (not only file data)
I/O request processing:
process
file system
drivers
cache
manager
disk
drivers
virtual memory
manager (VMM)
I/O
manager
Kernel
  I/O request from process
  I/O manager forwards to cache manager
in cache:
  cache manager locates and copies data to process buffer via VMM
  VMM notifies process
on disk:
  cache manager generates a page fault
  VMM makes a non-cached service request
  I/O manager makes request to file system
  file system forwards to disk
  disk finds data
  reads into cache
  cache manager copies data to process buffer via VMM
  VMM notifies process
Notes: See also:
https://www.microsoftpressstore.com/articles/article.aspx?p=2201309&seqNum=3
https://docs.microsoft.com/en-us/windows-hardware/drivers/kernel/overview-of-the-windows-i-o-model
https://docs.microsoft.com/en-us/windows-hardware/drivers/kernel/the-life-of-an-i-o-request

## Slide 50: Buffer Caching: Linux / Unix
Kernel
Process
virtual file
system
Linux ext2fs
HFS
(Macintosh)
FAT32
(Windows)
buffers
disk
drivers
A file system performs caching
  caches disk data (blocks) only
  may hint on caching decisions
  prefetching
I/O requests processing:
  I/O request from process
  virtual file system forwards to local file system
  local file system finds requested block number
  requests block from buffer cache
  data located…
    … in cache:
      return buffer memory address
    … on disk:
      make request to disk driver
      data is found on disk and transferred to buffer
      return buffer memory address
  file system copies data to process buffer
  process is notified

## Slide 51: Buffer Caching Structure
Many different algorithms for replacement,
similar to page replacement…

## Slide 52: File Systems

## Slide 53: Files??
A file is a collection of data – often for a specific purpose
  unstructured files, e.g., Unix and Windows
  structured files, e.g., early MacOS (to some extent) and MVS
In this course, we consider unstructured files
  for the operating system, a file is only a sequence of bytes
  it is up to the application/user to interpret the meaning of the bytes
  simpler file systems
Notes: MVS (Multiple Virtual Storage) is IBM's best-known operating system for mainframe and large server computers (successors: OS/390 and z/OS.)

## Slide 54: File Systems
File systems organize data in files and manage access regardless of device type:
  storage management (bottom-up view) – allocating space for files on secondary storage
  file management (top-down view) – mechanisms for files to be stored, referenced, shared, secured, …
    file integrity mechanisms – ensuring that information is not corrupted, intended content only
    access methods – provide methods to access stored data

## Slide 55: Organizing Files - Directories
A system usually has a large number of different files
To organize and quickly locate files, file systems use directories
  contain no data itself
  file containing name and locations of other files
  several types
    single-level (flat) directory structure
    hierarchical directory structure

## Slide 56: Single-level Directory Systems
CP/M
  Microcomputers
  Single user system
VM
  Host computers
  “Minidisks”: one partition per user
Root directory
Four files

## Slide 57: Hierarchical Directory Systems
Tree structure
  nodes = directories root node = root directory
  leaves = files
Directories
  stored on disk
  attributes just like files
To access a file
  must (often) test all directories in path for
    existence
    being a directory
    permissions
  similar tests on the file itself
/
/

## Slide 58: Hierarchical Directory Systems
Windows: one tree per partition or device
\
Device D
Complete filename example:
C:\WinNT\EXPLORER.EXE
\
Device C
WINNT
EXPLORER.EXE

## Slide 59: Hierarchical Directory Systems
Unix: single acyclic graph spanning several devices
/
cdrom
Complete filename example:
/cdrom/doc/Howto
/
doc
Howto

## Slide 60: File & Directory Operations
File:
  create
  delete
  open
  close
  read
  write
  append
  seek
  get/set attributes
  rename
  link
  unlink
  …
Directory:
  create
  delete
  opendir
  closedir
  readdir
  rename
  link
  unlink
  …

## Slide 61: Example: open(), read() and close()
#include <stdio.h>
#include <stdlib.h>
int main(void)
{
int fd, n;
char buffer[BUFSIZE];
char *buf = buffer;
if ((fd = open( “my.file” , O_RDONLY , 0 )) == -1) {
printf(“Cannot open my.file!\n”);
exit(1); /* EXIT_FAILURE */
}
while ((n = read(fd, buf, BUFSIZE) > 0) {
<<USE DATA IN BUFFER>>
}
close(fd);
exit(0); /* EXIT_SUCCESS */
}
Notes: int
open( const char *path , int oflag, ...);
oflag – reading/writing/create/locks/blocking, etc
mode – umask / chmod premissions

## Slide 62: Open
Operating System
open(name,oflags,mode)
sys_open()  vn_open():
  Check if valid call
  Allocate file descriptor
  If file exists, open for read (remember O_RDONLY). Must get directory inode (?). May require disk I/O.
  Set access rights, flags and pointer to vnode (?)
  Return index to file descriptor table
fd
BSD example
system call handling as described earlier
control block
control block
user
kernel
fd
control block
Notes: inodes later…

## Slide 63: Example: open(), read() and close()
#include <stdio.h>
#include <stdlib.h>
int main(void)
{
int fd, n;
char buffer[BUFSIZE];
char *buf = buffer;
if ((fd = open( “my.file” , O_RDONLY , 0 )) == -1) {
printf(“Cannot open my.file!\n”);
exit(1); /* EXIT_FAILURE */
}
while ((n = read(fd, buf, BUFSIZE) > 0) {
<<USE DATA IN BUFFER>>
}
close(fd);
exit(0); /* EXIT_SUCCESS */
}
Notes: ssize_t
read(int fildes, void *buf, size_t nbyte);

## Slide 64: Read
Operating System
buffer
read(fd, *buf, len)
sys_read()  dofileread()  (*fp_read==vn_read)():
  Check if valid call and mark file as used
  Use file descriptor as index in file descriptor table to find corresponding file pointer
  Use data pointer in file structure to find vnode
  Find current offset in file
  Call local file system
VOP_READ(vp,len,offset,..)
system call handling as described earlier
BSD example

## Slide 65: Read
Operating System
VOP_READ(...) is a pointer to a read function in the
corresponding file system, e.g., Fast File System (FFS)
READ():
  Find corresponding inode
  Check if valid call: len + offset ≤ file size
  Loop and find corresponding blocks
    find logical blocks from inode, offset, length
    do block I/O, fill buffer structure e.g., bread(...)  bio_doread(...)  getblk()
    return and copy block to user
VOP_READ(vp,len,offset,..)
getblk(vp,blkno,size,...)

## Slide 66: Read
Operating System
A | B | C | D | E | F | G | H | I | J | K | L
M
getblk(vp,blkno,size,...)
Search for block in buffer cache, return if found (hash vp and blkno and follow linked hash list)
Get a new buffer (LRU, age)
Call disk driver - sleep or do something else
Reorganize LRU chain and return buffer
VOP_STRATEGY(bp)

## Slide 67: Read
Operating System
VOP_STRATEGY(bp)
VOP_STRATEGY(...) is a pointer to the corresponding
driver depending on the hardware,
e.g., SCSI - sdstrategy(...)  sdstart(...)
Check buffer parameters, size, blocks, etc.
Convert to raw block numbers
Sort requests according to SCAN - disksort_blkno(...)
Start device and send request

## Slide 68: Read
file attributes
...
data pointer
data pointer
data pointer
data pointer
data pointer
...
...
Operating System
M

## Slide 69: Read
Operating System
A | B | C | D | E | F | G | H | I | J | K | L
Search for block in buffer cache, return if found (hash vp and blkno and follow linked hash list)
Get a new buffer (LRU, age)
Call disk driver - sleep or do something else
Reorganize LRU chain and return buffer
M
M
Interrupt to notify end of disk IO
Kernel may awaken sleeping process
M

## Slide 70: Read
Operating System
READ():
  Find corresponding inode
  Check if valid call - file size vs. len + offset
  Loop and find corresponding blocks
    find logical blocks from inode, offset, length
    do block I/O, e.g., bread(...)  bio_doread(...)  getblk()
    return and copy block to user
buffer
M

## Slide 71: Example: open(), read() and close()
#include <stdio.h>
#include <stdlib.h>
int main(void)
{
int fd, n;
char buffer[BUFSIZE];
char *buf = buffer;
if ((fd = open( “my.file” , O_RDONLY , 0 )) == -1) {
printf(“Cannot open my.file!\n”);
exit(1); /* EXIT_FAILURE */
}
while ((n = read(fd, buf, BUFSIZE) > 0) {
<<USE DATA IN BUFFER>>
}
close(fd);
exit(0); /* EXIT_SUCCESS */
}

## Slide 72: Management of File Blocks
file attributes
...
data pointer
data pointer
data pointer
data pointer
data pointer
...
...

## Slide 73: Management of File Blocks
Many files consist of several blocks
  relate blocks to files
  how to locate a given block
  maintain order of blocks
Approaches
  chaining in media
  chaining in a map
  table of pointers
  extent-based allocation

## Slide 74: Chaining in the Media
Metadata points to chain of used file blocks
Free blocks may also be chained
nice if you only read sequentially from the start
expensive to search (random access)
must read block by block
Metadata
File blocks

## Slide 75: Chaining in a Map
Metadata
File blocks
Map

## Slide 76: Chaining in a Map: FAT Example
FAT: File Allocation Table
Versions FAT12, FAT16, FAT32
  number indicates number of bits used to identify blocks in partition (212,216,232)
  FAT12: Block sizes 512 bytes – 8 KB: max 32 MB partition size
  FAT16: Block sizes 512 bytes – 64 KB: max 4 GB partition size
  FAT32: Block sizes 512 bytes – 64 KB: max 2 TB partition size
Boot
sector
FAT1
FAT2
(backup)
Root
directory
Other directories and files
…
0000
0003
0004
FFFF
0006
0008
FFFF
FFFF
0000
…
File1
File1
File1
empty
File2
File2
File2
File3
empty
empty
empty
empty
empty
empty
empty
empty
empty
empty
0001
0002
0003
0004
0005
0006
0007
0008
0009
Notes: FAT32, with cluster values held in a 32-bit field, of which 28 bits are used to hold the cluster number, for a maximum of approximately 268 million (228) clusters. This allows for drive sizes of up to 8 terabytes with 32KB clusters, but the boot sector uses a 32-bit field for the sector count, limiting volume size to 2 TB on a hard disk with 512 byte sectors.
https://www.pjrc.com/tech/8051/ide/fat32.html

## Slide 77: Kom hit!

## Slide 78: Table of Pointers
Metadata
File blocks
Map
inefficient search in the map

## Slide 79: Table of Pointers
Metadata
File blocks
Table of pointers
good random and sequential access
main structure small, extra blocks if needed
uses one indirect block regardless of size
can be too small for large files

## Slide 80: Unix/Linux Example: FFS, UFS, …
mode
owner
…
Direct block 0
Direct block 1
…
Direct block 10
Direct block 11
Single indirect
Double indirect
Triple indirect
Data block
Data block
Data block
Data block
index
Data block
Data block
Data block
Data block
index
index
index
index
index
index
Data block
Data block
Data block
Data block
index
index
Data block
inode
Flexible block size
e.g. 4KB
1024 entries
per index block
Data block
Notes: direkte = 4kb * 12 = 48 kb
1.indirekte = 4kb * 1024 (+ direkte) = 4 MB
2.indirekte = 4kb * 1024 * 1024 (+ direkte/indirekte) = 4 GB
3.indirekte = 4kb * 1024 * 1024 * 1024 (+ direkte/indirekte) = 4 TB

## Slide 81: Extent-based Allocation
Metadata
File blocks
List of extents
1
3
2
faster block allocation (many at a time)
higher performance reading large data elements
less file system meta data
reduce number of lookups reading a file
Observation: indirect block reads introduce disk I/O and break access locality

## Slide 82: Linux Example: XFS, JFS, EXT4…
Count-augmented address indexing in the extent sections
Introduce a new inode structure
  add counter field to original direct entries
    direct points to a disk block
    count indicated how many other blocks is following the first block (contiguously)
direct 0
direct 1
direct 2
…
direct 10
direct 11
triple indirect
single indirect
double indirect
attributes
count 0
count 1
count 2
…
count 10
count 11
data
3
data
data
inode

## Slide 83: ext4_inode
direct 1
direct 2
…
direct 10
direct 11
attributes
count 0
count 1
count 2
…
count 10
count 11
data
3
data
data
inode
struct ext4_inode {
__le16 i_mode; /* File mode */
__le16 i_uid; /* Low 16 bits of Owner Uid */
__le32 i_size; /* Size in bytes */
__le32 i_atime; /* Access time */
__le32 i_ctime; /* Inode Change time */
__le32 i_mtime; /* Modification time */
__le32 i_dtime; /* Deletion Time */
__le16 i_gid; /* Low 16 bits of Group Id */
__le16 i_links_count; /* Links count */
__le32 i_blocks; /* Blocks count */
__le32 i_flags; /* File flags */
...
__le32 i_block[EXT4_N_BLOCKS];/* Pointers to blocks */
__le32 i_generation; /* File version (for NFS) */
__le32 i_file_acl; /* File ACL */
__le32 i_dir_acl; /* Directory ACL */
__le32 i_faddr; /* Fragment address */
...
__le32 i_ctime_extra; /* extra Change time (nsec << 2 | epoch) */
__le32 i_mtime_extra; /* extra Modification */
__le32 i_atime_extra; /* extra Access time */ __le32 i_crtime; /* File Creation time */ __le32 i_crtime_extra; /* extra */
};
direct 0
i_block [15]
Notes: #define EXT4_N_BLOCKS 12 +1+1+1 = 15 (60 bytes)

## Slide 84: ext4_inode
ext4_extent_header
ext4_extent
ext4_extent
ext4_extent
ext4_extent
struct ext4_extent {
__le32 ee_block; /* first logical block extent covers */
__le16 ee_len; /* number of blocks covered by extent */
__le16 ee_start_hi; /* high 16 bits of physical block */
__le32 ee_start; /* low 32 bits of physical block */
};
i_block [NUM]
4
Theoretically, each extent can have 216 - 1 continuous blocks, i.e., 64 GB data using a 4KB block size,
but limited to 128 MB
Max size of 4 x 128 = 512 MB files?
What about fragmented disks??
...
__le16 eh_depth;
...
Tree of extents organized using an HTREE
Notes: ext4_inode has i_block array (60 bytes total).
The first 12 bytes store ext4_extent_header;
the remainder stores an array of 4 of ext4_extent.
#define EXT4_N_BLOCKS 12 +1+1+1 = 15 (60 bytes)
An HTREE is a specialized tree data structure for directory indexing, similar to a B-tree. They are constant depth of either one or two levels, have a high fanout factor, use a hash table of the filename, and do not require balancing.
Htree indexes are used in the ext3 and ext4 Linux filesystems

## Slide 85: ext4_inode
ext4_extent_header
ext4_extent_idx
ext4_extent_idx
ext4_extent_idx
ext4_extent_idx
struct ext4_extent_idx {
__le32 ei_block; /* index covers logical blocks from 'block' */ __le32 ei_leaf; /* pointer to the physical block of the next * * level. leaf or next index could be there */
__le16 ei_leaf_hi; /* high 16 bits of physical block */
__u16 ei_unused;
};
i_block [NUM]
...
__le16 ee_len;
__le16 ee_start_hi;
__le32 ee_start;
 one 4 KB can hold 340 ext4_extents(_idx)
 first level can hold 170 GB
 second level can hold 56 TB (limed to 16 TB, 32 bit pointer)
4
Notes: NOTE: first level CAN hold 170 GB IF all extents are full

## Slide 86: Windows Example: NTFS
Each partition contains a master file table (MFT)
  a linear sequence of 1 KB records
  each record describes a directory or a file (attributes and disk addresses)
first 16 reserved for
NTFS metadata
record header
standard info
file name
data header
info about data blocks
…data…
A file can be …
stored within the record (immediate file, < few 100 B)
represented by disk block addresses (which hold data): runs of consecutive blocks (<addr, no>, like extents)
use several records if more runs are needed
20
4
run 1
30
2
run 2
74
7
run 3
unused
24 - base record
26 - first extension record
27 - second extension record
10
2
run 1
78
3
run k
MFT 27
2nd extension
MFT 26
1st extension
run 2, run 3, …, run k-1

## Slide 87: Recovery & Journaling
When data is written to a file, both metadata and data must be updated
  metadata is written asynchronously, data may be written earlier
  if a system crashes, the file system may be corrupted and data is lost
Journaling file systems provide improved consistency and recoverability
  makes a log to keep track of changes
  the log can be used to undo partially completed operations
  e.g., ReiserFS, JFS, XFS and Ext3 (all Linux)
  NTFS (Windows) provide journaling properties where all changes to MFT and file system structure are logged

## Slide 88: Multiple Disks

## Slide 89: Parallel Access
Disk controllers and busses manage several devices
One can improve total system performance by replacing one large disk with many small accessed in parallel
Several independent heads can read simultaneously
Single disk:
Two disks:
Note: the single disk might be faster, but as seek time and rotational delay are the dominant factors of total disk access time, the two smaller disks might operate faster together performing seeks in parallel...

## Slide 90: Striping
Client1
Client2
Client3
Client4
Client5
Server
A reason to use multiple disks is when one disk cannot deliver requested data rate
In such a scenario, one might use several disks for striping:
  bandwidth disk: Bdisk
  required bandwidth: Bconsume
  Bdisk < Bconsume
  read from n disks in parallel: n Bdisk > Bconsume
Advantages
  higher transfer rate compared to one disk
Drawbacks
  can’t serve multiple clients in parallel
  positioning time increases (i.e., reduced efficiency)

## Slide 91: Interleaving (Compound Striping)
Full striping usually not necessary today:
  faster disks
  better compression algorithms
Interleaving lets each client be serviced by only a set of the available disks
  make groups
  ”stripe” data in a way such that a consecutive request arrive at next group
  one disk group example:
Client1
Client2
Client3
Server

## Slide 92: Interleaving (Compound Striping)
Divide traditional striping group into sub-groups, e.g., staggered striping
Advantages
  multiple clients can still be served in parallel
  more efficient disks operations
  potentially shorter response time
Potential drawback/challenge
  load balancing (all clients access same group)
X0,0
X0,1
X1,0
X1,1
X2,0
X2,1
X3,1
X3,0
X4,0
X4,1

## Slide 93: Mirroring
Multiple disks might do come in the situation where all requests are for one of the disks and the rest lie idle
In such cases, it might make sense to have replicas of data on several disks – if we have identical disks, it is called mirroring
Advantages
  faster response time
  survive crashes – fault tolerance
  load balancing by dividing the requests for the data on the same disks equally among the mirrored disks
Drawbacks
  increases storage requirement
  more expensive write operations

## Slide 94: Redundant Array of Inexpensive Disks
The various RAID levels define different disk organizations to achieve higher performance and more reliability
  RAID 0 - striped disk array without fault tolerance (non-redundant)
  RAID 1 - mirroring
  RAID 2 - memory-style error correcting code (Hamming Code ECC)
  RAID 3 - bit-interleaved parity
  RAID 4 - block-interleaved parity
  RAID 5 - block-interleaved distributed-parity
  RAID 6 - independent data disks with two independent distributed parity schemes (P+Q redundancy)
  RAID 10 - striped disk array (RAID level 0) whose segments are mirrored (RAID level 1)
  RAID 0+1 - mirrored array (RAID level 1) whose segments are RAID 0 arrays
  RAID 03 - striped (RAID level 0) array whose segments are RAID level 3 arrays
  RAID 50 - striped (RAID level 0) array whose segments are RAID level 5 arrays
  RAID 53, 51, …

## Slide 95: DAS vs. NAS vs. SAN??
Direct attached storage
Network attached storage
  uses some kind of file-based protocol to attach remote devices non-transparently
  NFS, SMB, CIFS
Storage area network
  transparently attach remote storage devices
  iSCSI (SCSI over TCP/IP), iFCP (SCSI over Fibre Channel), HyperSCSI (SCSI over Ethernet), ATA over Ethernet
How will the introduction of network attached disks influence storage?

## Slide 96: Example: Network File System (NFS)
Distributed file system – allowing a client to access a file over a network
local file system
virtual file system
system call layer
NFS client
virtual file system
system call layer
RPC client stub
NFS server
virtual file system
RPC server stub
local file system
network
UDP,TCP / IP
UDP,TCP / IP
local
network attached
Notes: NFS v2 – udp, stateless, v3 – udp+tcp, stateless, v4 – statefull, compound requests, … (performance, security, …)
RPC Sequence of events
The client calls the client stub. The call is a local procedure call, with parameters pushed on to the stack in the normal way.
The client stub packs the parameters into a message and makes a system call to send the message. Packing the parameters is called marshalling.
The client's local operating system sends the message from the client machine to the server machine.
The local operating system on the server machine passes the incoming packets to the server stub.
The server stub unpacks the parameters from the message. Unpacking the parameters is called unmarshalling.
Finally, the server stub calls the server procedure. The reply traces the same steps in the

## Slide 97: Mechanical Disks vs. Solid State Disks???
 | Storage capasity (GB) | Average (seek) time / latency (ms) | Sustained transfer rate (MBps) | Interface (Gbps)
Seagate Cheetah X15.6 (3.5 inch) | 450 | 3.4 (track to track 0.2) | 110 - 171 | SAS (3) FC (4)
Seagate Savvio 15K (2.5 inch) | 73 | 2.9 (track to track 0.2) | 29 - 112 | SAS (3)
Sagate Barracuda Pro | 14000 | 8.5 (track to track 1.0) | 250 | SATA (6)
Intel X25-E (extreme) | 64 | 0.075 | 250 | SATA (3)
Intel Drive 910 Series | 800 | < 0.065 | 2000 | SAS (6)
Intel DC S3700 Series | 2000 | 0.020 | 2000 | PCIe, v3
Intel DC P3608 | 4000 | 0.020 | 5000 | PCIe, v3
How will the introduction of SSDs influence storage?
2017 Price?
$ 8.999 2019 (3.2TB ) = 80 KNOK
Komplett.no ~5 KNOK (2019):
Standard HDD: 12 TB
Standard SSD: 2 TB
Notes: https://www.intel.com/buy/us/en/product/components/intel-dc-p3608-4000gb-485298
DC P3608 - seq read: 850 000 IOPS, 5GB/s, 20 microsec latency
4 TB : $8,759 (2017 price)
3.2 TB : 80.000 NOK ( )
PCIe, v3 (7.8/lane)
FC = fibre channel
SAS = serial attached SCSI
SATA = Serial ATA (Advanced Technology Attachment)

## Slide 98: Mechanical Disks vs. Solid State Disks???
 | Storage capasity (GB) | Average (seek) time / latency (ms) | Sustained transfer rate (MBps) | Interface (Gbps)
Seagate Cheetah X15.6 (3.5 inch) | 450 | 3.4 (track to track 0.2) | 110 - 171 | SAS (3) FC (4)
Seagate Savvio 15K (2.5 inch) | 73 | 2.9 (track to track 0.2) | 29 - 112 | SAS (3)
Sagate Barracuda Pro | 14000 | 8.5 (track to track 1.0) | 250 | SATA (6)
Intel X25-E (extreme) | 64 | 0.075 | 250 | SATA (3)
Intel Drive 910 Series | 800 | < 0.065 | 2000 | SAS (6)
Intel DC S3700 Series | 2000 | 0.020 | 2000 | PCIe, v3
Intel DC P3608 | 4000 | 0.020 | 5000 | PCIe, v3
How will the introduction of SSDs influence storage?
SSD or HDD
Speed
Life-time
Type of machine
Data & operations
Capacity
Latency
Price
Notes: https://www.intel.com/buy/us/en/product/components/intel-dc-p3608-4000gb-485298
DC P3608 - seq read: 850 000 IOPS, 5GB/s, 20 microsec latency
4 TB : $8,759 (2017 price)
PCIe, v3 (7.8/lane)
FC = fibre channel
SAS = serial attached SCSI
SATA = Serial ATA (Advanced Technology Attachment)
https://www.extremetech.com/extreme/210492-extremetech-explains-how-do-ssds-work

## Slide 99: The End: Summary

## Slide 100: Summary
Disks are the main persistent secondary storage device
The main bottleneck is often disk I/O performance due to disk mechanics: seek time and rotational delays
Much work has been performed to optimize disks performance
  scheduling algorithms try to minimize seek overhead (most systems use SCAN derivates)
  memory caching can save disk I/Os
  additionally, many other ways (e.g., block sizes, placement, prefetching, striping, …)
  world today more complicated (both different access patterns, unknown disk characteristics, …)  new disks are “smart”, we cannot fully control the device
File systems provide
  file management – store, share, access, …
  storage management – of physical storage
  access methods – functions to read, write, seek, …
  …
New non-mechanical storage may change the way of thinking…!!??