## Slide 1: In memory of
Per Stokke
4/2-1936 to 8/2-2025

## Slide 2: From Theory to Practice
IN2140
Plenum 3
Kristoffer Robin Stokke
Principal Software Engineer, PhD
University of Oslo, Institute of Informatics

## Slide 3: Pentium Memory Lookup
31 |  |  |  |  |  |  |  |  | 22 | 21 |  |  |  |  |  |  |  |  | 12 | 11 |  |  |  |  |  |  |  |  |  |  | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0
Incoming virtual address (CR2)
(0x1802038, 20979768)
31 |  |  | 12 |  |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0...01010101111 |  |  |  | ... |  |  |  |  |  |  |  |  |  | 1
0...01111111000 | ... |  |  |  |  |  |  |  | 0
0...01110000111 | ... |  |  |  |  |  |  |  | 0
0...00001010101 | ... |  |  |  |  |  |  |  | 1
0...01111000101 | ... |  |  |  |  |  |  |  | 0
0...00000000100 | ... |  |  |  |  |  |  |  | 1
...... |  |  |  |  |  |  |  |  | 
Index to page directory
(0x6, 6)
Page Directory Base Address
CR3:
31 |  |  | 12 |  |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0...01010101111 |  |  |  | ... |  |  |  |  |  |  |  |  |  | 1
0...01010100000 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
0...01100110011 |  |  |  |  |  |  |  |  |  |  |  |  |  | 1
0...00010000100 |  |  |  |  |  |  |  |  |  |  |  |  |  | 1
...... |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Page table:
Index to page table
(0x2, 2)
Page frame PF:
Save pointer to instruction
Move linear address to CR2
Generate a PF exception – jump to handler
Programmer reads CR2 address
Upper 10 CR2 bits identify needed PT
Use middle 10 CR2 bit to determine entry in PT – holds a mass storage address
Allocate a new page – write back if dirty
Read page from storage device
Insert new page frame base address into page table entry
Return and restore faulting instruction
Resume operation reading the same page directory entry and page table entry again – both now P = 1

## Slide 4: Plenum 3
Finish “blocking” and “interrupt” examples
Talk about the Tuesday lecture
Unfortunately, there’s not too much code today.
Do you have any coding questions or topics that you would want me to visit instead?

## Slide 5: Process States
running
ready
blocked
process blocks for input
scheduler starts process
scheduler stops process
external event finished
process creation
process termination
Example:
Blocking IO

## Slide 6: Why would we not want to block, wasting CPU time spinning?

## Slide 7: Interrupt Program Execution
CPU
We may use “polling”…!?
Example:
Signals and polling

## Slide 8: Interrupting a process
CPU
CTRL+C sends a SIGINT on Linux, to the process running in the shell.
We can decide what to do when receiving SIGINT with signal(..)
  What if we don’t care?
Various tools to list running processes
  top / htop -> more interactive
  ps aux | grep <name_of_binary>
kill <pid>
  Brutally kills a running executable
  Add -9 to really kill hard

## Slide 9: Makefiles
Anyone want a quick introduction?

## Slide 10: Makefiles
A set of rules of the form:
  “to make this file” : “you need this or these files”
Make uses timestamps to figure out if it needs to rebuild files.
The first rule is the default one.
Large makefiles grow complex and hard to read, but they are very fast
hello :
echo “Hello, world” > hello
The world’s simplest makefile?

## Slide 11: Memory Management for Multiprogramming
Use of secondary storage
  keeping all programs and their data in memory may be impossible
  move (parts of) a process from memory
Swapping: remove a process from memory
  with all of its state and data
  store it on a secondary medium (disk, flash RAM, … , historically also tape)
Overlays: manually replace parts of code/data
  programmer’s rather than OS’s work
  only for very old and memory-scarce systems
Segmentation/paging: remove parts of a process from memory
  store it on a secondary medium
  sizes of such parts are usually fixed

## Slide 12: Overlays & Secondary Storage to “Swap” Memory

## Slide 13: Game boy architecture
8-bit
CPU
Memory
(ROM)
Game boy console side
Cartridge side
Only 16 kB!
16kB
bank
16kB
bank
16kB
bank
16kB
bank
Memory bank controller
Up to 2 MB of game code could be accessed in this way.
0x0000
0x3FFF

## Slide 14: Tetris
https://b13rg.github.io/Gameboy-Bank-Switching/

## Slide 15: What about game saves?
Remember how each box held only 20 pokemon, and you had 16 boxes you had to switch between?

## Slide 16: Game boy architecture
8-bit
CPU
ROM 16k
Game boy console side
Cartridge side
16kB
MBC
16kB
MBC
RAM 8k
8kB
8kB
8kB
8kB
0x0000
0x3FFF
0xA000
0xBFFF
Bank0: Halle of fame
Bank1: Player name, party, current box
Bank2: Pokemon box 1-6
Bank3: Pokemon box 7-12
https://retrocomputing.stackexchange.com/questions/13237/what-technological-limitations-required-the-box-system-in-gen-1-pok%C3%A9mon-games

## Slide 17: To change boxes
Copy the current box (from “main” bank1) to storage (bank2 or bank3)
Copy the desired box (from bank2 or bank3) to “main” bank 1
The notion of boxes in pokemon stems from this limitation..
  And it has consequences for the game even today
So actually, many of you are actually familiar with secondary storage and swapping out memory!

## Slide 18: Memory Management for Multiprogramming
Use of secondary storage
  keeping all programs and their data in memory may be impossible
  move (parts of) a process from memory
Swapping: remove a process from memory
  with all of its state and data
  store it on a secondary medium (disk, flash RAM, … , historically also tape)
Overlays: manually replace parts of code/data
  programmer’s rather than OS’s work
  only for very old and memory-scarce systems
Segmentation/paging: remove parts of a process from memory
  store it on a secondary medium
  sizes of such parts are usually fixed

## Slide 19: Macintosh 128k
Just one floppy drive
  No hard drive etc
Floppy applications..
  Are copied to RAM
Swap application floppies..
  To run different applications..
Data floppies
  For save data (remove application floppy first!)

## Slide 20: Memory Management for Multiprogramming
Use of secondary storage
  keeping all programs and their data in memory may be impossible
  move (parts of) a process from memory
Swapping: remove a process from memory
  with all of its state and data
  store it on a secondary medium (disk, flash RAM, … , historically also tape)
Overlays: manually replace parts of code/data
  programmer’s rather than OS’s work
  only for very old and memory-scarce systems
Segmentation/paging: remove parts of a process from memory
  store it on a secondary medium
  sizes of such parts are usually fixed
Reducing memory usage
(move unused data to store)
Reducing memory usage (move unused data to store)
Processes primitively share a machine (floppy)
The future
(will get back to this)

## Slide 21: Standard memory view of a process
THE STACK
0xFFFFFFFF
0x0
THE STACK
THE STACK
CODE
DATA

## Slide 22: What about a program that does this:
?
A program
Prints the sum of all the numbers
(10 in this case)
INPUT
OUTPUT
A sequence of numbers in ascii
(1234)

## Slide 23: In the news:

## Slide 24: Heap Allocations
The required memory size is not always known in advance
  E.g., the number of characters in a string from a user.
We can dynamically allocate an arbitrary number of bytes
  pointer = malloc( <size in bytes> );
Remember to free your memory
  free( pointer );
Is your program large and you’re not sure you free’d everything?
  valgrind –leak-check=full <executable> <arguments>
or just lazy?

## Slide 25: The standard process view – final! (?)
THE STACK
0xFFFFFFFF
0x0
THE STACK
STACK
CODE
DATA
Temporary data in each scope
Code (read-only)
Data (static + heap allocations)

## Slide 26: Do you HAVE to have malloc() and free()?

## Slide 27: Fixed Partitioning
Divide memory into static partitions at system initialization time (boot or earlier)
Advantages
  easy to implement
  can support swapping of processes
Equal-size partitions
  large programs cannot be executed (unless parts of a program are loaded from disk)
  small programs don't use the entire partition (problem called “internal fragmentation”)
Unequal-size partitions
  large programs can be loaded at once
  less internal fragmentation
  require assignment of jobs to partitions
  one queue or one queue per partition
  …but, what if only small or large processes?
Operating system
8MB
8MB
8MB
8MB
8MB
8MB
8MB
8MB
Operating system
8MB
8MB
8MB
2MB
4MB
6MB
12MB
16MB
Equal sized:
Unequal sized:

## Slide 28: Fixed (Static) Partitioning
Very commonplace in µcs today!
Example tasks:
  UART / Command line interface
  GPIO
  I2C communication
  Sensor readings
    Gyro, GPS, Magnetometer..
No heap! No malloc(..)
  All data allocated compile-time
No Operating System
  Thin C libary
  Thin drivers (UART, Interrupts, I2C)
AT Mega microcontollers
UART
I2C
I2C
UART
CLI
GPIO
I2C
Sensor
Support Libraries (C/C++) and Drivers
GPIO
GPS
Magnetometer
Hardware units
Off-chip units
Application layer
µc >> Please enter command.
µc >> help!
Applications “yield” to the next application.
NON-PREEMPTIVE SCHEDULING

## Slide 29: Actually..
Even for relatively complex applications, it can make sense NOT to use heap allocations like malloc(..).
Why?
  Pointers creates bugs, even for experienced programmers.
You can get away with statically allocating everything..
  And testing like crazy

## Slide 31: Process A & B Share the LMC
They relinquish control of the CPU:
  “Calling” yield()
They share memory
  “Static allocations” – Just take some cells
Process A
Process B
Scheduler
SCHEDULER
PROCESS A
PROCESS B

## Slide 32: LMC Scheduler: Weaknesses
One process can..
  HLT the machine entirely
  BRA into the other process’ code
  Starve the other process by not yield()’ing
  Use LDA and STA to mess up the other process’ counting
Process A
Process B
Scheduler
SCHEDULER
PROCESS A
PROCESS B
Example: pointer sharing

## Slide 33: So in summary, we have the following (RAM) challenges:
Conserving RAM (memory) usage
  Not everything needs to be in RAM at all times.
  Some of it could be on a disk.
Sharing RAM between processes
  Several processes must be able to utilize available RAM
  Processes may even share RAM to communicate
Protecting processes from each others’ RAM
  Accidental or malicious attempts to write each others’ memory
SHARING
CONSERVING
PROTECTING

## Slide 35: IBM System 370 (1970s)
“The bank previously had nine computers running 2,000 different programs. By switching to System/370, it was able to run all its programs on a single mainframe.”
“By fully utilizing virtual storage, System/370 enabled programmers to use more memory than might be physically available.”
“Part of System/370’s success can be attributed to the fact that it was among the first computers to include full support for virtual memory”
SHARING
https://www.ibm.com/history/system-370
CONSERVING

## Slide 36: You are ready for the truth!

## Slide 37: A very simple 32-bit machine with 2 GB of RAM.
0x0
0xFFFFFFFF
With 32 bits →
  possible addresses
4294967296 bytes OR 4 GB
Highest address: 2^32-1
  0xFFFFFFFF (32 bits, all ones)
Even though we can address 4GB..
  We only have 2 GB of RAM installed.
So in reality we can just address ..
  0x0 to 0x80000000 (0GB  2GB)
INSTALLED RAM
FULL ADDRESSABLE SPACE
0x80000000

## Slide 38: Next, consider our process running in our machine.
THE STACK
0x0
THE STACK
STACK
CODE
DATA
0xFFFFFFFF
The stack is all the way up here
Something is odd, isn’t it?
0x0
0xFFFFFFFF
INSTALLED RAM
0x80000000
0x80000000
How can the stack be in this part of RAM, where there is no actual RAM installed?
???

## Slide 39: How can this be?

## Slide 40: Virtual and physical addresses
STACK
CODE
DATA
INSTALLED RAM
The stack, code and data regions of our process are actually located somewhere else in PHYSICAL RAM.
STACK
CODE
DATA
ADDRESS TRANSLATION

## Slide 41: This is Virtual Memory
STACK
CODE
DATA
The memory addresses that a process “sees” is called virtual memory.
0x0
0xFFFFFFFF
Virtual memory stretches from address 0 and all the way to the maximum possible address ().

## Slide 42: This is Physical Memory
INSTALLED RAM
Physical memory is the actual addressable range of memory, that depends on how much is installed.
In our case, it stretches from 0x0 to 0x80000000 (2GB).
Accessing physical memory outside this region yields undefined behaviour.
0x80000000
0x0

## Slide 43: Virtual and physical memory
STACK
CODE
DATA
INSTALLED RAM
Virtual memory
Physical memory

## Slide 44: Let’s make it simpler
0x0
STACK
CODE
DATA
0xFFFFFFFF
Process A

## Slide 45: Let’s make it simpler
0x0
0xFFFFFFFF
Process A

## Slide 46: And a little more complex... Two processes
0x0
0xFFFFFFFF
Process A
0x0
0xFFFFFFFF
Process B
Each process has its own “virtual memory” from the minimum (0x0) to the maximum (0xFFFFFFFF) address range.

## Slide 47: Now for the mapping
0x0
0xFFFFFFFF
Process A
0x0
0xFFFFFFFF
Process B
INSTALLED RAM
ADDRESS TRANSLATION
Notice how process A and process B seem to share the same memory ranges (upper part of memory); however, they are actually mapped to completely unique physical addresses.

## Slide 48: The great revelation
0x0
0xFFFFFFFF
Process A
0x0
0xFFFFFFFF
Process B
INSTALLED RAM
ADDRESS TRANSLATION
Each process runs as if it owns the entire address space, while in reality, it is shared with other processes.
In this way, processes are protected from each other, and we share the physical RAM.
PROTECTING
SHARING

## Slide 49: This is called Virtual Memory.

## Slide 50: Where is the magic in Virtual Memory?
0x0
0xFFFFFFFF
Process A
0x0
0xFFFFFFFF
Process B
INSTALLED RAM
ADDRESS TRANSLATION

## Slide 51: On IBM 370, this was called “Dynamic Address Translation”
https://www.google.com/url?sa=t&source=web&rct=j&opi=89978449&url=https://www.vm.ibm.com/history/50th/370info.pdf

## Slide 52: On x86, this is called the Memory Management Unit (MMU)
0x0
0xFFFFFFFF
Process A
0x0
0xFFFFFFFF
Process B
INSTALLED RAM
MMU

## Slide 53: Address Translation
How is it done?

## Slide 54: Address Translation
Let’s say that a process tries to read from virtual address 0x00c03010
The MMU’s goal is now:
  Translate virtual addresses into a physical process.
  Such that the value from that address can be fetched.
CPU
MMU
RAM
mov 0x00c03010, rax
0x00c03010
???

## Slide 55: IN1020 Background Knowledge
0x00c03010
00000000110000000011000000010000
The first 10 bits is 3
The next 10 bits is 3
The last 12 bits is 8
The virtual address that the CPU reads

## Slide 56: You’re good to go!

## Slide 57: Each process has its own page directory in RAM
A process’ page directory

## Slide 58: The first 10 bits of the address points to an entry
A process’ page directory
0x00c03010
First 12 bits =
000000000011
which is 3
I.e., the first ten bits point to entry 3 of the page directory

## Slide 59: That entry points to a page table, which is also in RAM
A process’ page directory
0x00c03010
A page table

## Slide 60: The next 10 bits of the address points to an entry in the page table
A process’ page directory
0x00c03010
Next 12 bits =
0000000011
which is 3
I.e., the first ten bits point to entry 3 of the page table
A page table

## Slide 61: Finally, the page table entry contains the first 20 bits of the physical address
A process’ page directory
0x00c03010
A page table
RAM
For illustrative purposes I choose this number
Add the last 12 bits of the virtual address to get the physical address: 0xff000010
+
0xff000

## Slide 62: This is how the MMU translates virtual to physical addresses.
For x86 (32-bit).
CPU
MMU
RAM
mov 0x00c03010, rax
0x00c03010
0xff000010
PROTECTING
SHARING

## Slide 63: Page Directory & Page Table Entries are 32 bit Long
The first 20 bits of an address
11 bits that are not vital to our discussion
P
If present is 1:
Can point to:
-> A page table
-> A physical address
PRESENT: Important!
1: Page is present in RAM
0: Page is no present in RAM
If present is 0:
Can point to:
-> Anything you like
-> A disk sector?
CONSERVING

## Slide 64: If the present bit is not set during lookup, a page fault is generated
CPU
MMU
RAM
mov 0x00c03010, rax
0x00c03010
P != 1
PROTECTING
SHARING
PAGE FAULT!
DISK
The CPU must handle the fault, and move the desired memory from the disk and to the RAM.
0xff000010

## Slide 65
Thanks for today!