## Slide 1: Data Communication: Network structures
IN2140: Introduction to Operating Systems and Data Communication

## Slide 2: Programming the network
import urllib.request
contents = urllib.request.urlopen(
urllib.request.Request(
"https://www.uio.no/studier/emner/matnat/ifi/IN2140/v25/index.html")
).read()
print(contents.decode(’utf-8’))

## Slide 3: Programming the network
import urllib.request
contents = urllib.request.urlopen(
urllib.request.Request(
"https://www.uio.no/studier/emner/matnat/ifi/IN2140/v25/index.html")
).read()
print(contents.decode(’utf-8’))
<!DOCTYPE html>
<html lang="no">
<head>
<meta charset="utf-8" >
<meta http-equiv="X-UA-Compatible" content="IE=edge" />
<meta id="viewport" name="viewport" content="width=device-width, initial-scale=1" />
<meta name="format-detection" content="telephone=no">
<meta name="generator" content="Vortex" />
<title>Semesterside for IN2140 - – Universitetet i Oslo</title>
<meta property="og:title" content="Semesterside for IN2140 - – Universitetet i Oslo" />
<meta name="twitter:card" content="summary" />
<meta name="twitter:site" content="@unioslo" />
<meta name="twitter:title" content="Semesterside" />
<meta name="twitter:description" content="Les denne saken på UiOs nettsider." />
<meta name="twitter:image" content="https://www.uio.no/vrtx/dist/resources/uio2/css/images/social/uio-twitter-share-1000x1000.jpg" />
<meta name="twitter:url" content="https://www.uio.no/studier/emner/matnat/ifi/IN2140/v25/index.html" />
<meta property="og:url" content="https://www.uio.no/studier/emner/matnat/ifi/IN2140/v25/index.html" />
<meta property="og:type" content="website" />
<meta property="og:description" content="Les denne saken på UiOs nettsider." />
<meta property="og:image" content="https://www.uio.no/vrtx/dist/resources/uio2/css/images/social/uio-share-1200x630.jpg" />
<meta property="og:image:width" content="1200" />
<meta property="og:image:height" content="630" />
<meta property="og:updated_time" content="1741591281" />
<link rel="shortcut icon" href="/vrtx/dist/resources/uio2/css/images/favicon/favicon.png">

## Slide 4: Web-based software
Banking
Video
TV
Office tools
Navigation
Shopping

## Slide 5: Isn’t this enough?
In everyday live,
the network and network functions are black boxes,
language is very inaccurate … and that is only fair
the net
the cloud
applications
applications
But we – as software designers, architects, developers or researchers – must understand more

## Slide 6: Is this the whole story?
How do you get from a cable in the ground to a virtual home assistant?
Notes: badthings@flickr
Masaki Tokutomi@flickr

## Slide 7: A possible communication path
fiber
node
modem
pool
cable
modem
home
assistant
cable
headend
router
telco company
tier 1
provider
Oslo
Dublin
Copenhagen?
London?
assistant
compute
cluster
AI software
= ”Alexa”?
compute
cluster
Home
automation
?
tier 1
provider
tier 1
provider
tier 2
provider
https://youtu.be/F1a-eMF9xdY
Notes: This morning: 42ms from my desktop to Dublin (www.computing.dcu.ie)

## Slide 8: But does it matter if we understand it?
the net
Standards
contributions
Linux
contributions

## Slide 9: Network structures Structures
IN2140: Introduction to Operating Systems and Data Communication

## Slide 10: Network Components
ES - End system
end systems are “at the edge” of a network
examples: computer, mobile phone, tablet, smart watch, printer, TV, smoke detector, weather station, lamp, door opener, fridge, traffic light …
IS - Intermediate system
examples:
  router, switch
  base station, modem
  gateway: web proxy, firewall, NAT gateway
  repeater, bridge
end system
intermediate system
network
network
is sub-network (subnet) of
node

## Slide 11: Network Structures
without the lines showing network boundaries, this looks like a typical graph
there are nodes, and edges connecting pairs of nodes to each other
a specific arrangement of nodes and edges is called a topology
the terminology implies that edges are network connections
Notes: but it looks chaotic
on the large scale, it is chaotic
on the small scale, we have much more structure
it is called a topology especially when is has a sensible structure

## Slide 12: Network Structures
Point-to-point channels
Docsis (cable modems)
  star topology
Notes: give an example of a new 10GB Ethernet, show old FDDI/TokenRing, show how to arrange Ethernets in a tree
DOCSIS modem -> clearest point-to-point
full mesh: a few supercomputers, Torus
DOCSiS modem photo: Mike Cohen @ Flickr

## Slide 13: Network Structures
Point-to-point channels
Docsis (cable modems)
  star topology
Gigabit Ethernet (“1GB Ethernet”)
  star or tree topology
Notes: give an example of a new 10GB Ethernet, show old FDDI/TokenRing, show how to arrange Ethernets in a tree
DOCSIS modem -> clearest point-to-point
full mesh: a few supercomputers, Torus
ethernet switch: mine
ALSO INSIDE A COMPUTER: PCIe

## Slide 14: Network Structures
Point-to-point channels
Docsis (cable modems)
  star topology
Gigabit Ethernet (“1GB Ethernet”)
  star or tree topology
IEEE 802.5 “TokenRing” (outdated)
  ring topology
Some supercomputers use
  full mesh topology
  hypercube topology
  torus topology
  fat tree topology
ring
full mesh
torus
fat tree
hypercube
Notes: give an example of a new 10GB Ethernet, show old FDDI/TokenRing, show how to arrange Ethernets in a tree
DOCSIS modem -> clearest point-to-point
full mesh: a few supercomputers, Torus
ethernet switch: mine

## Slide 15: Questions
The majority of computers today use PCI Express (PCIe) for connectivity between devices
Q: Which topology do most desktops use between devices today?

## Slide 16: Questions
full mesh
hypercube
ring
star
tree
A
B
C
D
E
Q: Which topology do most desktops use between devices today?
Notes: A tree

## Slide 17: Questions
The connectivity between CPUs and RAM banks is solved by a network.
Names of recent technologies are
Hypertransport
QuickPath Interconnect
Ultra Path Interconnect
Q: Which topology do computers with several CPUs use for connecting to RAM today?

## Slide 18: Questions
full mesh
hypercube
ring
star
tree
A
B
C
D
E
Q: Which topology do computers with several CPUs use for connecting to RAM today?
Notes: A hypercube

## Slide 19: Network Structures
Broadcasting channels
Cable
  old-fashioned Ethernet
Radio
  Aloha (first wireless data transmission)
  WiFi (IEEE 802.11)
  mobile: 3G, 4G, 5G
  satellites
Properties
  when one node sends, potentially many nodes can hear it
Notes: WIFI image from gcg2009@flickr
I made an Ethernet star once – didn’t work so well at the time

## Slide 20: Network Structures
Broadcasting channels
Cable
  old-fashioned Ethernet
Radio
  Aloha (first wireless data transmission)
  WiFi (IEEE 802.11)
  mobile: 3G, 4G, 5G
  satellites
Properties
  when one node sends, potentially many nodes can hear it
  when two nodes send, both messages are potentially ruined
  error detection is important
  coordination is desirable
Notes: give an example of a new 10GB Ethernet, show old FDDI/TokenRing, show how to arrange Ethernets in a tree
DOCSIS modem -> clearest point-to-point
full mesh: a few supercomputers, Torus
ethernet switch: mine

## Slide 21: Network Structures
Broadcasting channels
Cable
  old-fashioned Ethernet
Radio
  Aloha (first wireless data transmission)
  WiFi (IEEE 802.11)
  mobile: 3G, 4G, 5G
  satellites
Properties
  when one node sends, potentially many nodes can hear it
  when two nodes send, both messages are potentially ruined
  error detection is important
  coordination is desirable

## Slide 22: Network structures Network’s tasks
IN2140: Introduction to Operating Systems and Data Communication

## Slide 23: A lot of tasks
knowing the way
from one IS to another
knowing which
ES to contact
knowing
which process
to contact on that ES
knowing how to
find the reverse way

## Slide 24: A lot of tasks
knowing the way
from one IS to another
knowing which
ES to contact
knowing
which process
to contact on that ES
knowing how to
find the reverse way
Should we have dinner?
我们应该吃晚餐吗
coding the data
in a comprehensible
manner

## Slide 25: A lot of tasks
coding the data
in a comprehensible
manner
knowing the way
from one IS to another
knowing which
ES to contact
knowing
which process
to contact on that ES
knowing how to
find the reverse way
dealing with
networking problems
maintaining
privacy
maintaining
security

## Slide 26: A lot of tasks
knowing the way
from one IS to another
knowing which
ES to contact
knowing
which process
to contact on that ES
knowing how to
find the reverse way
dealing with
networking problems
maintaining
privacy
maintaining
security
avoiding
high delays
support
high traffic
coding the data
in a comprehensible
manner

## Slide 27: A lot of tasks
There are a lot of aspects to worry about
the application
knowing the way
from one IS to another
knowing which
ES to contact
knowing
which process
to contact on that ES
knowing how to
find the reverse way
coding the data
in a comprehensible
manner
maintaining
privacy
dealing with
networking problems
maintaining
security
avoiding
high delays
support
high traffic
applications
determine
requirements

## Slide 28: A lot of tasks
There are a lot of aspects to worry about
the application
knowing the way
from one IS to another
knowing which
ES to contact
knowing
which process
to contact on that ES
knowing how to
find the reverse way
coding the data
in a comprehensible
manner
maintaining
privacy
dealing with
networking problems
maintaining
security
avoiding
high delays
support
high traffic
applications
determine
requirements

## Slide 29
the application
dealing with
networking problems
avoiding
high delays
support
high traffic
applications
determine
requirements

## Slide 30: the application
dealing with
networking problems
avoiding
high delays
support
high traffic
File download and Web browsing
Internet
uncritical
uncritical
critical

## Slide 31: Textual commands and textual chat
Internet
dealing with networking problems
avoiding high delays
support high traffic
uncritical
uncritical
critical
Notes: delay: human reading speed

## Slide 32: Live and on-Demand Streaming
Internet
dealing with networking problems
avoiding high delays
support high traffic
some ok
critical
some ok
Notes: packet loss: acceptable (some)

## Slide 33: AV chat and AV conferencing
Internet
dealing with networking problems
avoiding high delays
support high traffic
some ok
important
some ok

## Slide 34: Haptic Interaction
Internet
dealing with networking problems
avoiding high delays
support high traffic
critical
uncritical
some ok
Notes: add oculus on one side!

## Slide 35: The Internet must support all of them
Internet

## Slide 36: Questions
The previous slides showed some examples of applications that must be supported by the Internet. But some really important ones are missing.
Q: Can you give an example of an important kind of application that was missing?
Notes: My additional ideas:
Web 2.0 (Facebook)
Cloud gaming
Peer-to-peer networking
Live interaction with AIs

## Slide 37: Network structures Structuring the tasks
IN2140: Introduction to Operating Systems and Data Communication

## Slide 38: Questions
It is impossible for a single person to solve all of these challenges for all intermediate systems, end systems and applications in the entire world.
Collaboration and coordination is necessary.
Many ideas have been proposed.
Q: How would you structure all of these tasks?
find out how tasks depend on each other, solve the most basic ones first, and build the next most important on top of them, etc
create a large toolbox of standard algorithms, and put them together as required
solve local challenges locally, use that to solve them for a longer distances, repeat for even longer distances, etc … recursively
knowing the way
from one IS to another
knowing which
ES to contact
knowing
which process
to contact on that ES
knowing how to
find the reverse way
coding the data
in a comprehensible
manner
maintaining
privacy
dealing with
networking problems
maintaining
security
avoiding
high delays
support
high traffic

## Slide 39: Approaches to structure the tasks
layered approach: arrange tasks in layers
specify hardware
encode bits, choose speed, fix errors
build data units from bits
transfer between neighbors, adapt speed
find neighbours
transfer longer distances
find a process
establish connections
choose common encoding
advantages:
clear interfaces
clear assignment of responsibilities
develop layers independently
disadvantages:
not perfectly suited for all jobs
similar problems are solved several times

## Slide 40: Approaches to structure the tasks
component approach: interacting components
encoding
algorithms
location
algorithms
speed ctrl
algorithms
recovery
algorithms
advantages:
possible to avoid duplicated functions
possible to choose perfect network behaviour for every application
disadvantages:
must negotiate choice of every piece with all nodes
toolbox must be complete on all nodes
needs flexible interfaces

## Slide 41: Approaches to structure the tasks
recursive approach: handle challenges locally
advantages:
reuse the concept of inter-process communication on all levels
concepts are repeated at every level
all challenges can be solved as local as possible
disadvantages:
more negotiations and setup than layered
unclear how to best share resources

## Slide 42: Questions
These three ways of structuring the tasks of networks are frequently discussed, as well as used. The reality is a mixture, but one of them dominates how we think about task structuring.
Q: Which of these three approaches is the dominant one?
Layers
Components
Recursion
Notes: The answer is layering

## Slide 43: Network structures Layering model
IN2140: Introduction to Operating Systems and Data Communication

## Slide 44: Approaches to structure the tasks
Right now, the layered models dominate
ISO OSI (Open Systems Interconnection) Reference Model
and
TCP/IP Reference Model Internet Architecture
layers are easy to understand
interfaces are clearly defined
not every node must implement every layer
…

## Slide 45: Reference Model for Open Systems Interconnection
ISO OSI (Open Systems Interconnection) Reference Model
model for layered communication systems
defines fundamental concepts and terminology
defines 7 layers and their functionalities
1
Physical layer
2
Data link layer
3
Network layer
4
Transport layer
5
Session layer
6
Presentation layer
7
Application layer

## Slide 46: Layer functions: physical layer
Responsibility: insecure bitstream between adjacent systems
  mechanics
  electronics
  procedural
1
Physical layer
encoding and
decoding of
bits

## Slide 47: Layer functions: data link layer
Responsibility: error-recovering frame stream, adjacent systems
Reliable data transfer between adjacent stations with frames
2
Data link layer
Logical Link
Control (LLC)
Medium Access
Control (MAC)
error detection
access to medium
SOF
DATA
CHK SUM
EOF
start of frame
e.g. 01111110
end of frame
e.g. 01111101
create data frames from bits
where to send? → MAC address
when to send? → wait for silence, wait for token
correct frame? → check for bit errors and repair
handle speed differences between nodes
handle several L3 protocols
translate between different MAC layers

## Slide 48: Layer functions: network layer
Responsibility: packet stream between end systems
3
Network layer
end-to-end transport of packets
ability to address source and target nodes
routing from source node to target node
Notes: map of Oslo: Dr Blofeld@Wikimedia via OpenStreetMap

## Slide 49: Layer functions: network layer
Responsibility: packet stream between end systems
3
Network layer
end-to-end transport of packets
ability to address source and target nodes
routing from source node to target node
find routes
choose between alternative routes
determine best packet size for a route
translate addresses
prevent or handle congestion
multiplexing of L4 packets
Notes: map of Oslo: Dr Blofeld@Wikimedia via OpenStreetMap

## Slide 50: Layer functions: transport layer
Responsibility: end-to-end message stream between processes
4
Transport layer
end-to-end transport of packets
ability to address source and target processes
establish process-to-process relation
multiplex traffic
end-to-end flow control (handles speed differences)
end-to-end error correction
wide range of services offered to L5:
connection establishment
no connection
hide L3 packet size limitations
limit L4 packet size to L3 packet’s
error correction
no error correction
ensure order of received packets
deliver packets as the arrive
adapt sending speed to receiver
send as fast as possible

## Slide 51: Layer functions: session layer
Responsibility: structured dialogue
support a “session” over a longer period
5
Session layer
Google OT (operation transformation) allows Google Docs to work
user identify when multiple devices are used
several inputs on the same document at the same time
conflict resolution when writing to the same location
session management
establishing identities
assigning writes
tracking identities (cookies)
token management
passing permission to speak in a (large) tele-conference
write-locking of networked files
transaction management in databases
synchronization
lip synchronization of speech and video in tele-conferencing
show live football concurrently on all devices
checkpointing
make program snapshots to disk
restart after crash

## Slide 52: Layer function: presentation layer
Responsibility: exchange of data (semantics!)
6
Presentation layer
encoding of int
big endian
little endian
XML (as string)
ASN.1 (shortest possible big endian bit sequence)
XDR (4-byte big endian)
encoding of strings
ASCII
UTF-8
Unicode
EBCDIC
semantics
NOK, EUR, USD
file name representation
/mnt/user/n.txt
m:\user\n.txt
encoding of date
seconds since 1.1.1970
nanoseconds since 1.1.1601
string “12 March 2019 13:32:54 UTC”
encoding of structs (“serialization”)
ASN.1
XDR
XML
JSON
Java serialization
Google protocol buffers
image formats
JPG, PNG
compression
zip, gzip, bzip2
encryption methods
PGP, S/MIME
Notes: Extended Binary Coded Decimal Interchange Code (EBCDIC)

## Slide 53: Layer functions: application layer
Responsibility: cooperating entities
7
Application layer
Notes: texting: Wonderlane@Flickr
Thunderbird: Mozilla Foundation
Weather: Daniel Nisbet@Flickr
Hangouts: OHSU Teacher@Vimeo
ESports: EsportsNews@Wikimedia
High Speed Trading: Rafael Matsunaga@Flickr via Wikimeddia

## Slide 54: Architecture
Data flow between two adjacent systems
1
Physical
2
Data link
3
Network
4
Transport
5
Session
6
Presentation
7
Application
End system
End system
peers
peers
peers
peers
peers
peers
peers

## Slide 55: Architecture
Data flow between two non-adjacent systems
1
2
3
4
5
6
7
End system
End system
peers
peers
peers
peers
peers
peers
peers
1
2
3
4
5
6
7
1
2
3
peers
peers
peers
Intermediate system

## Slide 56: Data Units
Application level “messages” are processed as data units.
Following notions for data units have become common:
  packet: “unit of transportation” (may contain fragments)
  datagram: instead of packet if sent individually (connectionless)
  frame: with final envelope, ready to send (next to lowest layer)
  cell: small packet (or packet fragment) of fixed size
OSI terminology: „message“ is a PDU
  PDU: Protocol Data Unit
  SDU: Service Data Unit = payload - optionally carried in PDU for user
    (N)-PDU: semantics understood by peer entities of (N)-service
    (N)-PDU = (N)-information plus (N)-SDU
    (N)-SDU = (N-1)-information plus (N-1)-SDU
© Ralf Steinmetz, Technische Universität Darmstadt
Notes: 56
ENVELOP: KONVOLUTT

## Slide 57: Network structures TCP/IP model
IN2140: Introduction to Operating Systems and Data Communication

## Slide 58: Five Layer Reference, Internet Reference Model and a Comparison
OSI Reference Model
TCP/IP Reference Model Internet Architecture
  ISO-OSI presentation, session and application layer merged
  ISO-OSI data link layer and physical layer merged to form Network Interface
1
2
3
4
some people use:
1
Physical layer
2
Data link layer
3
Network layer
4
Transport layer
5
Session layer
6
Presentation layer
7
Application layer
1/2
Network interface layer
Application layer
5

## Slide 59: TCP/IP Layering considerations
Why no clear separation of upper layers?
layers 1-4 are essential for co-existence on the Internet
  e.g. different congestion control mechanisms on different hosts can lead to strong congestion
session and presentation layer functions provide mostly application support
Layers 3 and 4 are not clearly separated
transport protocol (TCP, UDP, others) and network protocol IP
sometimes hard to draw a clear line where TCP ends and IP begins
example:
  Explicit Congestion Notification (ECN) capability is indicated on layer 3 and congestion is indicated on layer 3
  sender is told about receiver’s reception of congestion signal on layer 4
Notes: 59
Sidenote: 7-layer model has been extended… :-)
Layer 8: Financial layer
Layer 9: Political layer

## Slide 60: Internet Protocol Stack
Data link and
Physical layer
Network
layer
Transport
layer
Application
layer
WANs
ATM
LLC & MAC
physical
LANs
MANs
IPv4 + IPv6
+ ICMP
+ ARP
TCP
UDP
SMTP
HTTP
SCP
SSH
NFS
SRTP
Nickname: “Hourglass Model”
Notes: TIMEGLASS model