## Slide 1: Department of Informatics Networks and Distributed Systems (ND) group
IN3230/4230
Wireless Communications - III
Özgü Alay
ozgua@ifi.uio.no

## Slide 2: Outline
Mobile Broadband Networks
  International Roaming
Massive IoT
  NB-IoT
  LORAWAN
Paving the future
  Wifi 6
  5G and Beyond

## Slide 3: Free roaming in Europe

## Slide 4: Roaming Infrastructure

## Slide 5: Roaming Models
Home Routed (HR):
  The IP address of the roaming user is provided by the home network.
  All traffic to and from the mobile user is routed through the home network, for which a GTP tunnel is set up between the SGW of the visited network and the PGW of the home network (red path in the figure).
Local BreakOut (LBO):
  When LBO is used, the IP address of the roaming user is provided by the visited network.
  The GTP tunnel is terminated at the PGW of the visited network and IP-based services can be accessed directly from there (purple path in the figure).
IPX Hub Breakout (IHBO):
  The IP address of the roaming user is provided by the IPX network. The GTP tunnel from the SGW in the visited network terminates at a PGW in the IPX network (green path in the figure).
  There may be multiple PGWs so that latency and resource usage can be reduced by selecting one geographically close to the visited network.

## Slide 6
6 countries, 16 operators, each country has two nodes
One measurement server per country
Norway: Telia, Telenor
Sweden: Telenor, Tre, Telia
Spain: Orange, Vodafone, Movistar
Germany: Vodafone, O2, T-Mobile
UK: Vodafone, EE
Italy: Vodafone, TIM, WIND
MONROE-Roaming Nodes

## Slide 7
Roaming Configuration
Home Routed (HR) Roaming was used by all 16 MNOs!
Why all traffic is sent back to home network?
  HR provides the home operators with all the accounting and billing information
  Operators want to have near real-time view of the customer traffic for accounting reasons
  More complex debugging if HR is not used, who is responsible if there is a problem?

## Slide 8: Delay penalty of home-routed roaming
Packets go back and forth
Mimics LBO
Tunnel
vs
Internet

## Slide 9: Delay penalty of home-routed roaming geographically
RTT difference between the roaming SIM and the visited SIM
South to North has the highest delays
Germany is in a good position being in central Europe

## Slide 10: Outline
Mobile Broadband Networks
  International Roaming
Massive IoT
  NB-IoT
  LORAWAN
Paving the future
  Wifi 6
  5G and Beyond

## Slide 11: Growth in the number of connected devices

## Slide 13: Key Challenges for Massive IoT
Battery life – many IoT devices will be battery-powered, and often the cost of replacing batteries in the field is not viable. (Battery life time of 10 years)
Coverage and Range – deep indoor connectivity is a requirement for many applications in the utility area. Regional (or even national or global) coverage is a prerequisite for many use cases, especially within the transport area. (5 –40 km in the open field)
Quality of Service – providing a certain low bitrate reliably is important for many applications while latency is not that critical. (Typically a few hundred bit/s or less)
Deployment and device cost – clearly a key enabler for high-volume, mass-market applications, enabling many of the use cases. Moreover, in order to enable a Massive IoT market, networks need to scale efficiently. (Device cost of a few Euros)

## Slide 14: Low Power Wide Area Networks (LPWAN)

## Slide 15: What is LORAWAN?
Low Power, Wide Area (LPWA) networking protocol for IoT
Provides bi-directional communication, end-to-end security, mobility and localization services
Open source standard
Unlicensed band (EU 868)
LORA Alliance (400+ industry partner)
The Things Network (TTN)*: “a global, crowdsourced, open, free and decentralized LoRaWAN IoT platform”
*https://www.thethingsnetwork.org/

## Slide 16: LoRaWAN Architecture

## Slide 17: LoRaWAN Specification
Spectrum | Unlicenced 863-870 MHz frequency bands (in Europe) 125/250 KHz channels
Modulation and Access | LoRa modulation (Chirp Spread Spectrum (CSS)) LORAWAN MAC (Aloha)
Data rate | 250bps-50kbps
UE Max Tx Power | 14 dBm
Range | 5 km (urban), 20 km (rural)
Energy Efficiency | Adaptive Data Rate (ADR)
Notes: CSS used for Sonar and Radar

## Slide 18: Adaptive Data Rate (ADR)
Adaptive Data Rate (ADR) is a mechanism for optimizing data rates, airtime and energy consumption in the network.
Spreading Factor (SF): is the duration of the chirp. LoRa operates with spread factors from 7 to 12. SF7 is the shortest time on air, SF12 will be the longest.
ADR triggers:
  SF increase (device-side): Improves message delivery in harsh radio conditions
  SF decrease (network-side): Improves data rate and power consumption

## Slide 19: LORAWAN Network Coverage

## Slide 20: What is NB-IoT?
LPWAN radio technology standard developed by 3GPP to meet IoT application requirements
Builds on the LTE ecosystem, and can be deployed as a simple addition of new software to existing LTE infrastructure
  leading to fast development, scalibility, and global roaming
Includes state-of-the-art LTE security
  Identity management
  Authentication and authorization (embedded SIM)
  End to end encription of device data and signalling
Future feature growth for MBB and NB-IoT use cases

## Slide 21: NB-IoT Specification
Spectrum Deployment | 
Modulation and Access | Modulation: BPSK/QPSK MAC: DL: OFDMA, UL: SC-FDMA
Peak data rate | DL: 250 kbps UL: 20 kbps
UE Max Tx Power | 23 dBm
Coverage enhancements | Power Spectral Density boost Repetitions
Range | 1 km (urban), 10 km (rural)
Energy Efficiency | Power Saving Mode (PSM) extended Discontinuous Reception (eDRx)
Rel-13

## Slide 22: NB-IoT Coverage
Coverage Enhancement (CE) Techniques (w.r.t. LTE)
  Power Spectral Density boost: Tx power focused on smaller bands
  Repetitions: messages can be repeated up to 128 times
CE Level (CL) | # Repetitions
0 | [0-2]
1 | [4-16]
2 | [32-128]
CL0 = LTE coverage

## Slide 23: NB-IoT Power Savings
Power Saving Mode (PSM) is a power-off mode, in which the device nevertheless remains registered on the network
TAU: Tracking Area Update
RRC: Radio Resource Control
DRX: Discontinuous Reception

## Slide 24: NB-IoT Power Savings
extended Discontinuous Reception (eDRx) mode allows you to significantly increase the period of time when the receiving path of the device is turned off.

## Slide 25: NB-IoT Deployment
*Source: https://www.kotonlink.com/NewsDetail/2434022.html

## Slide 26: LORAWAN vs NB-IoT
Range and Penetration
Battery
Cost (deployment, spectrum, device)

## Slide 27: Overall LORAWAN vs NB-IoT

## Slide 28: Outline
Mobile Broadband Networks
  International Roaming
Massive IoT
  NB-IoT
  LORAWAN
Paving the future
  Wifi 6
  5G and Beyond

## Slide 29: Evolution of Use Cases
IEEE 802.11ac was designed for the traditional Wi-Fi application
  Consumer market with emphasize on Internet access.
  Enterprise application, e.g. an office building or a university with focus on connectivity.
IEEE 802.11ac design
  Wider Channels (80 and 160 MHz)
  DL MU MIMO
  Higher order MCS (256 QAM)

## Slide 30: Wifi 6: New Use Cases
The Wi-Fi landscape has been rapidly changing – more devices and bandwidth demanding applications
Multiple Interfering Devices
(dense deployment)
Video Traffic is becoming Dominate
Hotspots and Data offloading

## Slide 31: Key 802.11ax Enhancements
OFDMA
PHY and MAC Efficiency
Uplink
MU-MIMO
1024-QAM
Power Efficiencies
BSS Coloring
Frequency /Subcarriers

## Slide 32: 802.11ax – OFDMA Enables Spectral Efficiency
Frequency /Subcarriers
Frequency /Subcarriers
Time
Time
User1
User2
User3
User4
OFDM
OFDMA
Full Channel Bandwidth allocated to single user
Channel BW allocated among multiple users
Increase in spectral efficiency
Supports heterogeneous users – i.e. IM vs Large downloads

## Slide 33: Downlink and Uplink MU-MIMO
Up to 8x8 MU-MIMO Downlink
  Serving 8 users simultaneously in downlink
  2x gains compared to 4x4 MU-MIMO in 802.11ac
802.11ax introduces Up to 8x8 MU-MIMO Uplink
  Serving 8 users simultaneously in uplink
  8x gains compared to 1x1 MIMO in 802.11ac

## Slide 34: 802.11ax – Band and Sub-Carrier Spacing
Operates on 3 different frequency band
sub-carrier spacing is reduced to enable a 4X increase in the number of available channels, compared to 802.11ac.

## Slide 35: 802.11ax – 1024-QAM Constellation
25%
DATA RATE
INCREASE
256-QAM
1024-QAM
constellation diagrams
11ac
11ax

## Slide 36: 802.11ax – Power Efficiency
11ax AP
User1
User2
BEACON
TRIGGER
TRIGGER
AP
AWAKE
User1
User2
AWAKE
SLEEP
SLEEP
SLEEP
Pre-negotiated Wake times between AP and Users
AP can tell a user when to sleep and when to wake
Avoids contention on the air among users
Improves battery life since a device will know when to listen on a channel (up to 67% lower power consumption)
TARGET WAIT TIME

## Slide 37: 802.11ax – Spatial frequency reuse and BSS Coloring
OBSS – OVERLAPPING Basic Service Set
All APs using channel 1 waits for each other.
Different color APs using the same channel can ignore Interference from others. Colors enable them to differentiate between each other's data

## Slide 38: What is 5G?
5G is the 5th generation of mobile networks
Analogue
Digital
SMS
Multimedia
Video Calling
Mobile internet
Mobile Broadband
Enhanced Video
Mobile Connected World
Enhanced Mobile Broadband
Low latency applications
Internet of Things
Augmented and Virtual Reality (AR & VR)

## Slide 39: Different requirements for 5G applications and services

## Slide 40
Multi domain performance
  Energy Performance
  Critical machine type of communications
  Global standard
5G Mobile Network Expected Performance

## Slide 41: Back in the day…

## Slide 42: Network Flexibility: Virtualization

## Slide 45: Network Slicing for diverse requirements

## Slide 46: Capacity Enhancements
Small cells,
Relays, mobile
Relays and
Drones
new spectrum @ higher frequencies (above 6 GHz)
Massive MIMO
Spectrum sharing

## Slide 47: 5G Bands and its impact on Cell size

## Slide 48: Visible Light Communications
https://attract-eu.com/showroom/project/vladimir/

## Slide 49: Millimeter Wave Massive MIMO
B. Yang, Z. Yu, Y. Dong, J. Zhou and W. Hong, "Compact Tapered Slot Antenna Array for 5G Millimeter-Wave Massive MIMO Systems," in IEEE Transactions on Antennas and Propagation, vol. 65, no. 12, pp. 6721–6727, Dec. 2017.

## Slide 50: Multi-User MIMO Beamforming

## Slide 51: Spectrum Sharing: Multi-connectivity

## Slide 52: Ultra high reliability and Low Latency

## Slide 53
From 4G to 5G Transition
4G
5G
EPC
5G-CN
Today – 4G Access
Device attaches to LTE/4G radio and Evolved Packet Core (EPC)
Early 5G – Non-Standalone
Device attaches to 5G-NR, which routes either via 4G Base Station to EPC, or direct to EPC
4G acts as control plane
5G Standalone
Device attaches to 5G-NR and 5G Core Network.