## Slide 1: Department of Informatics Networks and Distributed Systems (ND) group
IN 3230 / IN 4230
Networking principles
Michael Welzl

## Slide 2: University education
“When I took Electrical Engineering, I didn’t learn how Sony builds amplifiers, I learned Maxwell.“ - John Day
Engineering training (job preparation): ok to focus on what and how
  You’re going to use it, you must know how it works
University education: should explain why
  You’re going to design future systems, you need to understand why things are how they are, and what is good or bad about them

## Slide 3: Next: communication principles
Building networking from scratch
  Starting with IPC in a single host
Several slides taken/adapted from John Day
For more details:
  John Day, “Patterns in Network Architecture: A Return to Fundamentals”. Prentice Hall, 2007.
First and foremost, a different way to think about layers

## Slide 4: Two application processes on one system
Inter Process Communication (IPC) within
a Single Processing System
IPC Facility
Application
Processes
Port
Ids
A
B
Application
Flow
This establishes the API: the application should not be able to distinguish a slow correspondent from operating over the Network.

## Slide 5: Two systems: how?
Distributed
IPC Facility
EFCP
EFCP
Application
Processes
Port
Ids
Management needed to find the other application
To do that, and then transfer data: need some sort of error and flow control protocol (EFCP) to transfer information between the two systems
  What are the functions this protocol needs?

## Slide 6: Functions of a Protocol
Data Corruption Detection/Correction – Making sure that the bits in the packet are correct (within some probability)
Delimiting – Packing SDUs into the User Data of PDUs and Marking the boundaries of an SDU, so we can find them again.
Fragmentation/Reassembly; Combining/Separation – Last Step of Delimiting, Creating User-Data fields of the PDUs
Ordering/Sequencing – Putting the PDUs in order, or putting sequence numbers on them for sending.
Loss and Duplicate Detection – Detecting entire lost PDUs, or duplicates due to retransmission.
Data Corruption Detection
Ordering
Frag/Reassembly
Delimiting

## Slide 7: Functions of a Protocol /2
Retransmission Control (Acknowledgement) – Recovering from lost PDUs.
Flow Control – Keeping the sender from overrunning the receiver, using either a Sliding Window or Rate-based.
These two are feedback mechanisms, therefore we need:
Synchronization – Ensuring that the sender and receiver maintain consistent state relative to each other.
Allocation/Deallocation – Allocating/Deallocating ports and creating and terminating synchronization.
Re-transmission
Control
Flow Control
Allocation
Synchronization
State
Vector
Data Corruption Detection
Ordering
Frag/Reassembly
Delimiting

## Slide 8: More than one application per system at the same time
Requires two new capabilities
EFCP must be able to distinguish one flow from another
  Typically use the port-ids of the source and destination
Will also need an application to manage multiple users of a single resource
Mux
Mux
EFCP
EFCP
EFCP
EFCP
EFCP
EFCP
Op
Seq #
CRC
Data
Connection-id
Src-port
Dest-port

## Slide 9: Communication with N systems

## Slide 10: Communication with N systems /2: A little re-organizing
We now have a Distributed IPC Facility (DIF) for each Interface, and to maintain the API we need an application over all of them.
  The user shouldn’t have to figure out which wire to use
But this will not scale, and it will get expensive fast. We need a cheaper way to do this.
Dir
Finder
A Virtual IPC Facility?
Res
Alloc

## Slide 11: Communication with N systems /3
Dedicate systems to IPC: since not everyone talks to everyone else the same amount, can reduce the number of lines required and even out usage.

## Slide 12: Communication with N systems /4
Relaying systems over a wider scope requires carrying addresses
Creates more problems: e.g., can’t avoid transient congestion and bit errors in relay memories; what about message order? etc.
  Will have to have an EFCP operating over the relays
EFCP
EFCP
Interface
IPC
Processes
Relaying
Application
Relaying
PM
Interface
IPC
Processes
Dest Addr
Src Addr
Common Relaying and Multiplexing Application Header

## Slide 13: A recursive structure!
Distributed IPC Facilities

## Slide 14: Implications
The essential role of layers is not to be a collection of a specific set of functions but instead to define a communication scope
  Different from what OSI and DoD models say!
Some essential functions exist at every layer, although they might be instantiated differently depending on the environment
  Even if the functions are exactly the same, it's not a repetition: they only occur once per scope
Layers can be stacked as needed, there should be no dependencies and there can always be the same interfaces between layers

## Slide 15
Layers
Networks have loci of distributed shared state with different scopes
At the very least, differences of scope require different layers
If layers have the same scope, their functions should be completely independent
Does this picture show the Internet?
Host or End System
Router
Increasing
Scope
Notes: 15

## Slide 16
The Internet
Host or End System
Router
Link layer
Physical layer
Network layer
Transport layer
Application layer
Remember the IP fragmentation problem from intro lecture?
  Dependencies between functions of layers with the same scope
What does the recursive structure tell us, what can we learn?
  Next: an example of functionality: flow + congestion control
Notes: 16

## Slide 17: Developing flow + congestion control
How fast can we send?
  Vertical interface should probably include a “rate”
  EFCP should implement flow control
S1
R1
A1
A2
DIF
Sender
Receiver
Or something similar...e.g. a credit (window)

## Slide 18: Developing flow + congestion control /2
How fast can we send?
  Vertical interface should probably include a “rate”
  EFCP should implement flow control
S1
R1
A1
A3
DIF
A2
Sender
Relay
Receiver
1
1
2
1

## Slide 19: Developing flow + congestion control /3
How fast can we send?
  Vertical interface should probably include a “rate”
  Layer ("DIF") should implement flow + congestion control
S2
R1
A1
A3
DIF
A2
Sender
Relay
Receiver
1
1
2
1
S1
R2
Multiple senders / receivers

## Slide 20: Developing flow + congestion control /4
How fast can we send?
  Vertical interface should probably include a “rate”
  2-DIFs EFCP should (at least) implement flow control, and 1-DIF EFCP should (at least) implement congestion control
S1
A1
A2
A3
1-DIF
B1
B2
2-DIF #2
S2
R1
R2
B1
B2
2-DIF #1

## Slide 21: Developing flow + congestion control /5
How fast can we send?
  Vertical interface should probably include a “rate”
  Every layer should probably implement some form of flow control, and congestion control when there are relays serving multiple flows
A1
A2
S
R
A2
A1
B1
B2
B3
1-DIF #2
2-DIF
Sender
Relay 1
Receiver
1-DIF #1
Relay 2
A3
C1
C2
3-DIF
Multiple senders / receivers

## Slide 22: And the Internet?
How fast can we send?
  Who’s deciding what, what are the interfaces?
A1
A2
S
R
A2
A1
B1
B2
B3
Ether- net
Network layer
Sender
IP router
Receiver
WiFi
Ethernet switch
A3
C1
C2
Transport layer
Down/up: just buffers
Down/up: just buffers
No info about speed; only queue management
Even here we don't easily learn "how fast" !
MAC algorithms implement overload control
TCP etc. implement congestion control
Notes: Strictly speaking, the 4 addresses in WiFi are two layers with the relay occurring in the upper WiFi layer to Ethernet, so in this figure there is no relaying in the Network Layer.

## Slide 23: E.g. Linux
Useful TCP "speed" feedback: "low water mark"
  Patch with "TCP_NOTSENT_LOWAT" socket option, 2013
  Apple computers also offer this
From: C. A. Grazia, N. Patriciello, T. Høiland-Jørgensen, M. Klapez, M. Casoni and J. Mangues-Bafalluy, "Adapting TCP Small Queues for IEEE 802.11 Networks," PIMRC 2018, Bologna.
L2
L3
L4

## Slide 24
Addresses
Host or End System
Router
Increasing
Scope
Network 1. Addresses could be:
A, B, C, D, ...
Network 2. Addresses could be: 1, 2, 3, 4, ...
Addresses could be: 129.240.118.130
Network 1 is completely unaware of addresses of type 1, 2, 3,..
  Networks and their addresses could dynamically be registered (attached)
  This is also more secure
Notes: 24

## Slide 25
Internet addresses
Host or End System
Router
Link layer
Physical layer
Network layer
Transport layer
Application layer
No intermediate layer of smaller scope
  IP addresses are long, routers need to store a lot of information
Also, running out of addresses: IPv6 is the solution
Network Address (and Port) Translators (NA(P)Ts): more practical
  Store mapping: “local IP address + TCP port  global IP address + TCP port”
  Problem because depends on transport protocol, inside the network... e.g., need to send keep-alives to keep state up
  Peer-to-peer communication, both peers behind NATs: how to talk? Complex solutions (STUN, TURN, ICE protocols)
Notes: 25

## Slide 26: IP mobility
Long ago, I moved from Bogstadveien to Thorvald Meyers Gate
  I registered to have mail forwarded for a month for free (postens flyttehjelp)
  This gave me time to inform everyone about my new address (posten offers an easy service to do that)
  After this month, I had no more business with the old address
Imagine a world without addresses
  But where, instead, my name is Bogstadveien
  Moving: use “postens flyttehjelp” forever!
One of the Internet's solutions: Multipath TCP (MPTCP)
  Applications should bind to names, not IP addresses
  MPTCP can switch without interruption
Mobile IP does exactly this.
or 129.240.118.130, for example...

## Slide 27
Routing
Host or End System
Router
Increasing
Scope
How would one route between the addresses on network 1?
Next: an example with multi-homing and link failure
Network 1. Addresses could be:
A, B, C, D, ...
Notes: 27

## Slide 28: Using node addresses
Since we want to emphasize that we are naming nodes, lets just use the letters for addresses. But we still have to say which wire to send them on.
  There are two cases in general:
    Point-to-point Wire: No need for lower layer addresses, use local identifiers.
    Multi-access wired or wireless: Here we need addresses, use MAC addresses.
  We have only wires, so lets assign small integers as the local interface identifiers.
Now lets say that A wants to send a PDU to H, so it goes to DNS and looks up the address and gets 9. Now these nodes have been running a routing algorithm and the route is A, B, D, F, H.
So what do the router tables look like? (see next slide)
G
A
B
C
E
D
F
H
1
2
3
1
2
1
3
4
1
2
3
1
2
3
1
2
3
1
1
2
2
2
Notes: What is the first thing you notice about the routing tables?
They are much shorter. Previously we need 22 addresses, now we need 8. The more wires terminating on each node the more addresses we will need for interface addressing.
Remember point to point wires don’t need addresses so we can use local identifiers at each node to identify which wire we are sending it on. They don’t have to be unique.
So what happens when a PDU is sent?

## Slide 30: Sending a PDU from A to H
A has a PDU addressed to H:
  A consults its Forwarding Table and sends the PDU on interface 2 to B.
  B consults its Forwarding Table and sends the PDU on interface 2 to D.
  D consults its Forwarding Table and sends the PDU on interface 2 to F.
  F consults its Forwarding Table and sends the PDU on interface 2 to H.
G
A
B
C
E
D
F
H
1
2
3
1
2
1
3
4
1
2
3
1
2
3
1
2
3
1
1
2
2
2
Notes: Sorry about that I didn’t intend for the interfaces to all turn out to have the same number! ;-) When I assigned them, I was trying to make sure it didn’t have the same number on both ends! ;-)

## Slide 31: What happens when link F - H fails?
What happens if just after the PDU is sent the Link from F to H fails?
  In a few 10s of ms, a routing update is done, and a new Routing Table is generated.
  The PDU gets to D after the routing update has concluded and is delivered to H as if nothing happened.
  PDUs that might have been between B, D, and F might get re-routed. Only PDUs on the wire from F to H would be lost.
G
A
B
C
E
D
F
H
1
2
3
1
2
1
3
4
1
2
3
1
2
3
1
2
3
1
1
2
2
2
Notes: Can you come up with the new Tables?

## Slide 32
Internet routing
Host or End System
Router
Link layer
Physical layer
Network layer
Transport layer
Application layer
Always Between IP addresses
What if a node has multiple interfaces ( = is multihomed) ?
  Need to use an IP address per interface to distinguish them
  Hence, IP address identifies the interface, not the node
Next: example, using “normal” letters and numbers for clarity
Notes: 32

## Slide 33: Internet multihoming
Internet addresses name the interfaces. Let’s see what this does
Assume: A wants to send a PDU to H, so it goes to DNS and looks up the address and gets 9. Now these nodes have been running a routing algorithm and the route is A, B, D, F, H.
So what do the router tables look like? (next slide)
G
A
B
C
E
D
F
H
1
2
6
5
8
3
14
18
17
16
15
19
21
13
20
9
11
10
12
4
7
22
Notes: I used a very scientific algorithm. ;-) First I chose the path from A to H and pretended it was the optimal path chosen by a routing algorithm. Then for the forwarding tables, I assumed that even if it might be more hops, it was the preferred path. I also assumed nearest neighbors were always cheaper than going elsewhere (I think I did that). So if a Destination was more than one hop away but on the chosen path from A to H, I went to the nearest node on that path. That doesn’t really matter to what we are demonstrating.

## Slide 35: A PDU is sent with destination address 9 from A
A consults its Forwarding Table and sends it on outgoing address 1, next hop 22.
B consults its FT and sends it on outgoing address 7, next hop 15.
D consults its FT and sends it on outgoing address 14, next hop 20.
F consults its FT and sends it on outgoing address 11, next hop 9.
Now another PDU is sent from A to address 9, just after it leaves, the interface goes down.
G
A
B
C
E
D
F
H
1
2
6
5
8
3
14
18
17
16
15
19
21
13
20
9
11
10
12
4
7
22

## Slide 36: What happens when link F - H fails?
What happens if the link with address 9 goes down?
  In a few 10s of ms, a routing update is done, and Addresses 9 and 11 are eliminated from the forwarding table.
  After several seconds and many retries, A determines that Address 9 is not responding,
  All TCP connections with Address 9 are terminated.
  All PDUs enroute to 9 are lost.
  Hopefully, there is a second DNS entry that lists H as also at Address 10.
  Connections are re-established using address 10. Several seconds have elapsed.
G
A
B
C
E
D
F
H
1
2
6
5
8
3
14
18
17
16
15
19
21
13
20
9
11
10
12
4
7
22

## Slide 37: A modern Internet solution: MPTCP
A and H initially tell each other about all their addresses (A: 1, 2; H: 9, 10)
MPTCP subflows are established; number depends on path manager configuration
  E.g. fullmesh: 4 subflows (1-9, 1-10, 2-9, 2-10)
  Then, normally: use all of them (schedule traffic, e.g. round-robin or preferring least-RTT path until cwnd full; “cautious” congestion control – be at most as aggressive as 1 TCP across a common bottleneck)
F-H link goes down: one subflow becomes unavailable, no TCP failure for application
This is done e.g. by iPhones since iOS 7: https://support.apple.com/en-us/HT201373
G
A
B
C
E
D
F
H
1
2
6
5
8
3
14
18
17
16
15
19
21
13
20
9
11
10
12
4
7
22

## Slide 38: Architectural principles of the Internet
Yes, there are some...
Different from recursive principles laid out so far

## Slide 39: Two important Internet rules
End-to-end ("e2e") argument
  Carefully consider trade-offs between implementing functions inside the network versus end systems
  Think twice before letting the network do it
  No application-specific functionality in the network
  Frequently interpreted too strictly: "keep the network dumb, put all logic in end systems"
Postel's robustness principle: "Be conservative in what you send, be liberal in what you accept"
  Ensures downward compatibility (e.g. "reserved" bits)

## Slide 40: .. and problems with them
"Pervasive Monitoring is an Attack"
  RFC 7258
Also: ossification
  Middleboxes make assumptions, e.g. about TCP, break Postel's principle
Solution(?) encrypt everything, end-to-end !
  Also protocol headers (e.g. QUIC)
  Pure "e2e" restored - no more ossification; good?
  Also, no more control by ISPs... more control to Google?
Header field “greasing”
  Avoiding to create expectations like “this bit is always 0” (“Use it or lose it”)
Consider: intro slides multi-path transfer example

## Slide 41: Critical thinking, applied to common Internet views
NATs are evil. IPv6 should be deployed everywhere.
  Or... are NATs doing the right thing?
IP fragmentation is a bad idea
  or does it just highlight a design flaw?
Middleboxes are bad
  or are we just missing interfaces to cleanly make them a part of the architecture?

## Slide 42: A final note about recursive networking
Recursive InterNetwork Architecture (RINA)
  By John Day
  More material: http://pouzinsociety.org
Research prototypes exist, ... but many issues and unresolved questions
  Just saying “everything is wrong” does not automatically solve it...
  So, again: this was about a way of thinking

## Slide 43: Thank you!
Questions?