## Slide 1: Introduction to MPLS
Tor Skeie
University of Oslo, Department of informatics
This presentation is based mainly on Santanu Dasgupta´s slide series that describe the Multiprotocol Label Switching (MPLS) concept Santanu Dasgupta is a Distinguished Architect at Cisco

## Slide 2: Theory
ISO/OSI model
DoD model
5. Application
4. Transport
3. Network
2. Link Layer

## Slide 3: Reality
Typical packet from AT&T backbone network
Pamela Zave and Jennifer Rexford. 2019. The compositional architecture of the internet. Commun. ACM 62, 3 (February 2019), 78-87. DOI: https://doi.org/10.1145/3226588

## Slide 4: Introduction to MPLS
Santanu Dasgupta
sadasgup@cisco.com

## Slide 5: Goals of this Lecture
Understand the business drivers for MPLS
Learn about MPLS customer and market segments
Understand the problems MPLS is addressing
Understand benefits of deploying MPLS
Understand the major MPLS technology components
Understand typical applications of MPLS

## Slide 6: Agenda
Introduction
MPLS Network Components
MPLS Traffic Engineering
MPLS VPNs
  MPLS Layer-3 VPNs
  MPLS Layer-2 VPNs
Summary
Core MPLS
End-to-end MPLS Services
MPLS Network Services

## Slide 7
Introduction

## Slide 8: The Big Picture
MPLS in Core Network
Edge
Edge
Edge
Edge
Core
Core
Core
Core
Edge
Edge
Edge
Edge
Network Infrastructure
MPLS Signaling and Forwarding
MPLS Signaling and Forwarding
MPLS Network Services
MPLS QoS
MPLS OAM/MIBs
MPLS TE
End-to-end MPLS VPN Services
End-to-end MPLS-enabled Services
Layer-3 VPNs
Layer-2 VPNs
Network Infrastructure
MPLS Signaling and Forwarding
Layer-3 VPNs
Layer-2 VPNs
MPLS QoS
MPLS OAM/MIBs
MPLS TE
End-to-end Services
MPLS Network Services
Core MPLS

## Slide 9: Why Multi Protocol Label Switching?
SP/Carrier perspective
  Reduce costs (CAPEX); consolidate networks
  Consolidated network for multiple Layer-2/3 services
  Support increasingly stringent SLAs
  Handle increasing scale/complexity of IP-based services
Enterprise/end-user perspective
  Campus/LAN
  Need for network segmentation (users, applications, etc.)
  WAN connectivity (connecting enterprise networks)
  Need for easier configuration of site-to-site WAN connectivity
Notes: Carrier perspective
  Reduce costs (CAPEX); need for collapsing separate (legacy) networks into a single converged network infrastructure
  Need for support of both traditional layer-2 services (ATM, FR) and IP/Layer-3 IP-services over single network infrastructure
  Increasingly stringent SLAs; need for ‘layer-2’-type traffic engineering, incl. bandwidth management, failure protection
  Increasing scale of IP-based services; need for flexible and scalable service provisioning and maintenance capabilities

## Slide 10: What Is MPLS Technology?
It’s all about labels …
Use the best of both worlds
  Layer-2 (ATM/FR): efficient forwarding and traffic engineering
  Layer-3 (IP): flexible and scalable
MPLS forwarding plane
  Use of labels for forwarding Layer-2/3 data traffic
  Labeled packets are being switched instead of routed
  Leverage layer-2 forwarding efficiency
MPLS control/signaling plane
  Use of existing IP control protocols extensions + new protocols to exchange label information
  Leverage layer-3 control protocol flexibility and scalability

## Slide 11: Evolution of MPLS
Evolved from tag switching in 1996 to full IETF standard, covering over 130 RFCs
Key application initially were Layer-3 VPNs, followed by Traffic Engineering (TE), and Layer-2 VPNs

## Slide 12: MPLS Applications
EWAN
Edge
Service
Providers
Enterprise Data
Center
Data center interconnects
L2/L3VPN’s
TE/FRR
QoS
High Availability
VPN’s / VRF’s
VRF-Aware Security
High Availability
Hosted Data centers
Data center interconnect
Segmentation for IT
Mergers, Acquisitions, spinoffs
Applications
Key Features
Departmental segmentation
Service multiplexing
Security
Mergers, Acquisitions, spinoffs
Disaster Recovery
Vmotion support
Branch Interconnects
Internet Access
Branch Connectivity
VPN’s / VRF’s
VRF Aware Security
High Availability
VPN’s
TE/FRR
High Availability
Network Consolidation – Merging Multiple parallel network into a shared infrastructure
Network segmentation – By user groups or business function
Service and policy centralization – Security policies and appliances at a central location
New applications readiness – Converged multi-service network
Increased network security – User groups segmentation with VPNs
For your reference only

## Slide 13: Enterprise MPLS Customers
Two types of enterprise customers for MPLS technology
MPLS indirectly used as subscribed WAN service
  Enterprise subscribes to WAN connectivity data service offered by external Service Provider
  Data connectivity service implemented by Service Provider via MPLS VPN technology (e.g., layer-2 and layer-3 VPNs)
  VPN Service can be managed or unmanaged
MPLS used as part of self managed network
  Enterprise deploys MPLS in it’s own network
  Enterprise manages it’s own MPLS-based network

## Slide 14
MPLS Technology Components
Basic building blocks of MPLS

## Slide 15: MPLS Forwarding and Signaling
MPLS label forwarding and signaling mechanisms
Network Infrastructure
MPLS Signaling and Forwarding
Layer-3 VPNs
Layer-2 VPNs
MPLS QoS
MPLS OAM/MIBs
MPLS TE
Core MPLS

## Slide 16: Basic Building Blocks
The big picture
  MPLS-enabled network devices
  Label Switched Paths (LSPs)
The internals
  MPLS labels
  Processing of MPLS labels
  Exchange of label mapping information
  Forwarding of labeled packets
Other related protocols to exchange label information
  Between MPLS-enabled devices

## Slide 17: MPLS Network Overview
MPLS Domain
P (Provider) router = label switching router = core router (LSR)
  Switches MPLS-labeled packets
PE (Provider Edge) router = edge router (LSR)
  Imposes and removes MPLS labels
CE (Customer Edge) router
  Connects customer network to MPLS network
CE
CE
CE
CE
Label switched traffic
P
P
P
P
PE
PE
PE
PE

## Slide 18: MPLS Label and Label Encapsulation
COS/EXP = Class of Service: 3 Bits; S = Bottom of Stack; TTL = Time to Live
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
Label # – 20bits
EXP
S
TTL-8bits
MPLS Label
Label
PPP Header
Layer 2/L3 Packet
PPP Header
(Packet over SONET/SDH)
MPLS Label Encapsulation
One or More Labels Appended to the Packet (Between L2/L3 packet header and link layer header)
LAN MAC Label Header
Label
MAC Header
Layer 2/L3 Packet

## Slide 19: MPLS Label Operations
Label imposition (Push)
  By ingress PE router; classify and label packets
Label swapping or switching
  By P router; forward packets using labels; indicates service class & destination
Label disposition (PoP)
  By egress PE router; remove label and forward original packet to destination CE
CE
CE
CE
CE
P
P
PE
PE
PE
L1
Label Imposition (Push)
L2/L3 Packet
L1
L2
Label Swap
P
L2
L3
Label Swap
PE
L3
Label Disposition (PoP)
P

## Slide 20: Forwarding Equivalence Class
Mechanism to map ingress layer-2/3 packets onto a Label Switched Path (LSP) by ingress PE router
  Part of label imposition (Push) operation
Variety of FEC mappings possible
  IP prefix/host address
  Groups of addresses/sites (VPN x)
  Used for L3VPNs
  Layer 2 circuit ID (ATM, FR, PPP, HDLC, Ethernet)
  Used for Pseudowires (L2VPNs)
  Tunnel interface
  Used for MPLS traffic engineering (TE)

## Slide 21: Label Distribution Protocol
MPLS nodes need to exchange label information with each other
  Ingress PE node (Push operation)
    Needs to know what label to use for a given FEC to send packet to neighbor
  Core P node (Swap operation)
    Needs to know what label to use for swap operation for incoming labeled packets
  Egress PE node (Pop operation)
    Needs to tell upstream neighbor what label to use for specific FEC type LDP used for exchange of label (mapping) information
Label Distribution Protocol (LDP)
  Defined in RFC 3035 and RFC3036; updated by RFC5036
  LDP is a superset of the Cisco-specific Tag Distribution Protocol
Note that, in addition LDP, also other protocols are being used for label information exchange
  Will be discussed later

## Slide 22: Some More LDP Details
Assigns, distributes, and installs (in forwarding) labels for prefixes advertised by unicast routing protocols
  OSPF, IS-IS, EIGRP, etc.
Also used for Pseudowire/PW (VC) signaling
  Used for L2VPN control plane signaling
Uses UDP (port 646) for session discovery and TCP (port 646) for exchange of LDP messages
LDP operations
  LDP Peer Discovery
  LDP Session Establishment
  MPLS Label Allocation, Distribution, and Updating MPLS forwarding
Information repositories used by LDP
  LIB: Label Information Database (read/write)
  RIB: Routing Information Database/routing table (read-only)
For your reference only

## Slide 23: LDP Operations
LDP Control Plane
MPLS Node A
LDP startup
  Local labels assigned to RIB prefixes and stored in LIB
  Peer discovery and session setup
  Exchange of MPLS label bindings
Programming of MPLS forwarding
  Based on LIB info
  CEF/MFI updates
MPLS Node B
Session Setup
Label Binding Exchange
MPLS Forwarding
CEF/MFI
RIB
LIB
MPLS Forwarding
CEF/MFI
LDP Interactions with MPLS Forwarding
LIB
RIB
Notes: This diagram depicts the most important interactions internal and external to a node.
LDP keeps local labels mapping and remote bindings learned from its peers in a data structure call the LIB (Label Information Base). The contents of LIB are kept up to date with interaction with RIB. On route up and down the contents are change as seen necessary. On the other hand the remote bindings are updated as peers go away, new peers come up, or a peer decides to use a different label for a specific prefix.
LDP also interacts with the MFI/CEF to ensure that if an mpls path is available for a route known by IGP, the incoming and outgoing label are made available. LDP is also responsible to update this information if there is a route change or a change by a peer dictates change in the forwarding.
The programming of the forwarding is normally done using the pull model. In other words when there is a change either in LDP control plane or igp, the forwarding infrastructure is asked to pull the label information from LDP and program into forwarding.

## Slide 24: MPLS Control and Forwarding Plane
MPLS control plane
  Used for distributing labels and building label-switched paths (LSPs)
  Typically supported by LDP; also supported via RSVP and BGP
  Labels define destination and service
MPLS forwarding plane
  Used for label imposition, swapping, and disposition
  Independent of type of control plane
  Labels separate forwarding from IP address-based routing
  MFI – MPLS Forwarding Infrastructure
LIB
Routing Updates/ Adjacencies
MFI
MPLS Traffic Forwarding
FIB
MPLS Process
Routing Process
RIB
Label Binding Updates/ Adjacencies
IP Traffic Forwarding

## Slide 25: IP Packet Forwarding Example
0
1
1
128.89
171.69
0
128.89.25.4
Data
128.89.25.4
Data
128.89.25.4
Data
128.89.25.4
Data
Packets Forwarded Based on IP Address (via RIB lookup)
…
128.89
171.69
Address
Prefix
I/F
1
1
…
128.89
171.69
Address
Prefix
I/F
0
1
…
128.89
171.69
Address
Prefix
I/F
0
1
FIB
FIB
FIB
Notes: Now when a packet comes into a router a look up is done based on the IP address in the packet, at match is obtained, and the packet is forwarded out the appropriate interface.
The packet follows the same process on a hop-by-hop bases through the network until it reaches its destination.

## Slide 26: Step 1: IP Routing (IGP) Convergence
128.89
171.69
1
0
1
In
Label
Address
Prefix
…
Out
I’face
128.89
1
171.69
1
…
Out
Label
In
Label
Address
Prefix
…
Out
I’face
128.89
0
171.69
1
…
Out
Label
In
Label
Address
Prefix
128.89
…
Out
I’face
0
…
Out
Label
0
You Can Reach 171.69 Thru Me
You Can Reach 128.89 and
171.69 Thru Me
Routing Updates (OSPF, EIGRP, …)
You Can Reach 128.89 Thru Me
MFI/FIB
MFI/FIB
MFI/FIB
Notes: Tag edge routers and tag switches use standard IP routing protocols to identify routes through the network. Theses fully interoperate with non-tag switching routers
So what tag switching does is it extends the forwarding table by adding a tag field. One for the incoming tag and one for the outgoing tag. Note the topology of the network is discovered using unmodified layer 3 protocols such as OSPF.

## Slide 27: Step 2a: LDP Assigns Local Labels
1
128.89
0
1
0
171.69
In
Label
Address
Prefix
128.89
171.69
…
Out
I’face
1
1
…
Out
Label
In
Label
Address
Prefix
128.89
171.69
…
Out
I’face
0
1
…
Out
Label
In
Label
Address
Prefix
128.89
…
Out
I’face
0
…
Out
Label
…
-
-
…
…
4
5
…
-
…
9
…
MFI/FIB
MFI/FIB
MFI/FIB
Notes: Tag routers and switches use the tables generated by the standard routing protocols to assign and distribute tag information via the tag distribution protocol (TDP). Tag routers receive the TDP information and build a forwarding database, which makes use of the tags.
TDP is then used to bind tags to routes and distribute this information to each routers upstream neighbor.

## Slide 28: Step 2b: LDP Assigns Remote Labels
1
128.89
0
1
0
Use Label 9 for 128.89
Use Label 4 for 128.89 and
Use Label 5 for 171.69
Label Distribution Protocol (LDP)
(Downstream Allocation)
171.69
Use Label 7 for 171.69
In
Label
Address
Prefix
128.89
171.69
…
Out
I’face
1
1
…
Out
Label
In
Label
Address
Prefix
128.89
171.69
…
Out
I’face
0
1
…
Out
Label
In
Label
Address
Prefix
128.89
…
Out
I’face
0
…
Out
Label
4
5
…
-
-
…
9
7
…
4
5
…
-
…
9
…
MFI/FIB
MFI/FIB
MFI/FIB
Notes: Tag routers and switches use the tables generated by the standard routing protocols to assign and distribute tag information via the tag distribution protocol (TDP). Tag routers receive the TDP information and build a forwarding database, which makes use of the tags.
TDP is then used to bind tags to routes and distribute this information to each routers upstream neighbor.

## Slide 29: Step 3: Forwarding MPLS Packets
1
0
1
128.89.25.4
Data
128.89.25.4
Data
4
128.89.25.4
Data
9
Label Switch Forwards Based on Label
128.89.25.4
Data
128.89
0
171.69
In
Label
Address
Prefix
128.89
171.69
…
Out
I’face
1
1
…
Out
Label
In
Label
Address
Prefix
128.89
171.69
…
Out
I’face
0
1
…
Out
Label
In
Label
Address
Prefix
128.89
…
Out
I’face
0
…
Out
Label
4
5
…
-
-
…
9
7
…
4
5
…
-
…
9
…
MFI/FIB
MFI/FIB
MFI/FIB
Notes: When we get to the first router, the one performing the tag imposition, there’s an IP look-up based on the IP prefix. It finds the forwarding table entry and it discovers that to get to the destination it should use tag x. It sticks that tag on the front of the packet and forwards it along to the next hop tag switch.
At this point the router can just do pure tag forwarding, gets in the packet with tag x, figures our that the outgoing interface is y, and the outgoing tag replaces the incoming tag. Note packet is forwarded based solely on the tag without re-analyzing the network layer header. This provides the essential separation of routing and forwarding referred to earlier.
The packet reaches the tag edge router at the egress point of the network ,where the tag is stripped off and the packet delivered.

## Slide 30: Summary Steps For MPLS Forwarding
Each node maintains IP routing information via IGP (Interior Gateway Protocol)
  IP routing table (RIB) and IP forwarding table (FIB)
LDP leverages IGP routing information
LDP label mapping exchange (between MPLS nodes) takes place after IGP has converged
  LDP depends on IGP convergence
  Label binding information stored in LIB
Once LDP has received remote label binding information MPLS forwarding is updated
  Label bindings are received from remote LDP peers
  MPLS forwarding via MFI (MPLS Forwarding Infrastructure)

## Slide 31: MPLS Network Protocols
IGP: OSPF, EIGRP, IS-IS on core facing and core links
LDP on core and/or core facing links
MP-iBGP on PE devices (for MPLS services), MP-BGP: Multiprotocol Border Gateway Protocol, used for MPLS L3 VPN
Label switched traffic
P
P
P
P
PE
PE
PE
PE
OSPF, IS-IS, EIGRP, EIGRP
LDP, RSVP
MP-iBGP
CE
CE
CE
CE

## Slide 32
MPLS Network Protocols

## Slide 33: Label Stacking
More than one label can be used for MPLS packet encapsulation
  Creation of a label stack
Recap: labels correspond to Forwarding Equivalence Class (FEC)
  Each label in stack used for different purposes
Outer label always used for switching MPLS packets in network
Remaining inner labels used to specific services/FECs, etc.
Last label in stack marked with EOS bit
Allows building services such as
  MPLS VPNs; LDP + VPN label
  Traffic engineering (FRR): LDP + TE label
  VPNs over TE core: LDP + TE + VPN label
  Any transport over MPLS: LDP + PW label
TE Label
LDP Label
VPN Label
Inner Label
Outer Label
Layer 2/3 Packet Header

## Slide 34
Tunnel label determines the path to remote edge
VC label designates connection at tunnel endpoint

## Slide 35
Tunnel label determines the path to remote edge
VC label designates connection at tunnel endpoint

## Slide 36: Summary
MPLS uses labels to forward traffic
More than one label can be used for traffic encapsulation; multiple labels make up a label stack
Traffic is encapsulated with label(s) at ingress and at egress labels are removed in MPLS network
MPLS network consists of PE router at ingress/egress and P routers in the core
MPLS control plane used for signaling label mapping information to set up end-to-end Label Switched Paths
MPLS forwarding plane used for label imposition (PUSH), swapping, and disposition (POP) operation

## Slide 37
MPLS Traffic Engineering
Technology Overview and Applications

## Slide 38: MPLS Technology Framework
Network Infrastructure
MPLS Signaling and Forwarding
Layer-3 VPNs
Layer-2 VPNs
MPLS QoS
MPLS OAM/MIBs
MPLS TE

Traffic engineering capabilities for bandwidth management and network failure protection

## Slide 39: Why Traffic Engineering?
Congestion in the network due to changing traffic patterns
  Election news, online trading, major sports events
Better utilization of available bandwidth
  Route on the non-shortest path
Route around failed links/nodes
  Fast rerouting around failures, transparently to users
  Like SONET APS (Automatic Protection Switching)
Build new services—virtual leased line services
  VoIP toll-bypass applications, point-to-point bandwidth guarantees
Capacity planning
  TE improves aggregate availability of the network

## Slide 40: The Problem with Shortest-Path
Massive (44%) packet loss at router B→router E!
  Changing to A->C->D->E won’t help
Router F
Router C
Router D
80 Mb Traffic
35 Mb Drops!
Router A
Router B
OC-3
OC-3
DS3
DS3
DS3
OC-3
OC-3
Some links are DS3 (45 Mbps), some are OC-3 (155 Mbps)
Router A has 40M of traffic for router F, 40M of traffic for router G
Router E
Router G
Node | Next-Hop | Cost
B | B | 10
C | C | 10
D | C | 20
E | B | 20
F | B | 30
G | B | 30
IP (Mostly) Uses Destination-Based Least-Cost Routing Alternate Path Under Utilized

## Slide 41: How MPLS TE Solves the Problem
Router A sees all links
Router A computes paths on properties other than just shortest cost; creation of 2 tunnels
No link oversubscribed!
Router C
Router D
40 Mb
OC-3
OC-3
DS3
DS3
DS3
OC-3
OC-3
Router F
Router C
Router D
Router G
Router A
Router B
Router E
40 Mb
Node | Next-Hop | Cost
B | B | 10
C | C | 10
D | C | 20
E | B | 20
F | Tunnel 0 | 30
G | Tunnel 1 | 30

## Slide 42: How MPLS TE Works
Link information Distribution*
  ISIS-TE
  OSPF-TE
Path Calculation (CSPF)*
Path Setup
Forwarding Traffic down Tunnel
  Auto-route
  Static
  PBR
  CBTS / PBTS
  Forwarding Adjacency
  Tunnel select
* Optional
IP/MPLS
Head end
Mid-point
Tail end
TE LSP

## Slide 43: Link Information Distribution
Additional link characteristics
  Interface address
  Neighbor address
  Physical bandwidth
  Maximum reservable bandwidth
  Unreserved bandwidth (at eight priorities)
  TE metric
  Administrative group (attribute flags)
IS-IS or OSPF flood link information
TE nodes build a topology database
Not required if using off-line path computation
http://www.cisco.com/go/mpls
IP/MPLS
TE Topology database
For your reference only

## Slide 44: Path Calculation
TE nodes can perform constraint-based routing
Constraints and topology database as input to path computation
Shortest-path-first algorithm ignores links not meeting constraints
Tunnel can be signaled once a path is found
Not required if using offline path computation
http://www.cisco.com/go/mpls
IP/MPLS
TE Topology database
5
3
10
15
10
10
8
10
R1
R8
Link with insufficient bandwidth
Link with sufficient bandwidth
n
n
Find shortest path to R8 with 8Mbps

## Slide 45: TE LSP Signaling
Tunnel signaled with TE extensions to RSVP
Soft state maintained with downstream PATH messages
Soft state maintained with upstream RESV messages
New RSVP objects
  LABEL_REQUEST (PATH)
  LABEL (RESV)
  EXPLICIT_ROUTE
  RECORD_ROUTE (PATH/RESV)
  SESSION_ATTRIBUTE (PATH)
LFIB populated using RSVP labels allocated by RESV messages
http://www.cisco.com/go/mpls
IP/MPLS
Head end
Tail end
TE LSP
PATH
RESV
L=16
Input Label | Out Label, Interface
17 | 16, 0
For your reference only

## Slide 46: MPLS TE FRR - Link Protection
Primary tunnel: A → B → D → E
Backup tunnel: B → C → D (preprovisioned)
Recovery = ~ 50 ms
Router D
Router C
Router A
Router B
Router E
Router Y
Router X
*Actual Time Varies—Well Below 50 ms in Lab Tests, Can Also Be Higher

## Slide 47: Use Case 1: Tactical TE Deployment
Requirement: Need to Handle Scattered Congestion Points in the Network
Solution: Deploy MPLS TE on Only Those Nodes that Face Congestion
Internet
Service Provider
Backbone
Bulk of Traffic Flow
e.g. Internet Download
Oversubscribed
Shortest Links
MPLS Traffic Engineering
Tunnel Relieves Congestion Points

## Slide 48: Use Case 2: 1-Hop Tunnel Deployment
Requirement: Need Protection Only — Minimize Packet Loss of Bandwidth in the Core
Solution: Deploy MPLS Fast Reroute for Less than 50ms Failover Time with 1-Hop Primary TE Tunnels and Backup Tunnel for Each
Service Provider
Backbone
VPN Site A
VPN Site B
Primary 1-Hop TE Tunnel
Backup Tunnel
Physical Links

## Slide 49: MPLS TE Summary
MPLS TE can be used to implement traffic engineering to enable enhanced network availability, utilization, and performance
Enhanced network availability can be implemented via MPLS TE Fast Re-Route (FRR)
  Link, node, and path protection
  Automatically route around failed links/nodes; like SONET APS
Better network bandwidth utilization can be implemented via creation of MPLS TE tunnels using explicit routes
  Route on the non-shortest path
MPLS TE can be used for capacity planning by creation of bandwidth-specific tunnels with explicit paths through the network
  Bandwidth management across links and end-to-end paths

## Slide 50
MPLS VPNs
Overviews

## Slide 51: MPLS Technology Framework
Network Infrastructure
MPLS Signaling and Forwarding
Layer-3 VPNs
Layer-2 VPNs
MPLS QoS
MPLS OAM/MIBs
MPLS TE
End-to-end Services

End-to-end data connectivity services across MPLS networks (from PE to PE)


## Slide 52: What Is a Virtual Private Network?
VPN is a set of sites or groups which are allowed to communicate with each other in a secure way
  Typically over a shared public or private network infrastructure
VPN is defined by a set of administrative policies
  Policies established by VPN customers themselves (DIY)
  Policies implemented by VPN service provider (managed/unmanaged)
Different inter-site connectivity schemes possible
  Ranging from complete to partial mesh, hub-and-spoke
Sites may be either within the same or in different organizations
  VPN can be either intranet or extranet
Site may be in more than one VPN
  VPNs may overlap
Not all sites have to be connected to the same service provider
  VPN can span multiple providers

## Slide 53: MPLS VPN Example
PE-CE link
  Connect customer network to SP network; layer-2 or layer-3
VPN
  Dedicated secure connectivity over shared infrastructure
Label switched traffic
P
P
P
P
PE
PE
PE
PE
CE
CE
CE
CE
VPN
PE-CE Link
PE-CE Link

## Slide 54: VPN Route Distribution
Full mesh of BGP sessions among all PE routers
  Multi-Protocol BGP extensions (MP-iBGP)
  Typically BGP Route Reflector (RR) used for improved scalability
Label switched traffic
P
P
P
P
PE
PE
PE
PE
CE
CE
CE
CE
Customer Route
Exchange
Customer Route
Exchange
VPN Route Exchange
BGP RR
VRF
VRF
VPN 2
VRF
VRF
VPN 1
MP-iBGP Session

## Slide 55: MPLS VPN Example

## Slide 56: MPLS VPN Benefits
SP/Carrier perspective
  Reduce costs (CAPEX)
  Leverage same network for multiple services and customers
  Migrate legacy networks onto single converged network
  Reduce costs (OPEX)
  Easier service enablement; only edge node configuration
Enterprise/end-user perspective
  Enables site/campus network segmentation
  Allows for dedicated connectivity for users, applications, etc.
  Enables easier setup of WAN connectivity
  Easier configuration of site-to-site WAN connectivity (for L3VPN); only one WAN connection needed

## Slide 57: MPLS VPN Options
MPLS VPN Models
CE connected to PE via IP-based connection (over any layer-2 type)
  Static routing
  PE-CE routing protocol; eBGP, OSPF, IS-IS
CEs peer with PE router
PE routers maintain customer-specific routing tables and exchange customer=specific routing information
Layer-3 VPN provider’s PE routers are part of customer routing
Layer-3 VPNs
Layer-2 VPNs
Point-to-Point
Layer-2 VPNs
Multi-Point
Layer-2 VPNs
CE connected to PE via p2p Layer-2 connection (FR, ATM)
CEs peer with each other (IP routing) via p2p layer-2 VPN connection
CE-CE routing; no SP involvement
CE connected to PE via Ethernet connection (VLAN)
CEs peer with each other via fully/partial mesh Layer-2 VPN connection
CE-CE routing; no SP involvement

## Slide 58
MPLS Layer-3 VPNs
Technology Overview and Applications

## Slide 59: MPLS L3 VPN Overview
Customer router (CE) has an IP peering connection with PE/edge router in MPLS network
  IP routing/forwarding across PE-CE link
MPLS VPN network responsible for distributing routing information to remote VPN sites
  MPLS VPN part of customer IP routing domain
MPLS VPNs enable full-mesh, hub-and-spoke, and hybrid connectivity among connected CE sites
MPLS VPN service enablement in MPLS networks only requires VPN configuration at edge/PE nodes
  Connectivity in core automatically established via BGP signaling

## Slide 60: MPLS Layer-3 Virtual Private Networks

## Slide 61: MPLS L3 VPN Technology Components
PE-CE link
  Can be any type of layer-2 connection (e.g., FR, Ethernet)
  CE configured to route IP traffic to/from adjacent PE
  Variety of routing options; static routes, eBGP, OSPF, IS-IS
MPLS L3VPN Control Plane
  Separation of customer routing via virtual VPN routing table
  In PE router: customer I/Fs connected to virtual routing table
  Between PE routers: customer routes exchanged via BGP
MPLS L3VPN Forwarding Plane
  Separation of customer VPN traffic via additional VPN label
  VPN label used by receiving PE to identify VPN routing table

## Slide 62: Virtual Routing and Forwarding Instance - VRF

## Slide 63: Virtual Routing and Forwarding Instance

## Slide 64: Virtual Routing and Forwarding Instance
Virtual Routing and Forwarding Instance (VRF)
Typically one VRF created for each customer VPN on PE router
VRF associated with one or more customer interfaces
VRF has its own instance of routing table (RIB) and forwarding table (CEF)
VRF has its own instance for PE-CE configured routing protocols
VRF Blue
VRF Green
CE
PE
CE
VPN 2
VPN 1
MPLS Backbone IGP

## Slide 65: VPN Route Distribution
Full mesh of BGP sessions among all PE routers
  Multi-Protocol BGP extensions (MP-iBGP)
  Typically BGP Route Reflector (RR) used for improved scalability
Label switched traffic
P
P
P
P
PE
PE
PE
PE
CE
CE
CE
CE
Customer Route
Exchange
Customer Route
Exchange
VPN Route Exchange
BGP RR
VRF
VRF
VPN 2
VRF
VRF
VPN 1
MP-iBGP Session

## Slide 66: VPN Control Plane Processing
Make customer routes unique:
Route Distinguisher (RD): 8-byte field, VRF parameters; unique value assigned by a provider to each VPN to make different VPN routes unique
VPNv4 address: RD+VPN IP prefix
Selective distribute customer routes:
Route Target (RT): 8-byte field, VRF parameter, unique value to define the import/export rules for VPNv4 routes
MP-iBGP: advertises VPNv4* prefixes + labels
Processing Steps:
CE1 redistribute IPv4 route to PE1 via eBGP.
PE1 allocates VPN label for prefix learnt from CE1 to create unique VPNv4 route
PE1 redistributes VPNv4 route into MP-iBGP, it sets itself as a next hop and relays VPN site routes to PE2
PE2 receives VPNv4 route and, via processing in local VRF (green), it redistributes original IPv4 route to CE2.
P
P
PE1
PE2
CE1
CE2
ip vrf Green
RD 1:100
route-target export 1:100
route-target import 1:100
No VPN Routes in core (P) nodes
eBGP:
16.1/16 IP Subnet
BGP advertisement:
VPN-IPv4 Addr = RD:16.1/16
BGP Next-Hop = PE1
Route Target = 100:1
Label=42
eBGP:
16.1/16 IP Subnet
VRF
VRF
VPN 1

## Slide 67: VPN Forwarding Plane Processing
Processing Steps:
CE2 forwards IPv4 packet to PE2.
PE2 imposes pre-allocated VPN label (learned via MP-IBGP) to IPv4 packet received from CE2.
PE2 imposes outer IGP label (learned via LDP) and forwards labeled packet to next-hop P-router P2.
P-routers P1 and P2 swap outer IGP label and forward label packet to PE1.
Router PE1 strips VPN label and forwards IPv4 packet to CE1.
P2
P1
PE1
PE2
CE1
CE2
ip vrf Green
RD 1:100
route-target export 1:100
route-target import 1:100
IPv4 Packet
VRF
VRF
VPN 1
IPv4 Packet
IPv4
IPv4
VPNv4 Label
IGP Label A
IPv4
VPNv4 Label
IGP Label B
IPv4
VPNv4 Label
IGP Label C
IPv4

## Slide 68: Use Case 1: Traffic Separation
Requirement: Need to ensure data separation between Aerospace, Cosmetics and Financial Services, while leveraging a shared infrastructure
Solution: Create MPLS VPN for each group
Aerospace
Cosmetics
Financial Services
Central site - HQ
Cosmetics
Financial
Services
Remote Site 1
Aerospace
Cosmetics
Remote Site 2
Aerospace
Financial
Services
Remote Site 3
VPN_Fin
VPN_Fin
VPN_Fin
VPN_Cos
VPN_Cos
VPN_Cos
VPN_Aero
VPN_Aero
VPN_Aero
MPLS Backbone
VRF instances created for each group at the edge

## Slide 69: Use Case 2: Simplify Hub Site Design
Requirement: To ease the scale and design of head-end site
Solution: Implement MPLS Layer 3 VPNs, which reduces the number of routing peers of the central site
Without MPLS
Central Site
Remote Sites
Central site has high number of routing peers – creates a complicated headend design
With MPLS
Central Site
Remote Sites
Central site has a single routing peer – enhancing head-end design
MPLS Backbone

## Slide 70: Use Case 3: Traffic Separation with L3 VPN in Airport
Requirement: To ease the scale and design of head-end site
Solution: Implement MPLS Layer 3 VPNs, which reduces the number of routing peers of the central site

## Slide 71: MPLS Layer-3 VPN Summary
Provide layer-3 connectivity among customer sites via Layer-3 VPN (and across PE-CE link)
Implemented via VRFs on edge/PE nodes providing customer route and forwarding segmentation
BGP used for control plane to exchange customer VPN (VPNv4) routes between PE routers
MPLS VPNs enable full-mesh, hub-and-spoke, and hybrid IP connectivity among connected CE sites

## Slide 72
MPLS Layer-2 VPNs
Technology Overview and Applications

## Slide 73: L2VPN Options
MPLS Layer-2 VPNs
VPLS Virtual Private LAN Service Point to Multipoint
VPWS
Virtual Private Wire Service
Point to Point
L2VPN Models
AToM
L2TPv3
IP Core
Frame Relay
ATM (AAL5 and Cell)
Ethernet
PPP and HDLC
MPLS Core
Frame Relay
ATM (AAL5 and Cell)
Ethernet
PPP and HDLC
MPLS Core
Ethernet
Any Transport over MPLS: AToM

## Slide 74: Layer-2 VPN Overview
Enables transport of any Layer-2 traffic over MPLS network
  Includes label encapsulation and translation
Ethernet
ATM
HDLC
PPP
FR
Pseudo Wire
SP Network
SP Interconnection
PE Router
PE Router
Many Subscriber Encapsulations Supportable

## Slide 75: Any Transport over MPLS Architecture
Based on IETF’s Pseudo-Wire (PW) Reference Model
PW is a connection (tunnel) between 2 PE Devices, which connects 2 PW End-Services
  PW connects 2 Attachment Circuits (ACs)
  Bi-directional (for p2p connections)
  Use of PW/VC label for encapsulation
Pseudo-Wires
Emulated Layer-2 Service
PWES
PWES
PSN Tunnel
PWES
PWES
Customer2 Site1
Customer1 Site1
Customer1 Site2
PE
PE
Customer2 Site2

## Slide 76: AToM Technology Components
PE-CE link
  Referred to as Attachment Circuit (AC)
  Can be any type of layer-2 connection (e.g., FR, Ethernet)
AToM Control Plane
  Targeted LDP (Label Distribution Protocol) Session
  Virtual Connection (VC)-label negotiation, withdrawal, error notification
AToM Forwarding Plane
  2 labels used for encapsulation
  Outer tunnel (LDP) label
  To get from ingress to egress PE using MPLS LSP
  Inner de-multiplexer (VC) label
  To identify L2 circuit (packet) encapsulated within tunnel label

## Slide 77: AToM Control Plane Processing
Processing Steps (for both P1 and P2):
CE1 and CE2 are connected to PE routers via layer-2 connections
Via CLI, a new virtual circuit cross-connect is configured, connecting customer interface to manually provided VC ID with target remote PE
New targeted LDP session between PE routers established, in case one does not already exist
PE binds VC label with customer layer-2 interface and sends label-mapping message to remote PE over LDP session
Remote PE receives LDP label binding message and matches VC ID with local configured cross-connect
P
P
PE1
PE2
CE1
CE2
Layer-2 Connection
Layer-2 Connection
3
LDP session
4
Label Mapping Messages
2
2
5
5

## Slide 78: AToM Forwarding Plane Processing
Processing Steps:
CE2 forwards layer-2 packet to PE2.
PE2 imposes VC (inner) label to layer-2 packet received from CE2 and optionally a control word as well (not shown).
PE2 imposes Tunnel outer label and forwards packet to P2.
P2 and P1 router forwards packet using outer (tunnel) label.
Router PE1 strips Tunnel label and, based on VC label, layer-2 packet is forwarded to customer interface to CE1, after VC label is removed
  In case control word is used, new layer-2 header is generated first.
P2
P1
PE1
PE2
CE1
CE2
Layer-2 Packet
Layer-2 Packet
L2
L2
VC Label
Tunnel Label A
L2
VC Label
Tunnel Label B
L2
VC Label
Tunnel Label C
L2

## Slide 79: Use Case: L2 Network Interconnect
Requirement: Need to create connectivity between remote customer sites, currently interconnected via Frame Relay WAN connectivity. Only point-to-point connectivity required.
Solution: Interconnect AToM PW between sites, enabling transparent Frame Relay WAN connectivity.
PE1
MPLS Backbone
PE2
CPE Router, FRAD
DLCI 101
DLCI 201
Directed LDP
Label Exchange for VC1 – Label 10
Neighbor LDP– Label 50
Neighbor LDP– Label 90
101
10
50
101
10
90
VC1 – Connects DLCI 101 to DLCI 201
CPE Router, FRAD

## Slide 80: Layer-2 VPN Summary
Enables transport of any Layer-2 traffic over MPLS network
Two types of L2 VPNs; AToM for point-to-point and VPLS point-to-multipoint layer-2 connectivity
Layer-2 VPN forwarding based on Pseudo Wires (PW), which use VC label for L2 packet encapsulation
  LDP used for PW signaling
AToM PWs suited for implementing transparent point-to-point connectivity between Layer-2 circuits