## Slide 1: Department of Informatics Networks and Distributed Systems (ND) group
IN3230/4230
Wireless Communications - III
Özgü Alay
ozgua@ifi.uio.no

## Slide 2: Outline
Mobile Broadband Networks
  Performance
  International Roaming
  Operations
Massive IoT
  NB-IoT
  LORAWAN
Paving the future
  5G and Beyond

## Slide 3: MONROE – Mobile Broadband Measurement Platform
Coverage in 4 European Countries (Norway, Sweden, Spain, Italy)
Under mobility (e.g., on-board of trains or buses) or in stationary scenarios (e.g., in laboratories, or hosted by volunteers in homes).
A set of 100 nodes equipped with Ethernet, WiFi and 3G/4G interfaces with commercial MBB subscriptions.

## Slide 4: Hourly and Daily Patterns

## Slide 5: LTE performance: Data rate and RTT

## Slide 6: Outline
Mobile Broadband Networks
  Performance
  International Roaming
  Operations
Massive IoT
  NB-IoT
  LORAWAN
Paving the future
  5G and Beyond

## Slide 7: Free roaming in Europe

## Slide 8: Roaming Infrastructure

## Slide 9: Roaming Models
Home Routed (HR):
  The IP address of the roaming user is provided by the home network.
  All traffic to and from the mobile user is routed through the home network, for which a GTP tunnel is set up between the SGW of the visited network and the PGW of the home network (red path in the figure).
Local BreakOut (LBO):
  When LBO is used, the IP address of the roaming user is provided by the visited network.
  The GTP tunnel is terminated at the PGW of the visited network and IP-based services can be accessed directly from there (purple path in the figure).
IPX Hub Breakout (IHBO):
  The IP address of the roaming user is provided by the IPX network. The GTP tunnel from the SGW in the visited network terminates at a PGW in the IPX network (green path in the figure).
  There may be multiple PGWs so that latency and resource usage can be reduced by selecting one geographically close to the visited network.

## Slide 10
6 countries, 16 operators, each country has two nodes
One measurement server per country
Norway: Telia, Telenor
Sweden: Telenor, Tre, Telia
Spain: Orange, Vodafone, Movistar
Germany: Vodafone, O2, T-Mobile
UK: Vodafone, EE
Italy: Vodafone, TIM, WIND
MONROE-Roaming Nodes

## Slide 11
Roaming Configuration
Home Routed (HR) Roaming was used by all 16 MNOs!
Why all traffic is sent back to home network?
  HR provides the home operators with all the accounting and billing information
  Operators want to have near real-time view of the customer traffic for accounting reasons
  More complex debugging if HR is not used, who is responsible if there is a problem?

## Slide 12: Delay penalty of home-routed roaming
Packets go back and forth
Mimics LBO
Tunnel
vs
Internet

## Slide 13: Delay penalty of home-routed roaming geographically
RTT difference between the roaming SIM and the visited SIM
South to North has the highest delays
Germany is in a good position being in central Europe

## Slide 14: Outline
Mobile Broadband Networks
  Performance
  International Roaming
  Operations
Massive IoT
  NB-IoT
  LORAWAN
Paving the future
  5G and Beyond

## Slide 15: Mobile Virtual Network Operators (MVNO)
MVNO is an entity that offers mobile network services to end-users, but does not own nor operate fully a cellular network. MVNOs lack of ownership of radio spectrum resources.
In order to operate, an MVNO needs to have agreements in place to access the network of at least one MNO.

## Slide 16: MVNO Models
A "light" MVNO is a service provider that has its own customer support, marketing, sales and distribution operations, and has the ability to set its tariffs independently from the retail prices set by the host MNO.
The “full” MVNO have a core network implementation operating essentially the same technology as a mobile network operator, only missing their own radio network. They run their own core network and rely on at least one host MNO who can offer access to the radio resources.
Mobile Network Aggregator (MNA): Some full MVNOs exploit more than one single MNO, establishing the MNA operating model. Aggregating multiple MNOs allows the MNA's customers to dynamically change the MNO they are attached to based on the different factors, such as policy, coverage, performance, etc.

## Slide 17: Outline
Mobile Broadband Networks
  International Roaming
Massive IoT
  NB-IoT
  LORAWAN
Paving the future
  5G and Beyond

## Slide 18: Growth in the number of connected devices

## Slide 20: Key Challenges for Massive IoT
Battery life – many IoT devices will be battery-powered, and often the cost of replacing batteries in the field is not viable. (Battery life time of 10 years)
Coverage and Range – deep indoor connectivity is a requirement for many applications in the utility area. Regional (or even national or global) coverage is a prerequisite for many use cases, especially within the transport area. (5 –40 km in the open field)
Quality of Service – providing a certain low bitrate reliably is important for many applications while latency is not that critical. (Typically a few hundred bit/s or less)
Deployment and device cost – clearly a key enabler for high-volume, mass-market applications, enabling many of the use cases. Moreover, in order to enable a Massive IoT market, networks need to scale efficiently. (Device cost of a few Euros)

## Slide 21: Low Power Wide Area Networks (LPWAN)

## Slide 22: What is LORAWAN?
Low Power, Wide Area (LPWA) networking protocol for IoT
Provides bi-directional communication, end-to-end security, mobility and localization services
Open source standard
Unlicensed band (EU 868)
LORA Alliance (400+ industry partner)
The Things Network (TTN)*: “a global, crowdsourced, open, free and decentralized LoRaWAN IoT platform”
*https://www.thethingsnetwork.org/

## Slide 23: LoRaWAN Architecture

## Slide 24: LoRaWAN Specification
Spectrum | Unlicenced 863-870 MHz frequency bands (in Europe) 125/250 KHz channels
Modulation and Access | LoRa modulation (Chirp Spread Spectrum (CSS)) LORAWAN MAC (Aloha)
Data rate | 250bps-50kbps
UE Max Tx Power | 14 dBm
Range | 5 km (urban), 20 km (rural)
Energy Efficiency | Adaptive Data Rate (ADR)
Notes: CSS used for Sonar and Radar

## Slide 25: Adaptive Data Rate (ADR)
Adaptive Data Rate (ADR) is a mechanism for optimizing data rates, airtime and energy consumption in the network.
Spreading Factor (SF): is the duration of the chirp. LoRa operates with spread factors from 7 to 12. SF7 is the shortest time on air, SF12 will be the longest.
ADR triggers:
  SF increase (device-side): Improves message delivery in harsh radio conditions
  SF decrease (network-side): Improves data rate and power consumption

## Slide 26: LORAWAN Network Coverage

## Slide 27: What is NB-IoT?
LPWAN radio technology standard developed by 3GPP to meet IoT application requirements
Builds on the LTE ecosystem, and can be deployed as a simple addition of new software to existing LTE infrastructure
  leading to fast development, scalibility, and global roaming
Includes state-of-the-art LTE security
  Identity management
  Authentication and authorization (embedded SIM)
  End to end encription of device data and signalling
Future feature growth for MBB and NB-IoT use cases

## Slide 28: NB-IoT Specification
Spectrum Deployment | 
Modulation and Access | Modulation: BPSK/QPSK MAC: DL: OFDMA, UL: SC-FDMA
Peak data rate | DL: 250 kbps UL: 20 kbps
UE Max Tx Power | 23 dBm
Coverage enhancements | Power Spectral Density boost Repetitions
Range | 1 km (urban), 10 km (rural)
Energy Efficiency | Power Saving Mode (PSM) extended Discontinuous Reception (eDRx)
Rel-13

## Slide 29: NB-IoT Coverage
Coverage Enhancement (CE) Techniques (w.r.t. LTE)
  Power Spectral Density boost: Tx power focused on smaller bands
  Repetitions: messages can be repeated up to 128 times
CE Level (CL) | # Repetitions
0 | [0-2]
1 | [4-16]
2 | [32-128]
CL0 = LTE coverage

## Slide 30: NB-IoT Power Savings
Power Saving Mode (PSM) is a power-off mode, in which the device nevertheless remains registered on the network
TAU: Tracking Area Update
RRC: Radio Resource Control
DRX: Discontinuous Reception

## Slide 31: NB-IoT Power Savings
extended Discontinuous Reception (eDRx) mode allows you to significantly increase the period of time when the receiving path of the device is turned off.

## Slide 32: NB-IoT Deployment
*Source: https://www.kotonlink.com/NewsDetail/2434022.html

## Slide 33: LORAWAN vs NB-IoT
Range and Penetration
Battery
Cost (deployment, spectrum, device)

## Slide 34: Overall LORAWAN vs NB-IoT

## Slide 35: Outline
Mobile Broadband Networks
  International Roaming
Massive IoT
  NB-IoT
  LORAWAN
Paving the future
  5G and Beyond

## Slide 36: What is 5G?
5G is the 5th generation of mobile networks
Analogue
Digital
SMS
Multimedia
Video Calling
Mobile internet
Mobile Broadband
Enhanced Video
Mobile Connected World
Enhanced Mobile Broadband
Low latency applications
Internet of Things
Augmented and Virtual Reality (AR & VR)

## Slide 37: Different requirements for 5G applications and services

## Slide 38
Multi domain performance
  Energy Performance
  Critical machine type of communications
  Global standard
5G Mobile Network Expected Performance

## Slide 39: Back in the day…

## Slide 40: Network Flexibility: Virtualization

## Slide 43: Network Slicing for diverse requirements

## Slide 44: Capacity Enhancements
Small cells,
Relays, mobile
Relays and
Drones
new spectrum @ higher frequencies (above 6 GHz)
Massive MIMO
Spectrum sharing

## Slide 45: 5G Bands and its impact on Cell size

## Slide 46: Visible Light Communications
https://attract-eu.com/showroom/project/vladimir/

## Slide 47: Millimeter Wave Massive MIMO
B. Yang, Z. Yu, Y. Dong, J. Zhou and W. Hong, "Compact Tapered Slot Antenna Array for 5G Millimeter-Wave Massive MIMO Systems," in IEEE Transactions on Antennas and Propagation, vol. 65, no. 12, pp. 6721–6727, Dec. 2017.

## Slide 48: Multi-User MIMO Beamforming

## Slide 49: Spectrum Sharing: Multi-connectivity

## Slide 50: Ultra high reliability and Low Latency

## Slide 51
From 4G to 5G Transition
4G
5G
EPC
5G-CN
Today – 4G Access
Device attaches to LTE/4G radio and Evolved Packet Core (EPC)
Early 5G – Non-Standalone
Device attaches to 5G-NR, which routes either via 4G Base Station to EPC, or direct to EPC
4G acts as control plane
5G Standalone
Device attaches to 5G-NR and 5G Core Network.