## Slide 1: Department of Informatics Networks and Distributed Systems (ND) group
IN 3230 / IN 4230
Congestion control
Michael Welzl

## Slide 2: A simple router model
Queue 1
Queue 2
In 1
In 2
In 3
Switching
Fabric
Out 1
Out 2
Switch(ing) fabric forwards a packet (dest. addr.) if no special treatment necessary: “fast path“ (hardware)
Queues grow when traffic bursts arrive
  low delay = small queues, low jitter = no queue fluctuations
Packets are dropped when queues overflow (“DropTail queueing“)
  low loss ratio = small queues

## Slide 3
Utilization: 2/3
Upgrade to 1 Mbit/s!

## Slide 4: Global congestion collapse
Craig Partridge, Research Director for the Internet Research Department at BBN Technologies:
Bits of the network would fade in and out, but usually only for TCP. You could ping. You could get a UDP packet through. Telnet and FTP would fail after a while. And it depended on where you were going (some hosts were just fine, others flaky) and time of day (I did a lot of work on weekends in the late 1980s and the network was wonderfully free then).
Around 1pm was bad (I was on the East Coast of the US and you could tell when those pesky folks on the West Coast decided to start work...).
Another experience was that things broke in unexpected ways - we spent a lot of time making sure applications were bullet-proof against failures. (..)
Finally, I remember being startled when Van Jacobson first described how truly awful network performance was in parts of the Berkeley campus. It was far worse than I was generally seeing. In some sense, I felt we were lucky that the really bad stuff hit just where Van was there to see it.

## Slide 5: Internet congestion control: history
around 1986: first congestion collapse
1988: "Congestion Avoidance and Control" (Jacobson) Combined congestion/flow control for TCP (also: variation change to RTO calculation algorithm)
Idea: packet loss = congestion, so throttle the rate; increase otherwise
Goal: stability - in equilibrum, no packet is sent into the network until an old packet leaves
  ack clocking, “conservation of packets“ principle
  made possible through window based stop+go - behaviour
Superposition of stable systems = stable  network based on TCP with congestion control = stable

## Slide 6: A control loop to stabilize (bring it to equilibrium and keep it there)
Diagrams taken from: V. Jacobson, K. Nichols K. Poduri, "RED in a Different Light", unpublished
  "...because someone on the program committee was offended by the diagram explaining its behavior." https://gettys.wordpress.com/2010/12/17/red-in-a-different-light/

## Slide 7: Reminder: TCP's sliding window
Receiver “grants“ credit (receiver window, rwnd)
  sender restricts sent data with window
Receiver buffer not specified
  i.e. receiver may buffer reordered segments (i.e. with gaps)
Sender buffer

## Slide 8: TCP Congestion Control: Tahoe
Distinguish:
  flow control: protect receiver against overload
  (receiver "grants" a certain amount of data ("receiver window" (rwnd)) )
  congestion control: protect network against overload
  ("congestion window" (cwnd) limits the rate: min(cwnd,rwnd) used! )
Flow/Congestion Control combined in TCP. Two basic algorithms:
  Slow Start: for each ack received, increase cwnd by 1 packet (exponential growth) until cwnd >= ssthresh
  Congestion Avoidance: each RTT, increase cwnd by at most 1 packet (linear growth - "additive increase“)

## Slide 9: TCP Congestion Control: Tahoe /2
If a packet or ack is lost (timeout), set cwnd = 1, ssthresh = cwnd / 2 (“multiplicative decrease") - exponential backoff
  Actually, “Flightsize/2“ instead of cwnd/2 because cwnd might not always be fully used
Timeout based on RTT; good estimation is crucial!
Later additions: TCP Reno, 1990 Fast retransmit / fast recovery Sender detects loss via duplicate acks; no need to slow start to ssthresh
Slow Start
Congestion Avoidance

## Slide 10: Background: AIMD

## Slide 11: AIMD is an easy way out, but...
Michael Welzl, Max Mühlhäuser: "CAVT - A Congestion Avoidance Visualization Tool", ACM SIGCOMM CCR 3(3), July 2003, pp. 95-101. http://welzl.at/research/tools/cavt/index.html

## Slide 12: Actual TCP (simulation)

## Slide 13: TCP Reno: building a queue
Chart: 
 | 1 | 2 | 4 | 8 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Capacity limit
Queue limit
Slow Start:
double cwnd every RTT
Congestion Avoidance:
cwnd++ every RTT
Upon loss: cwnd*=beta (beta=0.5)
Queue begins to grow (RTT grows)
Packet loss
Time
cwnd
ssthresh
(initially normally larger)

## Slide 14: How large should a queue be?
Old rule-of-thumb: “Bandwidth * delay product” (BDP) (bw = bottleneck link capacity; delay = RTT)
  Can be unreasonably large, causing unnecessary delay (severe e.g. for VoIP and games)
  For core routers, bw * RTT / sqrt(no. flows) was found to be enough
  No new rule exists for access equipment (routers, modems, ..)
Often, access link = bottleneck; access equipment’s queue = the one that grows
  Some equipment vendors sell “large buffer = feature”
  Effect: extreme delay, now called “buffer bloat”
Chart: 
 | 1 | 2 | 4 | 8 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Link capacity
Buffer

## Slide 15: Using delay as a signal
Delay grows before loss, so can react earlier, limit delay
  Noisy signal, but fine-grain and easily available
  Oldest known approach: TCP Vegas; works well but loses against Reno
LEDBAT: turning this bug into a feature
  For low-priority traffic that should not get in the way
  Encapsulation not (yet?) defined; implemented over UDP in BitTorrent

## Slide 16: More problems with delay as a signal
RTT easier to measure than One-Way Delay (OWD), but can be noisy (don’t want to react to queue on return path)
  Note: absolute OWD doesn’t usually matter (clock sync not needed), need changes of OWD
Size of buffer determines measurement granularity
Base delay (long-term min. delay) can create problems
  One flow’s congestion is the next flow’s base delay
  Need to occasionally refresh, but don’t measure yourself!
Ping delay across a 500 kbit/50ms Ethernet link, with libutp’s “utp test” program running

## Slide 17: Active Queue Management
1993: Random Early Detection ("Discard", "Drop") (RED) (since TCP backs off as packets are dropped, drop packets earlier to avoid queue overflows)
  Adds randomization to avoid traffic phase effects
  "Punishes" unresponsive flows, improving fairness
Qavg = (1 - Wq) x Qavg + Qinst x Wq (Qavg = average occupancy, Qinst = instantaneous occupancy, Wq = weight - hard to tune, determines how aggressive RED behaves)

## Slide 18: Phase effects of a FIFO queue
Constant bit-rate sender
TCP sender

## Slide 19: RED
Based on exponentially weighted moving average (EWMA) of instantaneous queue occupancy = low pass filter
  recalculated every time a packet arrives
Several variants exist (also entirely different algorithms): drop from front, drop based on instantaneous queue occupancy, drop arbitrary packets, drop based on priorities...
Drop!
Drop!
Q: does RED interoperate well with LEDBAT?

## Slide 20: Explicit Congestion Notification (ECN)
1999: Explicit Congestion Notification (ECN) Instead of dropping, set a bit (which the receiver tells the sender about)
End systems should act as if packet was dropped  real communication between hosts and routers!
  But cannot totally replace loss reaction!
ATM and Frame Relay: not only ECN but also BECN
  Internet BECN: proposed and discussed long ago (ICMP SQ), now obsolete... Perhaps not done well?
Up to date, ECN is still hardly deployed

## Slide 21: Delay-based congestion control
E.g., for multimedia traffic: try to co-exist with TCP, yet avoid building a queue if possible
  E.g., when TCP is absent
IETF RMCAT: congestion control for WebRTC, using RTP/RTCP
  Google Congestion Control (GCC) (used in Chrome), Cisco’s NADA, Ericsson’s SCREAM
CAIA Delay-Gradient (CDG)
  Sender-side TCP CC. mechanism; available in Linux
  Operates on RTT changes (gradient); less prone to errors than absolute delay (e.g. need no base delay)
  Tries to compete with normal TCP (e.g. using shadow window), but tends to be LEDBAT’ish

## Slide 22: TCP co-existence
Used to be called "being TCP-friendly"
  i.e., do not send more than TCP would under comparable circumstances
  Can be achieved by emulating the behaviour of TCP (or the desired parts of it)
E.g., simplified TCP: AIMD (additive incr.  , multiplicative decr. )
  0 <  , 0 <  < 1 -> stable and fair congestion control
   = 4 x (1 - ^2) / 3 -> TCP-friendly congestion control
   = 1,  = 1/2 -> TCP

## Slide 23: GAIMD congestion control
Relationship between  and  for TCP-friendliness:
TCP
smoother
more aggressive + responsive

## Slide 24: TCP's steady-state equation
Average transmission rate T (bytes/sec):
s: packet size
R: rtt
tRTO: TCP retransmit timeout
p: steady-state loss event rate (the difficult part!)
well known old mechanism TFRC (TCP-friendly rate control) used this as an upper bound, but with a smoother sending rate than TCP
  Less delay fluctuation, good for multimedia
GCC also uses this equation

## Slide 25: Congestion state and multiple flows
TCP Control Block (TCB): data such as RTO, cwnd, ..
  Related to path, yet separately stored per TCP connection
  Compare: layering problem of PMTU storage
Multiple TCP connections are not TCP-friendly to one
  Neither are short flows which start and stop in Slow Start
  Web browsers open hundreds!
Yet, sometimes fewer competing flows can be better
  E.g., new short flow can use already-large cwnd
  HTTP/2 replaced "sharding", now HTTP/3 ( = HTTP / QUIC / UDP )
TCB interdependence: share TCB info when flows start
  Temporal sharing: learn from previous connection
  Ensemble sharing: learn from existing connections

## Slide 26: Combining congestion control: an example

## Slide 27: MPTCP: being below-TCP-friendly
Many modern hosts are multihomed
  Smartphones (WiFi + 3G), data centers
  Why not use both connections at once?
Cannot know where bottleneck is
  If it is shared by the two connections, they should appear (be as aggressive) as only one connection
  MPTCP changes congestion avoidance “increase” parameter to “divide” aggression accordingly
    but instead of being “½ TCP”, tries to send as much as possible over least congested path
    Least congested = largest window achieved; hence, increase in proportion to window

## Slide 28: Fairness principles
TCP-friendliness is a fairness definition
  Based on technical behavior of TCP... is this meaningful?
E.g., ATM ABR: Max-Min-fairness
  “A (..) allocation of rates is max-min fair iff an increase of any rate (..) must be at the cost of a decrease of some already smaller rate.“
  One resource: mathematical definition satisfies "general" understanding of fairness - resource is divided equally among competitors
  Usually requires knowledge of flows in routers (switches) - scalability problem!

## Slide 29: Proportional Fairness
Proportional fairness:
  “An allocation of rates x is proportionally fair iff, for any other (..) allocation y, we have: “ (roughly approximated by AIMD!)
S1
D1
S2
S3
D2
D3
F. Kelly: Network should solve a global optimization problem (maximize log utility function)
Max-Min-fairness suboptimal: S1 = S2 = S3 = c/2
All link
capacities: c
Proportionally fair allocation: S1 = c/3, S2 = S3 = 2c/3

## Slide 30: Utility functions
Consider: multimedia applications
  not necessarily logarithmic (e.g. VoIP)
No constraints, like file transfer
"adaptive"
Hard real-time constraints
Soft real-time constraints

## Slide 31: TCP with High-Speed links
TCP over “long fat pipes“: large bandwidth*delay product
  long time to reach equilibrium, MD = problematic
  from RFC 3649 (HighSpeed RFC, Experimental): For example, for a Standard TCP connection with 1500-byte packets and a 100 ms round-trip time, achieving a steady-state throughput of 10 Gbps would require an average congestion window of 83,333 segments, and a packet drop rate of at most one congestion event every 5,000,000,000 packets (or equivalently, at most one congestion event every 1 2/3 hours). This is widely acknowledged as an unrealistic constraint.
Area: 3ct
Area: 6ct
Theoretically, utilization independent of capacity
But: longer convergence time

## Slide 32: Slow convergence animation
Chart: 
 | 1 | 2 | 4 | 8 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Chart: 
 | 1 | 2 | 4 | 8 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Slow link
Fast link

## Slide 33: Some proposed solutions
Scalable TCP: increase/decrease functions changed
  cwnd := cwnd + 0.01 for each ack received while not in loss recovery
  cwnd := 0.875 * cwnd on each loss event (probing times proportional to rtt but not to the capacity)
Source: http://www.deneholme.net/tom/scalable/
Standard TCP
Scalabe TCP

## Slide 34: Some proposed solutions /2
Rate Standard TCP recovery time Scalable TCP recovery time
1Mbps 1.7s 2.7s
10Mbps 17s 2.7s
100Mbps 2mins 2.7s
1Gbps 28mins 2.7s
10Gbps 4hrs 43mins 2.7s
HighSpeed TCP (RFC 3649, includes Scalable TCP discussion):
  response function includes a(cwnd) and b(cwnd), also depend on loss ratio
  less drastic in high bandwidth environments with little loss only
  Significant step!
  Previously, either TCP-friendly or better-than-TCP; no combinations!
"TCP-friendly" is now a term of the past
  "There is no point in being friendly to TCP, it will not return the favour". [Andrew McGregor]

## Slide 35: Proposed solutions /3
BIC, CUBIC
  BIC (Binary InCrease TCP) uses binary search to find the ideal window size:
    when loss occurs, current window = max, new window = min
    check midpoint;
    if no loss  new min, increase; else new window = new max
  CUBIC = BIC++ using cubic function; growth does not depend on RTT
After major press release (Slashdot: “BIC-TCP 6000 times quicker than DSL“), BIC became the default TCP CC. in Linux in mid-2004!
  Major change to the CC. landscape
  Soon after, replaced with CUBIC

## Slide 37: TCP over Satellite, and PEPs
Satellites combine several problems
  Long delay + high capacity (= large BDP)
  Wireless (but usually not noisy (for TCP) because of link layer FEC)
  Can be asymmetric (e.g. direct satellite downlink, 56k modem uplink)
Thus, TCP over satellite was a major research topic for a while
  Transparent improvements ("Performance Enhancing Proxies") common
  Figure: split connection approach: 2a / 2b instead of control loop 1
  Many possibilities - e.g. Snoop TCP: monitor + buffer; in case of loss, suppress DupACKs and retransmit from local buffer

## Slide 38: Pacing
"Micro burstiness" can lead to delay + packet drops
Generally, packet gap dictated by bottleneck link; but incoming data can be bursty (e.g. from slow start)
  Put the "pacing device" (PEP) close to bottleneck
Pacing is hard at high speeds (clock granularity)
  But getting more feasible; increasingly popular!
Various solutions
  e.g. "gap frames" that are later dropped by a link layer device; burst limits, e.g. Linux

## Slide 39: Congestion control reality check (note: no guarantee for correctness of this slide!)
Linux: Cubic (default, many others available)
  Cubic comes with a Slow Start early exit based on delay heuristics, called HyStart
Apple: standard (MP)TCP (or now also Cubic?)
  LEDBAT for OS updates
  Hosts sometimes try to negotiate ECN (someone needs to make a start!)
Windows: Cubic default for Windows 10, Windows Server 2019
  But with their own new HyStart++
  Old delay+loss variant Compound-TCP (CTCP) was default TCP CC. in Windows Server 2008 beta for testing purposes
  When it sees tiny RTTs, switches to Datacenter TCP (DCTCP), a very aggressive ECN based variant
  LEDBAT++ for OS updates
Applications:
  BitTorrent: LEDBAT
  WebRTC: RMCAT congestion controls
  YouTube: Google experiments with their own BBR cc. (now version 3) (Netflix uses Reno, but experiments with a BBR variant, in-house)
  Facebook: Meta experiments with delay-based COPA cc. for video
Messy... but the Internet still works 

## Slide 40: Thank you!
A humble reference suggestion: