## Slide 1: Interconnection Networks High Performance Computing / Computer Architecture
Tor Skeie
University of Oslo, Department of informatics
With major presentation contribution from: José Flich, Universidad Politécnica de Valencia
Timothy Mark Pinkston, University of Southern California

## Slide 2: Introduction
Reasons to devote attention to interconnection networks – “interconnects”
  They provide connectivity within a single computer system at many levels, and between aggregated computers to offer High Performance Computing (HPC)
  Trends: The convergence going on between AI and HPC requires smarter networks and ultra-high connectivity – application trends: Big Data, AI/ML, Internet of Things, Life Science …
    increased computing power and storage capacity
    switched networks are replacing buses
  Computer architects must understand interconnect problems and solutions in order to more effectively design and evaluate systems
Goal
  To provide an overview of designing interconnection networks and potential solutions

## Slide 3: Outline
  Introduction
  Interconnecting Two Devices
  Interconnecting Many Devices
  Network Topology
  Network Routing
  Concluding Remarks and References

## Slide 4: Introduction
Interconnection Network Domains
Interconnection networks can be grouped into two major networking domains, depending on the number and proximity of devices to be interconnected: OCNs and SANs
  On-chip networks (OCNs), a.k.a., network-on-chip (NoC)
    Interconnect microarchitecture functional units, register files, caches, compute tiles, processor GPU and CPU cores
    Chip or multichip modules
    Tens (in future, possibly 100s) of devices interconnected
    Maximum interconnect distance on the order of centimetres
    Examples (custom designed)
      Element Interconnect Bus (Cell Broadband Engine processor chip) 2,400 Gbps (3.2 Ghz processor clock), 12 elements on the chip

## Slide 5: Introduction
System/storage area networks (SANs), but also called off-chip networks
  Multiprocessor and multicomputer systems
    Is about aggregating computing power in a way that can deliver extreme computing (HPC)
    Interprocessor and processor-memory interconnections
  Server and data center environments
    Storage and I/O components
  Hundreds to thousands of devices interconnected
    Frontier - HPE supercomputer at Oak Ridge National Laboratory- the world´s most powerful computer right now (8,776 CPUs and 36 992 GPUs, 8 699 904 cores in total). Speed: 1.679 exaFlops. Power: 23 MW
  Maximum interconnect distance typically on the order of tens of meters, but some with as high as a few hundred meters
    InfiniBand: 120 Gbps over a distance of 300 m
  Examples (standards and proprietary)
    InfiniBand, Slingshot, CXL, OmniPath, BXI, Data Centre Ethernet, Ultra Ethernet is also emerging
Interconnection Network Domains

## Slide 6: Introduction
LANs
Distance (meters)
5 x 10-3
5 x 100
5 x 103
5 x 106
Number of devices interconnected
1
10
100
1,000
10,000
>100,000
OCNs
SANs
WANs
Interconnection Network Domains

## Slide 7: Outline
  Introduction
  Interconnecting Two Devices (Now)
    Network Interface Card Functions
    Basic Network Structure and Functions
    Characterizing Performance: Latency & Effective Bandwidth
  Interconnecting Many Devices
  Network Topology
  Network Routing
  Concluding Remarks and References

## Slide 8: Interconnecting Two Devices
An Ideal Network
  Two end node devices (A and B)
  Device A (or B) may read an address in device B (or A)
  Interconnection network behaves as dedicated links between A, B
    Unidirectional wires each way dedicated to each device
  Receiving buffers used for staging the transfers at the end nodes
  Communication protocol: request, reply
    basic functions at end nodes to commence and complete communication
int. network
Device A
Device B

## Slide 9: Interconnecting Two Devices
Network Interface Functions
  A message is the unit of information: header, payload, trailer
  Interfacing to the network (hardware)
    Communication device itself (OCNs and some SANs)
    Additional network interface card or NIC (SANs, LANs, WANs)
      Embedded processor(s), DMA engine(s), RAM memory
Memory
NIC
DMA
DMA
NIC
processor
internal interconnect
FIFO
Network
interface
to/from network
host interface
to/from host
header
Dest
Information
message payload
checksum
trailer
Type

## Slide 10: Interconnecting Two Devices
Communication Protocol
  Typical steps followed by the sender:
    System call by application
      Copies the data into OS and/or network interface memory
      Packetizes the message (if needed)
      Prepares headers and trailers of packets
    Checksum is computed and added to header/trailer
    Timer is started and the network interface sends the packets
proc/mem bus
IO bus or proc/mem bus
processor
memory
user
space
system
space
register
file
ni
FIFO
Interconnection
network
ni
FIFO
memory
user
space
system
space
processor
register
file
packet
user writes
data in
memory
system call
sends
1 copy
pipelined
transfer
e.g., DMA
IO bus or proc/mem bus
proc/mem bus

## Slide 11: Interconnecting Two Devices
Communication Protocol
  Typical steps followed by the receiver:
    NI allocates received packets into its memory or OS memory
    Checksum is computed and compared for each packet
      If checksum matches, NI sends back an ACK packet
    Once all packets are correctly received
      The message is reassembled and copied to user's address space
      The corresponding application is signalled (via polling or interrupt)
proc/mem bus
IO bus or proc/mem bus
processor
memory
user
space
system
space
register
file
ni
FIFO
Interconnection
network
ni
FIFO
memory
user
space
system
space
processor
register
file
packet
data
ready
interrupt
2 copy
pipelined
reception
e.g., DMA
IO bus or proc/mem bus
proc/mem bus

## Slide 12: Interconnecting Two Devices
Communication Protocol
  OS-bypassing (zero-copy or user-level protocols)
    Direct allocation for DMA transfer to/from memory/NI buffers
    Application directly reads/writes from/to these locations
    Memory-to-memory copies are avoided
    Protection is guaranteed by OS
proc/mem bus
IO bus or proc/mem bus
processor
memory
user
space
system
space
register
file
ni
FIFO
Interconnection
network
ni
FIFO
memory
system
space
processor
register
file
packet
interrupt:
data ready
Pipelined
peception
e.g., DMA
IO bus or proc/mem bus
proc/mem bus
user copies
data into pinned
user space
system call send.
pipelined transfer
e.g., DMA
user
space

## Slide 13: Interconnecting Two Devices
Communication Protocol
  OS-bypassing (zero-copy or user-level protocols)
    Direct allocation for DMA transfer to/from memory/NI buffers
    Application directly reads/writes from/to these locations
    Memory-to-memory copies are avoided
    Protection is guaranteed by OS
  Is it possible to take out register to memory/buffer copy as well?
proc/mem bus
processor
register
file
ni
FIFO
Interconnection
network
ni
FIFO
packet
processor
register
file
proc/mem bus
memory
system
space
IO bus or proc/mem bus
user
space
IO bus or proc/mem bus
memory
user
space
system
space

## Slide 14: Interconnecting Two Devices
Communication Protocol
  OS-bypassing (zero-copy or user-level protocols)
    Direct allocation of system or network interface memory/buffers
    Application directly reads/writes from/to these locations
    Memory-to-memory copies are avoided
    Protection is guaranteed by OS
  Is it possible to take out register to memory/buffer copy as well?
    NI buffer is associated with (or replaced by) register mapping
proc/mem bus
processor
register
file
ni
FIFO
Interconnection
network
ni
FIFO
packet
processor
register
file
proc/mem bus
Pipelined transfer

## Slide 15: Interconnecting Two Devices
Basic Network Structure and Functions
  Reliable delivery of packets: lossy versus lossless networks
    Must prevent the sender from sending packets at a faster rate than can be received and processed by the receiver
    Lossy networks
      Packets are dropped (discarded) at receiver when buffers fill up
      Sender is notified to retransmit packets (via time-out or NACK)
    Lossless networks (flow controlled)
      Before buffers fill up, sender is notified to stop packet injection
        Xon/Xoff (Stop & Go) flow control
        Credit-based flow control (token or batched modes)
    Implications of network type (lossless vs. lossy)
      Constrains the solutions for packet routing, congestion, & deadlock
      Affects network performance
      The network domain dictates which is one used
        OCN, SAN: typically lossless; LAN, WAN: typically lossy

## Slide 16: Interconnecting two devices

## Slide 17: Interconnecting Two Devices
Basic Network Structure and Functions
  Xon/Xoff flow control
receiver
sender
Xon
Xoff
a packet is injected if control bit is in Xon
Control bit
Xon
Xoff
pipelined transfer

## Slide 18: Interconnecting Two Devices
Basic Network Structure and Functions
  Xon/Xoff flow control
receiver
sender
Xon
Xoff
When Xoff threshold is reached, an Xoff notification is sent
Control bit
Xoff
Xon
When in Xoff,
sender cannot
inject packets
X
Queue is
not serviced
pipelined transfer

## Slide 19: Interconnecting Two Devices
Basic Network Structure and Functions
  Xon/Xoff flow control
receiver
sender
Xon
Xoff
When Xon threshold is reached, an Xon notification is sent
Control bit
Xon
Xoff
X
Queue is
not serviced
pipelined transfer

## Slide 20: Interconnecting Two Devices
Basic Network Structure and Functions
  Credit-based flow control
receiver
sender
Sender sends packets whenever credit counter
is not zero
10
Credit counter
9
8
7
6
5
4
3
2
1
0
X
Queue is
not serviced
pipelined transfer

## Slide 21: Interconnecting Two Devices
Basic Network Structure and Functions
  Credit-based flow control
receiver
sender
10
Credit counter
9
8
7
6
5
4
3
2
1
0
+5
5
4
3
2
X
Queue is
not serviced
Receiver sends credits after they become available
Sender resumes
injection
pipelined transfer

## Slide 22: Interconnecting Two Devices
Basic Network Structure and Functions
  Comparison of Xon/Xoff vs credit-based flow control
Stop & Go
Time
Credit
based
Time
Go
Stop
Go
Stop
Go
Stop
Sender
stops
transmission
Last packet
reaches receiver
buffer
Stop
Go
Packets in
buffer get
processed
Go signal
returned to
sender
Sender
resumes
transmission
First packet
reaches
buffer
# credits
returned
to sender
Sender
uses
last credit
Last packet
reaches receiver
buffer
Packets get
processed and
credits returned
Sender
transmits
packets
First packet
reaches
buffer
Flow control latency
observed by
receiver buffer
Stop signal
returned by
receiver
 Poor flow control can reduce link efficiency

## Slide 23: Interconnecting Two Devices
Basic Network Structure and Functions
  Example: impact of different link lengths
    Calculate the minimum amount of credits and buffer space for interconnect distances of 1 cm, 1 m, 100 m, and 10 km
    Assume a dedicated-link network with
      8 Gbps (raw) data bandwidth per link (each direction)
      Credit-based flow control
    Device A continuously sends 100-byte packets (header included)
    Consider only the link propagation delay (no other delays or overheads)
8 Gbps raw data bandwidth
int. network
Device A
Device B
Cr

## Slide 24: Interconnecting Two Devices
Basic Network Structure and Functions
  Example: comparison of flow control techniques
Packet propagation delay + Credit propagation delay ≤
Packet size
Bandwidth
х Credit count
distance
2/3 x 300,000 km/sec
(
)
х 2 ≤
100 bytes
8 Gbits/sec
х Credit count
1 cm → 1 credit
1 m → 1 credit
100 m → 10 credits
10 km → 1,000 credits
8 Gbps raw data bandwidth
int. network
Device A
Device B
Cr

## Slide 25: Outline
  Introduction
  Interconnecting Two Devices
  Interconnecting Many Devices (Now)
    Additional Network Structure and Functions
    Switched-based Networks
    Comparison of Shared-media versus Switched-based Networks
    Characterizing Performance: Latency & Effective Bandwidth
  Network Topology
  Network Routing
  Concluding Remarks and References

## Slide 26: Interconnecting Many Devices
Additional Network Structure and Functions
  Network topology – being a regular structure
    What paths are possible for packets?
    Networks usually share paths among different pairs of devices
  Routing
    Which of the possible paths are allowable (valid) for packets?
    Provides the set of operations needed to compute a valid path
    Executed at source, or at each intermediate node, but the routing tables is programmed by centralized controller, aka SDN (Software Defined Networking)
  Arbitration
    When are paths available for packets? (along with flow control)
    Resolves packets requesting the same resources at the same time
    For every arbitration, there is a winner and possibly many losers
      Losers are buffered (lossless) or dropped on overflow (lossy)
  Switching
    How are paths allocated to packets?
    The winning packet (from arbitration) proceeds towards destination
    Paths can be established one fragment at a time or in their entirety
    Complexity and applied order depends on the category of the topology: shared-media or switched media

## Slide 27: Interconnecting Many Devices
Switched-based Networks
  Disjoint portions of the media are shared via switching
  Switch fabric components
    Passive point-to-point links
    Active switches
      Dynamically establish communication between sets of source-destination pairs
  Aggregate bandwidth can be many times higher than that of shared-media networks
Node
Node
Node
Node
Switch
Fabric

## Slide 28: Interconnecting Many Devices
Comparison of Shared-media versus Switched-based Networks
  Shared-media networks
    Low cost
    Aggregate network bandwidth does not scale with # of devices
    Global arbitration scheme required (a possible bottleneck)
    Time of flight increases with the number of end nodes
  Switched-based networks
    Aggregate network bandwidth scales with number of devices
    Concurrent communication
      Potentially much higher network effective bandwidth
    Beware: inefficient designs are possible
      Superlinear network cost but sublinear network effective bandwidth

## Slide 29: Interconnecting Many Devices
Characterizing Performance: Latency & Effective Bandwidth
Packet size
Bandwidth
Latency = Sending overhead + (TTotalProp + TR + TA + TS) + + Receiving overhead
lower bound (contention delay not included)
TR = routing delay
TA = arbitration delay
TS = switching delay
TTotalProp = propagation delay
σ = average reception factor (contention at reception links due to application behavior)
Effective bandwidth = min (BWNetworkInjection, BWNetwork, σ × BWNetworkReception)
= min (N × BWLinkInjection, BWNetwork, σ × N × BWLinkReception)
upper bound (contention effects not fully included)

## Slide 30: Interconnecting Many Devices
Characterizing Performance: Latency & Effective Bandwidth
int. network
Device A
Device B
Injection
bandwidth
Network
injection
Reception
bandwidth
Network
reception
Aggregate
bandwidth
σ = 1
Dedicated-link network

## Slide 31: Interconnecting Many Devices
Characterizing Performance: Latency & Effective Bandwidth
int. network
Device A
Device B
Injection
bandwidth
(N times)
Network
injection
Reception
bandwidth
(N times)
Network
reception
Aggregate
bandwidth
BWLink = 1
Dedicated-link network
Node
Node
Node
BWNetwork = (BWNetworkInjection)/N
X
Shared-media network

## Slide 32: Interconnecting Many Devices
Characterizing Performance: Latency & Effective Bandwidth
int. network
Device A
Device B
Node
Node
Node
Injection
bandwidth (N times)
Network
injection
Reception
bandwidth (N times)
Network
reception
Aggregate
bandwidth (≥ N times)
Network
bandwidth
Node
Node
Node
Node
Switch
Fabric
σ < 1
X
Dedicated-link network
Shared-media network
Switched-based network
X
σ
Traffic with many-to-one communication

## Slide 33: Interconnecting Many Devices
Average load rate
Latency
Tsend
Treceive
Ttransmission
Tpropagation
Tsending
Treceiving
Ttransmission
Tpropagation
TS
TA
TR
Tcontention
Latency for just two devices
Average load rate
Effective bandwidth
Network
congestion
Characterizing Performance: Latency & Effective Bandwidth
  Characteristic performance plots: latency vs. average load rate; throughput (effective bandwidth) vs. average load rate
Peak throughput
Peak throughput

## Slide 34: Interconnecting Many Devices
Characterizing Performance: Latency & Effective Bandwidth
  Example: plot the total packet latency and effective bandwidth
    Assume N scales from 4 to 1024 end nodes and the following:
    Shared media (one link) and switched-based (N links)
    All network links have data bandwidth of 8 Gbps
    Unicast transmission of packets of size 100 bytes
    Overheads
      sending: x + 0.05 ns/byte; receiving: 4/3(x) + 0.05 ns/byte
      x is 0 for OCNs and 0.3 µs for SANs
      Distances: 0.5 cm for OCNs and 5 m SANs
    Routing, Arbitration, and Switching
      Shared-media: TR = 2.5 ns, TA = 2.5(N) ns, TS = 2.5 ns
      Switched-based: TR = TA = TS = 2.5 (log2N) ns
    σ = N-1 (shared), σ = (log2N)-1/4 (switched)

## Slide 35: Interconnecting Many Devices
Characterizing Performance: Latency & Effective Bandwidth
For OCNs, TR, TA, and
TS combine to dominate
time of flight delay and
are >> than other
latency components for
all network sizes.
For SANs, TR, TA, and
TS combine to dominate
time of flight delay, but
are less than other
latency components for
switched-based (but,
not negligibly so)

## Slide 36: Outline
  Introduction
  Interconnecting Two Devices
  Interconnecting Many Devices
  Network Topology (Now)
    Preliminaries and Evolution
    Indirect Networks
    Direct Networks
    Comparison of Indirect and Direct Networks
  Network Routing
  Concluding Remarks and References

## Slide 37: Network Topology
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0
Preliminaries and Evolution
  One switch suffices to connect a small number of devices
    Number of switch ports limited by VLSI technology, power consumption, packaging, and other such cost constraints
  A fabric of interconnected switches (i.e., switch fabric or network fabric) is needed when the number of devices is much larger
    The topology must make a path(s) available for every pair of devices—property of connectedness or full access (What paths?)
  Topology defines the connection structure across all components
    Bisection bandwidth: the minimum bandwidth of all links crossing a network split into two roughly equal halves
    Full bisection bandwidth:
      Network BWBisection = Injection (or Reception) BWBisection= N/2
    Bisection bandwidth mainly affects performance
  Topology is constrained primarily by local chip/board pin-outs, and not least the routing function …

## Slide 38: Network Topology
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0
Preliminaries and Evolution
  One switch suffices to connect a small number of devices
    Number of switch ports limited by VLSI technology, power consumption, packaging, and other such cost constraints
  A fabric of interconnected switches (i.e., switch fabric or network fabric) is needed when the number of devices is much larger
    The topology must make a path(s) available for every pair of devices—property of connectedness or full access (What paths?)
  Topology defines the connection structure across all components
    Bisection bandwidth: the minimum bandwidth of all links crossing a network split into two roughly equal halves
    Full bisection bandwidth:
      Network BWBisection = Injection (or Reception) BWBisection= N/2
    Bisection bandwidth mainly defines the performance potential
  Topology is constrained primarily by local chip/board pin-outs, and not least the routing function …

## Slide 39: Network Topology
Bisection bandwidth
For tree topology with n nodes can be bisected at the root by «breaking» one link, so bisection bandwidth is one link.
For Hyper-cube topology with n nodes, n/2 links should be «broken» to bisect the network, so bisection bandwidth is bandwidth of n/2 links.
For mesh topology with n nodes, should be «broken» to bisect the network, so bisection bandwidth is links.

## Slide 40: Network Topology
Preliminaries and Evolution
  One switch suffices to connect a small number of devices
    Number of switch ports limited by VLSI technology, power consumption, packaging, and other such cost constraints
  A fabric of interconnected switches (i.e., switch fabric or network fabric) is needed when the number of devices is much larger
    The topology must make a path(s) available for every pair of devices—property of connectedness or full access (What paths?)
  Topology defines the connection structure across all components
    Bisection bandwidth: the minimum bandwidth of all links crossing a network split into two roughly equal halves
    Full bisection bandwidth:
      Network BWBisection = Injection (or Reception) BWBisection= N/2
    Bisection bandwidth mainly defines the performance potential
  Topology is constrained primarily by local chip/board pin-outs, and not least the routing function …

## Slide 41: Network Topology
Crossbar (a single switch) Networks
    Crosspoint switch complexity increases quadratically with the number of crossbar input/output ports, N, i.e., grows as O(N2)
    Has the property of being non-blocking
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0

## Slide 42: Network Topology
Indirect Networks, a.k.a.
  Multistage interconnection networks (MINs)
    Crossbar split into several stages consisting of smaller crossbars => k x k switches
    Complexity grows as O(N × logkN), where N is # of end nodes, with logkN switch stages, each with N/k switches, and the total number of switches is N/k(logkN)
    Inter-stage connections represented by a set of permutation functions
Omega topology, perfect-shuffle exchange
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0

## Slide 43: Network Topology
Indirect Networks
  Going from a single switch network to a MIN comes at the price of performance
    MINs have the property of being blocking
    Contention is more likely to occur on network links
      Paths from different sources to different destinations share one or more links
blocking topology
X
non-blocking topology
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0

## Slide 44: Network Topology
Indirect Networks
  How to reduce blocking in MINs? Provide alternative paths!
    Use larger switches – can equate to using more switches
      Clos network: minimally three stages (non-blocking)
        A larger switch in the middle of two other switch stages provides enough alternative paths to avoid all conflicts
    Use more switches
      Add logkN - 1 stages, mirroring the original topology
        Rearrangeably non-blocking
        Allows for non-conflicting paths
        Doubles network hop count (distance), d
        Centralized control can rearrange established paths
      Benes topology: 2(log2N) - 1 stages (rearrangeably non-blocking)
        Recursively applies the three-stage Clos network concept to the middle-stage set of switches to reduce all switches to 2 x 2

## Slide 45: Network Topology
Indirect Networks
16 port Crossbar network
7
6
5
4
3
2
1
0
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
15
14
13
12
11
10
9
8

## Slide 46: Network Topology
Indirect Networks
16 port, 3-stage Clos network
7
6
5
4
3
2
1
0
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
15
14
13
12
11
10
9
8

## Slide 47: Network Topology
Indirect Networks
16 port, 5-stage Clos network
7
6
5
4
3
2
1
0
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
15
14
13
12
11
10
9
8

## Slide 48: Network Topology
Indirect Networks
16 port, 7 stage Clos network = Benes topology
7
6
5
4
3
2
1
0
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
15
14
13
12
11
10
9
8

## Slide 49: Network Topology
Indirect Networks
Alternative paths from 0 to 1. 16 port, 7 stage Clos network = Benes topology
7
6
5
4
3
2
1
0
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
15
14
13
12
11
10
9
8

## Slide 50: Network Topology
Indirect Networks
7
6
5
4
3
2
1
0
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
15
14
13
12
11
10
9
8
Alternative paths from 4 to 0. 16 port, 7 stage Clos network = Benes topology

## Slide 51: Network Topology
Indirect Networks
7
6
5
4
3
2
1
0
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
15
14
13
12
11
10
9
8
Contention free, paths 0 to 1 and 4 to 0. 16 port, 7 stage Clos network = Benes topology

## Slide 52: Network Topology
  Bidirectional MINs
  Increase modularity
  Reduce hop count, d
  Fat tree network
    Nodes as tree leaves
    Switches as tree vertices
    Total link bandwidth is constant across all tree levels, with full bisection bandwidth
    Equivalent to folded Benes topology
    Preferred topology in many SANs
Folded Clos = Folded Benes = Fat tree network
Indirect Networks
7
6
5
4
3
2
1
0
15
14
13
12
11
10
9
8

## Slide 53: Network Topology
  Bidirectional MINs
  Increase modularity
  Reduce hop count, d
  Fat tree network
    Nodes as tree leaves
    Switches as tree vertices
    Total link bandwidth is constant across all tree levels, with full bisection bandwidth
    Equivalent to folded Benes topology
    Preferred topology in many SANs
Folded Clos = Folded Benes = Fat tree network
Indirect Networks
7
6
5
4
3
2
1
0
15
14
13
12
11
10
9
8
Network
Bisection

## Slide 54: Network Topology
Myrinet-2000, two-level Fat-tee Network for 128 Hosts
Backplane of the M3-E128 Switch
M3-SW16-8F fiber line card (8 ports)
http://myri.com

## Slide 55: Network Topology
Direct Networks
  Tight integration of end node devices with network resources
    Compute nodes distributed among network switches
    A “network node” now consists of a network switch with one or more compute nodes directly connected to it
    Network nodes are directly connected to other nodes
  Fully-connected network: all nodes are directly connected to all other nodes using bidirectional dedicated links
6
2
4
5
7
0
1
3
Network node
Compute node

## Slide 56: Network Topology
Direct Networks
  Example: Compute the switch and link costs of interconnecting N nodes using a fully connected topology relative to a crossbar, assuming
      Cost of a k x k switch grows quadraticaly with the number of unidirectional ports
      Cost of a 1 x k switch grows only linearly
As N increases, the switch cost nearly doubles the crossbar’s
Link cost is always higher than a crossbar’s
No extra benefits of a fully connected network over a crossbar!
Relative costswitches =
2N(N-1)
N2
= 2 ( 1 -
1
N
)
Relative costlinks =
N (N + 1)
2N
=
N+1
2

## Slide 57: Network Topology
Direct Networks
2D torus of 16 nodes
hypercube of 16 nodes
(16 = 24, so n = 4)
2D mesh or grid of 16 nodes
Network
Bisection
full bisection bandwidth

## Slide 58: Network Topology
64-node system with 8-port switches, b = 4
32-node system with 8-port switches
Comparison of Indirect and Direct Networks
  Bristling can be used to reduce direct network switch & link costs
    “b” end nodes connect to each switch, where b is bristling factor
    Allows larger systems to be built from fewer switches and links
    Requires larger switch degree
    For N = 64 and k = 8, fewer switches and links than fat tree

## Slide 59: Network Topology
Comparison of Indirect and Direct Networks
  Blocking reduced by maximizing dimensions (switch degree)
    Can increase bisection bandwidth, but
      Additional dimensions may increase wire length (must observe 3D packaging constraints)
      Flow control issues (buffer size increases with link length)
      Pin-out constraints (limit the number of dimensions achievable)
Evaluation category
Bus
BWBisection in # links
Ring
2D mesh
1
Hypercube
Fat tree
2D torus
Fully
connected
2
8
16
32
32
1024
Max (ave.) hop count
1 (1)
32 (16)
14 (7)
8 (4)
6 (3)
11 (9)
1 (1)
I/O ports per switch
NA
3
5
5
7
4
64
Number of switches
NA
64
64
64
64
192
64
Number of net. links
1
64
112
128
192
320
2016
Total number of links
1
128
176
192
256
384
2080
Performance and cost of several network topologies for 64 nodes. Values are given in terms of bidirectional links & ports.
Hop count includes a switch and its output link (in the above, end node links are not counted for the bus topology).
Perf.
Cost

## Slide 60: Outline
  Introduction
  Interconnecting Two Devices
  Interconnecting Many Devices
  Network Topology
  Network Routing (Now)
  Concluding Remarks and References

## Slide 61: Routing in Interconnection Networks
Routing
  Performed at each switch, regardless of topology
  Defines the “allowed” path(s) for each packet (Which paths?)
  Need to direct packets through network to intended destinations
  Ideally:
    Supply as many routing options to packets as there are paths provided by the topology, and evenly distribute network traffic among network links using those paths, minimizing contention
  Problems: situations that cause packets to never reach their dest.
    Livelock
      Arises from an unbounded number of allowed non-minimal hops
      Solution: restrict the number of non-minimal (mis)hops allowed
    Deadlock
      Arises from a set of packets being blocked waiting only for network resources (i.e., links, buffers) held by other packets in the set
      Probability increases with increased traffic & decreased availability

## Slide 62: Routing in Interconnection Networks
Routing
  Common forms of deadlock:
    Routing-induced deadlock
p
c
1
c
2
c
4
c
5
c
7
c
8
c
10
c
11
p
1
p
1
p
2
p
3
p
2
p
3
p
4
p
4
c
0
1
c
3
p
2
c
6
p
3
c
9
p
4
c
12
p
5
s
1
d
1
s
2
s
3
d
3
d
2
c
1
c
2
c
4
c
7
c
8
c
10
c
5
c
11
s
4
d
4
c
0
c
3
c
6
c
9
s
5
d
5
c
12
Routing of packets in a 2D mesh
Channel dependency graph
ci = channel i
si = source node i
di = destination node i
pi = routing (packet) dependency i

## Slide 63: Routing in Interconnection Networks
Routing
  Common strategies to deal with all forms of deadlock
    Deadlock avoidance: restrict allowed paths only to those that keep the global state deadlock-free, i.e. the channel dependency graph cycle free
      DOR (dimension-order routing) on meshes and hypercubes
        Establish ordering on all resources based on network dimension
      DOR on rings and tori (k-ary n-cubes with wrap-around links)
        Ordering on all resources between and within each dimension
        Apply to multiple virtual channels (VCs) per physical channel
        Alternatively, keep resources along each dimension from reaching full capacity by ensuring the existence of a bubble(s)

## Slide 64: Routing in Interconnection Networks
Deadlock avoidance in ring using VCs
Routing
c13
c00
Network graph
Channel dependency graph
Deadlock avoidance in 2D mesh using DOR
ni = node i
ci = physical channel i
c1i = high-ordered VC i
c0i = low-ordered VC i
Routing
  Common strategies to deal with deadlock
    Deadlock avoidance:
2 virtual channels per physical channel

## Slide 65: Routing in Interconnection Networks
Routing
  Common strategies to deal with all forms of deadlock
    Deadlock recovery: allow deadlock to occur, but once a potential deadlock situation is detected, break at least one of the cyclic dependencies to gracefully recover
      A mechanism to detect potential deadlock is needed
      Regressive recovery (abort-and-retry): remove packet(s) from a dependency cycle by killing (aborting) and later re-injecting (retry) the packet(s) into the network after some delay
      Progressive recovery (preemptive): remove packet(s) from a dependency cycle by rerouting the packet(s) onto a deadlock-free lane
  Deterministic routing: routing function always supplies the same path for a given source-destination pair (e.g., DOR)
  Adaptive routing: routing function allows alternative paths for a given source-destination pair
    Increases routing freedom to improve network efficiency, r

## Slide 66: Routing in Interconnection Networks
Comparison of Routing Freedom
permissible paths
restricted paths
destination
source
Legend:
Dimension-order routing (deterministic)
Partial adaptive routing (Duato´s algorithm)
Recovery routing (true fully adaptive)
Routing
Routing freedom can increase r ( i.e., rR )

## Slide 67: Routing in Interconnection Networks
Routing
  Routing in Fat-tree (indirect) networks
    Least common ancestor (LCA) routing
      Applicable to fat tree and other bidirectional MINs
      Use resources in some partial order to avoid cycles, deadlock
      Reach any LCA switch through any one of multiple paths
      Traverse down the tree to destination through a deterministic path
      Self routing property: switch output port at each hop is given by shifts of the destination node address (least significant bit/digit)
    Up*/down* routing:
      Universally applicable to any topology: map a tree graph onto it
      Assign “up” and “down” directions to network links (or VCs)
      Allowed paths to destination consist of zero or more “up” traversals followed by zero or more “down” traversals
      Up-down traversals impose partial order to avoid cycles, deadlocks

## Slide 68: Concluding Remarks and References
Concluding Remarks
  Interconnection network design is an important area of computer architecture
    on-chip networks between cores within a chip
    off-chip networks between chips and boards within a system
  Interconnection networks should be designed to transfer the maximum amount of information within the least amount of time (and cost, power constraints) so as not to bottleneck the system
  The design of interconnection networks is end-to-end
    injection links/interface, network fabric, reception links/interface
    topology, routing, arbitration, switching, and flow control are among key concepts in realizing high-performance designs
    a simple, general throughput model can be used to guide design
  Improving the performance of interconnection networks is critical to advancing our information- and communication-centric world

## Slide 69: Interconnecting Two Devices
Characterizing Performance: Latency & Effective Bandwidth
Terms and Definitions:
  Bandwidth:
    Maximum rate at which information can be transferred (including packet header, payload and trailer)
    Unit: bits per second (bps) or bytes per second (Bps)
    Aggregate bandwidth: Total data bandwidth supplied by network
    Effective bandwidth (throughput): fraction of aggregate bandwidth that gets delivered to the application
  Time of flight: Time for first bit of a packet to arrive at the receiver
    Includes the time for a packet to pass through the network, not including the transmission time (defined next)
    Picoseconds (OCNs), nanoseconds (SANs), microseconds (LANs), milliseconds (WANs)

## Slide 70: Interconnecting Two Devices
Characterizing Performance: Latency & Effective Bandwidth
  Transmission time:
      The time for a packet to pass through the network, not including the time of flight
      Equal to the packet size divided by the data bandwidth of the link
  Transport latency:
      Sum of the time of flight and the transmission time
      Measures the time that a packet spends in the network
  Sending overhead (latency):
      Time to prepare a packet for injection, including hardware/software
      A constant term (packet size) plus a variable term (buffer copies)
  Receiving overhead (latency):
      Time to process an incoming packet at the end node
      A constant term plus a variable term
      Includes cost of interrupt, packet reorder and message reassembly

## Slide 71: Interconnecting Two Devices
Characterizing Performance: Latency & Effective Bandwidth
Receiver
Sender
Sending
overhead
Transmission time
(bytes/bandwidth)
Time of
flight
Transmission time
(bytes/bandwidth)
Receiving
overhead
Transport latency
Total latency
Time
Latency = Sending Overhead + Time of flight + + Receiving Overhead
packet size
Bandwidth