## Slide 1: Department of Informatics Networks and Distributed Systems (ND) group
IN3230/4230 - Nettverk
Wireless Communications - I
Özgü Alay
ozgua@ifi.uio.no

## Slide 2: Wireless Communications Networks

## Slide 3: Outline
Brief history of wireless
What is wireless communication?
Bottom-down approach: Wireless basics
  Physical layer : how can we transmit signals in air?
  Link layer : multiple access
  Wireless impact higher layers?
More advanced methods
  MIMO
  Beamforming
  mmWave

## Slide 4: Looking back in time to wireless
1873
1896
1980
1990
2000
2010
2020
Maxwell
equations
Radio Patent
Commercial Network, Cellphone
2G GSM, GPRS, EDGE
3G, Bluetooth, Wifi
4G/LTE, LTE-A
5G
5G
Lorem ipsum dolor sit amet, nibh est. A magna maecenas, quam magna nec quis, lorem nunc. Suspendisse viverra sodales mauris, cras pharetra.

## Slide 5: Outline
Brief history of wireless
What is wireless communication?
Bottom-down approach
  Physical layer : how can we transmit signals in air?
  Link layer : multiple access
  Wireless impact higher layers?
More advanced methods
  MIMO
  Beamforming
  mmWave

## Slide 6: Why Wireless?
Freedom from wires
  No cost of installing the wires
  Not deal with bunches of wires running around
Global coverage
  where wired communication is not feasible or costly e.g. rural areas, battle field and outer space.
Stay Connected
  Any where any time, even under mobility
Flexibility
  Connect to multiple devices simultaneously

## Slide 7: What is Wireless Communication?
Transmitting voice and data using electromagnetic waves in open space
Electromagnetic waves
    Travel at speed of light (c = 3x108 m/s)
    Has a frequency (f) and wavelength (l)
        c = f x l

## Slide 8: Wireless Link Characteristics
  decreased signal strength: radio signal attenuates (lose signal strength) as it propagates through matter (path loss)
      Higher frequencies will attenuate FASTER
      Higher frequencies also don’t penetrate objects as well
  interference from other sources: standardized wireless frequencies shared by other devices (e.g., phone); devices (motors) interfere as well
  multipath propagation: radio signal reflects off objects/ground, reaching destination at slightly different times
…. make communication across (even a point to point) wireless link much more “difficult”

## Slide 9: Electromagnetic Spectrum
104
102
100
10-2
10-4
10-6
10-8
10-10
10-12
10-14
10-16
104
106
108
1010
1012
1014
1016
1018
1020
1022
1024
IR
UV
X-Rays
Cosmic
Rays
Radio
Spectrum
3MHz ==100m 300MHz ==1m
30GHz ==1cm
< 30 KHz VLF 30-300KHz LF
300KHz – 3MHz MF 3 MHz – 30MHz HF 30MHz – 300MHz VHF
300 MHz – 3GHz UHF
3-30GHz SHF
> 30 GHz EHF
Micro wave
Visible light

## Slide 10: Outline
Brief history of wireless
What is wireless communication?
Bottom-down approach
  Physical layer : how can we transmit signals in air?
  Link layer : multiple access
  Wireless impact higher layers?
More advanced methods
  MIMO
  Beamforming
  mmWave

## Slide 11: Block diagram of radio transmission
Information (e.g. sound) is converted by a transducer (e.g. a microphone) to an electrical signal
This signal is used to modulate a radio wave sent from a transmitter.
A receiver intercepts the radio wave and extracts the information-bearing electronic signal, which is converted back using another transducer such as a speaker.

## Slide 12: What is modulation?
Modulation = Adding information to a carrier signal

## Slide 13: Modulation Process
Modulation implies varying one or more characteristics (modulation parameters a1, a2, … an) of a carrier f in accordance with the information-bearing (modulating) baseband signal.
Sinusoidal waves, pulse train, square wave, etc. can be used as carriers

## Slide 14: Carrier Signal
Carrier signal:

## Slide 15: Types of Modulation
Analog Modulation: If the variation in the parameter of the carrier is continuous in accordance to the input analog signal the modulation technique is termed as analog modulation scheme
Digital Modulation: If the variation in the parameter of the carrier is discrete then it is termed as digital modulation technique

## Slide 16: ANALOG MODULATION
Amplitude Modulation: Signal shapes the amplitude of the carrier
Frequency Modulation: Signal shapes the frequency of the carrier

## Slide 17: DIGITAL MODULATION TECHNIQUES

## Slide 18: DIGITAL MODULATION TECHNIQUES

## Slide 19: BPSK Representation
Transmit 1
Transmit 0
Q
I
Transmit 0
Transmit 1
{Phase 0}
{Phase }
2 symbols

## Slide 20: Constellation Diagram
Transmit 1
Transmit 0
Q
I
= graphical representation of the complex envelope of each possible symbol state
  The x-axis represents the in-phase component (real part) and the y-axis the quadrature component (imaginary part) of the complex envelope
  The distance between signals on a constellation diagram relates to how different the modulation waveforms are and how easily a receiver can differentiate between them.
Notes: In-phase (I) Axis:
  The in-phase axis represents the real part of the complex signal. It corresponds to the portion of the signal that is in phase with the carrier wave. Values on this axis indicate how much of the signal is aligned with the reference signal at a given time.
Quadrature (Q) Axis:
  The quadrature axis represents the imaginary part of the complex signal. It corresponds to the portion of the signal that is 90 degrees out of phase with the carrier wave. Values on this axis indicate the component of the signal that is orthogonally related to the in-phase component.

## Slide 21: QPSK Constellation Diagram
Quadrature Phase Shift Keying (QPSK) can be interpreted as two independent BPSK systems (one on the I-channel and one on Q)
Quadrature Phase Shift Keying has twice the bandwidth efficiency of BPSK since 2 bits are transmitted in a single modulation symbol
Carrier phases {0, /2, , 3/2}
Carrier phases {/4, 3/4, 5/4, 7/4}
Q
I
I
Q
4 symbols

## Slide 22: Quadrature Amplitude Modulation (QAM)
Both amplitude and phase modulation
16 symbols

## Slide 23: Multi-level (M-ary) Phase and Amplitude Modulation
16 QAM
16 APSK
16 PSK
There are different constellations having same number of logical states but different efficiency

## Slide 24: What is a good constellation?
Perfect channel
White noise
Phase jitter
Need to consider Distortions and the signal can be decoded!

## Slide 25: Impact of Distortions
Noise can change the amplitude easier than the phase. PSK is less susceptible to noise than ASK.
Major drawback of PSK is the rapid amplitude change between symbols due to phase discontinuity
PSK is superior to FSK because we do not need two carrier signals.
Binary Phase Shift Keying (BPSK) demonstrates better performance than ASK and BFSK

## Slide 26: Example
a) What type of modulation does this represent?
b) How many symbols are represented?
c)How many bits per symbol are used?
d)Would 16-QAM be more or less susceptible to noise than this type of modulation?

## Slide 27: Outline
Brief history of wireless
What is wireless communication?
Bottom-down approach
  Physical layer : how can we transmit signals in air?
  Link layer : multiple access
  Wireless impact higher layers?
More advanced methods
  MIMO
  Beamforming
  mmWave

## Slide 28: Multiplexing (MUX) / Multiple Access (MA)
Transmission of several data flows (logical connections) over one medium
  Realize individual “connections“, normally with deterministic properties (throughput, delay)
  Terminology: M (“.. Multiplexing“) or MA (“.. Multiple Access“)
Also: Transmission of one data flow (logical connection) over several media
  (increase performance and/or reliability)

## Slide 29: Time Division Multiple Access (TDMA)
Each user is allowed to transmit only within specified time intervals (Time Slots). Different users transmit in different Time Slots.
When users transmit, they occupy the whole frequency bandwidth (separation among users is performed in the time domain).
Commonly used in GSM together with frequency hopping

## Slide 30: Frequency Division Multiple Access (FDMA)
Each user transmits with no limitations in time, but using only a portion of the whole available frequency bandwidth
Different users are separated in the frequency domain
FDMA can be used for both digital and analog signals
Very common in satellite communications
The major disadvantage of FDMA is the relatively expensive and complicated bandpass filters required.

## Slide 31: FDMA in time domain

## Slide 32: Code Division Multiple Access (CDMA)
unique “code” assigned to each user; i.e., code set partitioning
  all users share same frequency, but each user has own “chipping” sequence (i.e., code) to encode data
  allows multiple users to “coexist” and transmit simultaneously with minimal interference
Chip sequences are orthogonal to ensure reconstructability:
  seq. 1: x = (x1, .. xn), seq. 2: y = (y1, .. yn)  xi yi = 0
  Common choice: Walsh sequence
encoded signal = (original data) X (chipping sequence)
decoding: inner-product of encoded signal and chipping sequence

## Slide 33: CDMA encode/decode
slot 1
slot 0
d1 = -1
1
1
1
1
1
-
1
-
1
-
1
-
Zi,m= di.cm
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
channel output Zi,m
sender
code
data
bits
slot 1
slot 0
d1 = -1
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
receiver
code
received
input
Di = S Zi,m.cm
m=1
M
M

## Slide 34: CDMA: two-sender interference
using same code as sender 1, receiver recovers sender 1’s original data from summed channel data!
Sender 1
Sender 2
channel sums together transmissions by sender 1 and 2

## Slide 35: Orthogonal Frequency Division Multiple Access (OFDMA)
The carriers are chosen such that they are orthogonal to one another
It allocates in both the time domain and the frequency domain, allowing for multiple users—even those with widely varying use patterns or data loads

## Slide 36: Orthogonality Principle
For a subcarrier in OFDM to be orthogonal, it must be spaced from its adjacent, neighboring subcarrier(s) in such a way that the peak of each adjacent subcarrier falls exactly at its zero crossings
Example: 5 adjacent subcarriers in the frequency domain, normalized to an amplitude of 1 and a frequency separation of 1.

## Slide 37: Summary: FDMA,TDMA, CDMA and OFDMA
1G/TACS
2G/GSM
3G
4G/LTE and Wimax

## Slide 38: Outline
Brief history of wireless
What is wireless communication?
Bottom-down approach
  Physical layer : how can we transmit signals in air?
  Link layer : multiple access
  Wireless impact higher layers?
More advanced methods
  MIMO
  Beamforming
  mmWave

## Slide 39: Wireless: impact on higher layers
logically, impact should be minimal …
  best effort service model remains unchanged
  TCP and UDP can (and do) run over wireless, mobile
… but performance-wise:
  packet loss/delay due to bit-errors (discarded packets, delays for link-layer retransmissions), and handoff
  TCP interprets loss as congestion, will decrease congestion window un-necessarily
  delay impairments for real-time traffic
  limited bandwidth of wireless links

## Slide 40: Outline
Brief history of wireless
What is wireless communication?
Bottom-down approach
  Physical layer : how can we transmit signals in air?
  Link layer : multiple access
  Wireless impact higher layers?
More advanced methods
  MIMO
  Beamforming
  mmWave

## Slide 41: What is MIMO?
MIMO is an acronym that stands for Multiple Input Multiple Output
Motivation: current wireless systems
  Capacity constrained networks
  Increasing interference, limited spectrum
MIMO exploits the space dimension to improve wireless systems capacity, range and reliability

## Slide 42: How does MIMO work?
MIMO uses multiple antennas to send multiple parallel signals (from transmitter). These parallel signals are intelligently coded
When there is enough distance between the antennas, different signals experience different paths -> MIMO takes advantage of multi-path
With MIMO, the receiving end uses an algorithm or special signal processing to sort out the multiple signals to produce one signal that has the originally transmitted data

## Slide 43: Different types

## Slide 44: Main Types of MIMO
Space Time Transmit Diversity (STTD) - The same data is coded and transmitted through different antennas, which effectively doubles the power in the channel. This improves Signal Noise Ratio (SNR) for cell edge performance.
Spatial Multiplexing (SM) - SM delivers parallel streams of data by exploiting multi-path. It can double (2x2 MIMO) or quadruple (4x4) capacity and throughput. SM gives higher capacity when RF conditions are favorable and users are closer to the base station.

## Slide 45: Outline
Brief history of wireless
What is wireless communication?
Bottom-down approach
  Physical layer : how can we transmit signals in air?
  Link layer : multiple access
  Wireless impact higher layers?
More advanced methods
  MIMO
  Beamforming
  mmWave

## Slide 46: Beamforming
Beamforming is a signal processing technique used for directional signal transmission or reception.
Elements of an antenna array is combined in such a way that signals at particular angles experience constructive interference while others experience destructive interference.

## Slide 47: An antenna radiates energy like....
from Mark Hickle https://youtu.be/vtPPAnvJS6c

## Slide 48: Forming a beam

## Slide 49: Transmit beam and receive strength

## Slide 50: Transmit beam and receive strength

## Slide 51: Transmit beam and receive strength

## Slide 52: Beamforming and Steering

## Slide 53: Outline
Brief history of wireless
What is wireless communication?
Bottom-down approach
  Physical layer : how can we transmit signals in air?
  Link layer : multiple access
  Wireless impact higher layers?
More advanced methods
  MIMO
  Beamforming
  mmWave

## Slide 54: What is mmWave?
Millimeter Wave Bands
Most wireless operates in this range
0
10GHz
20GHz
30GHz
40GHz
50GHz
60GHz
70GHz
80GHZ
90GHz
100GHz
Frequency Spectrum

## Slide 55: Why mmWave?
Shannon-Hartley Theorem
C—channel capacity (bps),
B—channel bandwidth (Hz),
S—average signal power, and
N— average noise and interference power.
At higher carrier rates, larger B -> higher
rates.
100-1000 times faster than existing wireless networks

## Slide 56: How does mmWave work?
mmWave: High attenuation at high frequencies -> very short range
Client
AP

## Slide 57: How does mmWave work?
To address high attenuation, beamforming is used!
Challenge: Beam alignment
Client
AP

## Slide 58: How does mmWave work?
Line of sight exists
Client
AP

## Slide 59: How does mmWave work?
Client
AP
Line of sight blocked

## Slide 60: Beamforming Training
Beamforming Training in 802.11ad