## Slide 1: Introduction to video coding
February 3, 2026
using slides by
Håvard Espeland, Pål Halvorsen,
Preben N. Olsen, Carsten Griwodz
IN5050: Programming heterogeneous multi-core processors

## Slide 2: Why ?
IN5050 is about programming heterogeneous multi-core processors.
Why an intro to video coding?
Parallel processing without workloads has always targeted individual algorithms: counting, searching, sorting, ...
Real workloads use multiple, different algorithms that need to cooperate and be interconnected and have non-parallelizable steps as well
We want to look at parallelism that is required for everyday tasks, not at super-high-end scientific computing or incomprehensible machine learning stages
We know a bit more about video streaming than other casual tasks:
Many of its applications are time-critical
A codec can become memory-bound, CPU-bound, IO-bound
A single codec has opportunities for data parallelism, functional parallelism, and pipelining
It is also a very important workload in its own right
... and Håkon doesn't want me to use SIFT for IN5050 instead

## Slide 3: Why ?
IN5050 is about programming heterogeneous multi-core processors.
Why an intro to video coding?
Parallel processing without workloads has always targeted individual algorithms: counting, searching, sorting, ...
Real workloads use multiple, different algorithms that need to cooperate and be interconnected and have non-parallelizable steps as well
We want to look at parallelism that is required for everyday tasks, not at super-high-end scientific computing or incomprehensible machine learning stages
We know a bit more about video streaming than other casual tasks:
Many of its applications are time-critical
A codec can become memory-bound, CPU-bound, IO-bound
A single codec has opportunities for data parallelism, functional parallelism, and pipelining
It is also a very important workload in its own right
According to Cisco predictions in 2019, Internet video globally
… consumed 159 Exabytes per month in 2019.
… had a compound annual growth rate of 31%.
… was expected to reach 280 exabytes/month in 2022.
… had 82% of consumer Internet traffic in 2021.
...
Statista reports number of users
>3900 mio over-the-top (OTT) streaming users in 20241
Expect > 5110 mio users in 20302
(1 2024 information, 2 2026 prediction)

## Slide 4: High data volumes: Need for compression
PAL video sequence
  25 images per second
  3 bytes per pixel
    RGB (red-green-blue values)
    YUV (luminance + 2 chrominance values), usually often a compression already
  Uncompressed data rate depending on resolution:
    VGA: 640 * 480 * 3 Byte * 25/s = 23.040.000 byte/s = ~ 22 MByte/s
    HD 720p: 1280 * 720 * 3 Byte * 25/s = 69.120.000 byte/s = ~ 66 Mbyte/s
    HD 1080p: 1920 * 1080 * 3 Byte * 25/s = 155.520.000 byte/s = ~ 148 Mbyte/s
Network rates
  5 Mbps ADSL: 4% of 1 HD1080p
  1 Gbps Ethernet: 84% of 1 HD1080p
Need for compression

## Slide 5: Data Compression
Alternative description of data requiring less storage and bandwidth
Uncompressed: 1 Mbyte
Compressed (JPEG): 50 Kbyte (20:1)
... while, for example, a 20 Megapixel camera creates 6016 x 4000 images,
in 8-bit RGB that makes more than 72 uncompressed Mbytes per image

## Slide 6: Coding pictures
IN5050: Programming heterogeneous multi-core processors
„Kodak No 2-A Folding Autographic Brownie (ca 1917)“ by Carsten Corleis – own work. Licensed under Creative Commons Attribution-Share Alike 3.0

## Slide 7: JPEG
“JPEG”: Joint Photographic Expert Group
International Standard:
  For digital compression and coding of continuous-tone still images
  Gray-scale and color
Compression rate of 1:10 yields reasonable results (better rates are also possible)

## Slide 8: Color conversion: RGB to YCbCr
Y image is a greyscale version of the main image
the white snow is represented as a middle value in both Cr and Cb
the brown barn is represented by weak Cb and strong Cr
the green grass is represented by weak Cb and weak Cr
the blue sky is represented by strong Cb and weak Cr
RGB
YCbCr
G
B
Y
Cb
Cr
R
Notes: Originally, YUV was for analog signals and YCbCr was used for digital encoding of color information suited for video and still-image compression. Today, the term YUV is commonly used in the computer industry to describe file-formats that are encoded using YCbCr.
invented when engineers wanted color television in a black-and-white infrastructure -- UV representation of chrominance was chosen over straight R and B signals because U and V are color difference signals. This meant that in a black and white scene the U and V signals would be zero and only the Y' signal would need to be transmitted.
Y: luminance
Cb: Chroma blue, the difference between blue and luminance
Cr: Chrome red, the difference between red and luminance
consequently, green is implied by the residual values

## Slide 9: (Chroma) Downsampling
Downsampling (first compression step)
  humans can see considerably more fine detail in the brightness, i.e., can reduce the spatial resolution of the Cb and Cr components
  4:4:4 (no downsampling)
  4:2:2 (reduce by factor of 2 in horizontal direction)
  4:2:0 (reduce by factor of 2 in horizontal and vertical directions)
YCbCr
Y
Cb
Cr
Notes: Why 4:2:2 and 4:2:0?
4:2:2 – we take a square of 4x4 pixels. From the odd lines, we keep 2 pixels, from the even lines, we also keep 2 pixels.
4:2:0 – again, start with 4 pixels. From the odd lines, we keep 2 pixels, from the even lines, we keep 0 pixels.

## Slide 10: Split each picture in 8x8 blocks
Each Y, Cb and Cr picture is divided into 8x8 blocks

## Slide 11: Discrete cosine transform (DCT)
Each 8×8 block (Y, Cb, Cr) is converted to a frequency-domain representation, using a normalized, two-dimensional DCT
Notes: A discrete cosine transform (DCT) expresses a finite sequence of data points in terms of a sum of cosine functions oscillating at different frequencies.
it has a strong "energy compaction" property: most of the signal information tends to be concentrated in a few low-frequency components of the DCT -- this stems from the boundary conditions implicit in the cosine functions.

## Slide 12: DCT
Each 8×8 block (Y, Cb, Cr) is converted to a frequency-domain representation, using a normalized, two-dimensional DCT
  initially, each pixel is represented by a [0, 255]-value
  each pixel is transformed to a [-128, 127]-value
- 128 =

## Slide 13: DCT
- 128 =
Each 8×8 block (Y, Cb, Cr) is converted to a frequency-domain representation, using a normalized, two-dimensional DCT
  two-dimensional DCT:
    Gu,v is the DCT at output coordinates (u,v) in the transformed 8x8 matrix
    u and v are from {0, ..., 7}
    gx,y is the pixel value at input coordinates (x,y)
    α is a normalizing function:
Notes: Note: if u and v are 0, cos(0)=1 has a lot of weight. So, we normalize “harder” by multiplying with 1/8. On the left and upper edge, one of the cos values is 1, so we multiply with sqrt(1/8)*sqrt(2/8)=1/4*sqrt(1/2)=1/5.66. Inside, no cos values are 1, so we multiply with sqrt(2/8)^2=1/4

## Slide 14: DCT
- 128 =
Each 8×8 block (Y, Cb, Cr) is converted to a frequency-domain representation, using a normalized, two-dimensional DCT
  two-dimensional DCT:
    Gu,v is the DCT at output coordinates (u,v)
    u and v are from {0, ..., 7}
    gx,y is the pixel value at input coordinates (x,y)
    α is a normalizing function:
Notes: Note: if u and v are 0, cos(0)=1 has a lot of weight. So, we normalize “harder” by multiplying with 1/8. On the left and upper edge, one of the cos values is 1, so we multiply with sqrt(1/8)*sqrt(2/8)=1/4*sqrt(1/2)=1/5.66. Inside, no cos values are 1, so we multiply with sqrt(2/8)^2=1/4

## Slide 15: DCT
- 128 =
Apply DCT =
Note the rather large value of the top-left corner (DC coefficient). The remaining 63 are AC coefficients. The advantage of the DCT is its tendency to aggregate most of the signal (the block average) in one corner of the result, as may be seen to the right.
Compression possible: the following quantization step accentuates this effect while simultaneously reducing the overall size of the DCT coefficients

## Slide 16: DCT
- 128 =
Apply DCT =
Note the rather large value of the top-left corner (DC coefficient). The remaining 63 are AC coefficients. The advantage of the DCT is its tendency to aggregate most of the signal in one corner of the result, as may be seen to the right.
Compression possible: the following quantization step accentuates this effect while simultaneously reducing the overall size of the DCT coefficients
explain DC & AC

## Slide 17: Quantization
The human eye
  is good at seeing small differences in brightness over a large area
  not so good at distinguishing the exact strength of a high frequency brightness variation
  can reduce the amount of information in the high frequency components
  Simply dividing each component in the frequency domain by a known constant for that component, and then rounding to the nearest integer:
  where Qj,k is a quantization matrix

## Slide 18: Quantization Example

## Slide 19: Lossless compression
The resulting data for all 8×8 blocks is further compressed with a loss-less algorithm
1. organize numbers in zigzag pattern
  -26, -3, 0, -3, -2, -6, 2, -4, 1, -4, 1, 1, 5, 1, 2, -1, 1, -1, 2, 0, 0, 0, 0, 0, -1, -1, 0 , 0, 0, 0, 0, 0, 0, 0, 0, …., 0, 0
2. run-length coding

## Slide 20: JPEG Encoder Overview
Fn
(current)
Prepare
(RGB2YUV)
DCT
Quant
Entropy coding
Encoding:

## Slide 21: Coding videos
IN5050: Programming heterogeneous multi-core processors
"Pathé-Baby hand movie camera (right)” by Cquoi - Own work. Licensed under Creative Commons Attribution-Share Alike 3.0

## Slide 22: Motion JPEG
Motion JPEG
  compress video by repeating JPEG steps
  allows pipelining of frames
Motion JPEG is not a standard
  Apple has a Quicktime container
  Microsoft has another container
  the IETF has defined an RTP profile
  ...
  and they are all (mostly) incompatible
Fn
(current)
Prepare
(RGB2YUV)
DCT
Quant
Entropy coding
Still
very typical for
video editing tools
(but nothing else)

## Slide 23: A picture

## Slide 24: A new pictures? A changed picture!

## Slide 25: Macro blocks

## Slide 26: Focusing on blocks A B C & D

## Slide 27: Best match in reference frame

## Slide 28: 1. Challenge: small differences

## Slide 29: Challenge: Displacement

## Slide 30: Adding Motion to the JPEG pipeline
Fn
(current)
Prepare
(RGB2YUV)
DCT
Quant
Entropy coding

## Slide 31: Adding Motion to the JPEG pipeline
Fn
(current)
Fn-1
(reference)
Prepare
(RGB2YUV)
DCT
Quant
Entropy coding
Motion estimation

## Slide 32: Inter-Prediction
Predict a macroblock by reusing pixels from another frame
  Motion vectors are used to compensate for movement
  H.263: search in 1 frame
  MPEG-1/2: search in 2 frames
  H.264 (AVC) + H.265 (HEVC): search in 16 frames

## Slide 33: Full Search Motion Estimation
and so on ...
Find best match
Fn
(current)
Fn-1
(reference)
For comparing blocks:
SAD - Sum of Absolute Differences
W: fixed set, but not only integers !

## Slide 34: Diamond Motion Estimation Pattern
Heuristic
  start at the same place in previous frame
  search neighourhood first
  move search center to location with smallest SAD
  repeat until stable

## Slide 35: Motion Estimation
The estimators often use a two-step process, with initial coarse evaluation and refinements
Don’t do this for every frame, you must sometimes encode macroblocks in a “safe” mode that doesn’t rely on others
This is called “Intra”-mode
  When a complete frame is encoded in I-mode (always in MPEG-1 and MPEG-2), this is called an I-frame
  x264 calls I-frames "keyframes". But the word keyframe has many, many other meanings as well. Avoid misunderstandings. Write I-frame. There are also IBR frames.
Refinements include trying every block in the area, and also using sub-pixel precision (interpolation)
  quarter pixel in H.264

## Slide 36: Adding Motion to the JPEG pipeline
Fn-1
(reference)
Fn
(current)
Fn-1
(reference)
Prepare
(RGB2YUV)
DCT
Quant
Entropy coding
Motion estimation
Motion compen-sation

## Slide 37: Motion Compensation
When the best motion vector has been found and refined, a predicted image is generated using the motion vectors
The reference frame can not be used directly as input to the motion compensator
  The decoder never sees the original image. Instead, it sees a reconstructed image, i.e. an image that has been quantized (with loss)
A reconstructed reference image must be used as input to motion compensation

## Slide 38: Adding Motion to the JPEG pipeline
Fn-1
(reference)
Fn
(current)
Fn-1
(reference)
Prepare
(RGB2YUV)
DCT
Quant
Entropy coding
Motion estimation
Motion compen-sation

## Slide 39: Adding Motion to the JPEG pipeline
Fn-1
(reference)
Fn
(current)
Fn-1
(reference)
Prepare
(RGB2YUV)
DCT
iDCT
iQuant
Quant
Entropy coding
Motion estimation

## Slide 40: Frame Reconstruction
The motion compensator requires as input the same reference frame as the decoder will see
De-quantize and inverse-transform the residuals and add them to our predicted frame
The result is (roughly) the same reconstructed frame as the decoder will receive

## Slide 41: Residual Transformation
The pixel difference between the original frame and the reconstructed frame is called residuals
Since the residuals only express the difference from the prediction, they are much more compact than full pixel values such as in JPEG
Residuals are transformed using DCT and Quantization
MPEG uses special Quantization tables for residuals
in IN5050, we don’t

## Slide 42: Adding Motion to the JPEG pipeline
Fn-1
(reference)
Fn
(current)
Fn-1
(reference)
Prepare
(RGB2YUV)
DCT
iDCT
iQuant
Quant
Entropy coding
Motion estimation
Motion compen-sation
recon-struction

## Slide 43: Adding Motion to the JPEG pipeline
Fn-1
(reference)
Fn
(current)
Fn-1
(reference)
Prepare
(RGB2YUV)
DCT
iDCT
iQuant
Quant
Reorder
Entropy coding
Motion estimation
Motion compen-sation
recon-struction

## Slide 44: Macroblock Types
oldest
frame
newest
frame
MPEG-1 macroblocks are 8x8 pixels, they can be of type I, P or B
  Intra-MBs use Intra-prediction (like JPEG)
  Predicted MBs use Inter-prediction
  Bi-Directional Predicted MBs use prediction both backward and forward in time
  The frames are reordered in such a way that frames used for predicting other frames are decoded first

## Slide 45: Adding Motion to the JPEG pipeline
Fn-1
(reference)
Fn
(current)
Fn-1
(reference)
Prepare
(RGB2YUV)
DCT
iDCT
iQuant
Quant
Reorder
Entropy coding
Motion estimation
Motion compen-sation
recon-struction

## Slide 46: Simplified MPEG Encoder Overview
Fn-1
(reference)
Fn
(current)
Fn-1
(reference)
Prepare
(RGB2YUV)
DCT
iDCT
iQuant
Quant
Reorder
Entropy coding
Motion estimation
Motion compen-sation
Intra prediction
fail
ok
recon-struction

## Slide 47: GOP-based Approach
Delay pictures until there are multiple keyframes within the encoder pipeline
Intra-frames do not depend on previous frames, and thus can be used as starting points for multiple encodes
Adds a considerable pipeline to the encoder

## Slide 48: Slice-Based Approach
Split every frame into one or more slices
Supported since MPEG-1
Slices are completely independent – one may not predict across borders
Severely hurts compression efficiency

## Slide 49: Video Quality Assessment
Evaluating video quality is a research field by itself
Usually requires a panel of subjects that rate which version is best
  Subjects have different preferences for artifacts and quality reductions
Objective measurements give a rough number which says something about the difference between the original frames and the reconstructed frames
  Typically SSIM or PSNR
  A shell script for finding PSNR values of YUV frames can be found in the mplayer source tree under TOOLS/

## Slide 50: Conclusion
Video encoding is mainly about trying (and failing) different prediction modes limited by user-defined restrictions (resource usage)
The “actual” encoding of the video when the parameters are known (forgetting about all the failed tests) usually accounts for a small percentage of the running time
  This makes decoding cheap
  An important goal of MPEG
Any (reasonable) codec can produce the desired video quality – what differs between them is the size of the output