## Slide 1: IN5230 - Mandatory Task 2

## Slide 2: Deadline for delivery
October 14th @ 08:00.
Each group submits a report.
Image is borrowed from Internet!

## Slide 3: Electro-Magnetic Interface (EMI)
Provided Materials
  EMxpert Scanner
  Demo Board
  Laptop

## Slide 4: EMxpert Scanner
A1

## Slide 5: EMxpert Scanner
Paper tape for fixing the board on the scanner.

## Slide 6: EMxpert Scanner
USB Charger for powering up the boards.

## Slide 7: Laptop
Username: stoy, Password: stoystoy
C:\IN5230stud/2026
  GroupN_user1_user2
EMxpert64 Program

## Slide 8: Scanning Type
Spectral Scan
  Scanning the PCB at some locations in a wide frequency range.
Spatial Scan
  Scanning a selection of locations at a certain frequency.

## Slide 9: BRD#01
Protecting the power supply from EM field generated by the IC clock by:
  Decoupling capacitor
  Small loop
  Ferrite Bead*
* FB suppresses high-frequency electronic noise in electronic circuits.

## Slide 10: BRD#05
Routing the signal over the slot on the ground plane is dangerous!
High frequency signal tries to return in the same direction as the forward path.
Notes: Low Frequency signal selects the shortest path.

## Slide 11: BRD#07
Shielding reduces the EMI!

## Slide 12: BRD#10
Testing the performance of the NFC antenna by EM scanner.

## Slide 13: BRD#08, PhD
Critical signal near the edge of the board is not a good option causing fringing effect.

## Slide 14: Scaling

## Slide 15: Project Setting
Spectral Scan
  Scanning the PCB at some locations in a wide frequency range.
  Start frequency = 10MHz, Stop frequency = 200MHz, and RBW=122.070 kHz
  Enable Interleaved Scan

## Slide 16: Project Setting
Spectral Scan Probes
  Select None and set Overlay editor and browse the image from: ‘C:\EMSCAN\IN5230 DemoCard\DemoBoardGerb’
  Adjust the image.

## Slide 17: Project Setting
Spatial Scan
  Scanning a selection of locations at a certain frequency.
  Set Center frequency = 20MHz.
  Enable Interleaved Scan

## Slide 18: Project Setting
Spatial Scan Probes
  The same as Spectral Scan Probes.

## Slide 19: Project Setting
Leave the Signal Conditioning section as it is.
Use the Description Tab to change the name of the project.
Create a new node for each exercise
  project → right click → add node → module
  change the module name to the exercise name
Add a new simulation within each exercise module
  exercise 1 → add node → Spectral/Special

## Slide 20: Enjoy 😊