## Slide 1: IN5230 - Mandatory Task 1

## Slide 2: Simulation Tool
LTspice
  https://www.analog.com/en/resources/design-tools-and-calculators/ltspice-simulator.html
  Download for either MAC or Windows.

## Slide 3: Report
Submitting Individually
Complete schematics including simulation mode as well as simulation results
White background on schematics and simulation results
Using legends
Avoiding yellow color on curves
Making a conclusion
  summary table
In English
PDF format
Attaching Schematics/symbols in LTspice format

## Slide 4: Deadline for delivery
September 16th @ 08:00
Image is borrowed from Internet!

## Slide 5: Task 1: Get familiar with the simulator
Op-amp LM741
a) Transient Analysis (.tran)
  Calculating the gain in theory
  Applying a DC offset for the negative input
and calculating the gain
  Finding DC offset interval where the output does not clip (.step)
b) AC Analysis (.ac)
  Finding DC gain and GBW
  Phase margin

## Slide 6: Task 1: Get familiar with the simulator
c) Common mode DC offset
d) Effect of the load capacitor on the DC gain and GBW

## Slide 7: Task 2: Frequency characteristics of some curves
Define the R1 and C1 value to have a very high cut-off frequency
Effect of the time step in .tran simulation on the FFT values.
FFT for different square pulse inputs with different rise time (freq. = 1KHz)
Redesign the filter so that the cut-off frequency is the 5 times over the fundamental frequency (1KHz), How is the FFT output?

## Slide 8: Task 3: Decoupling capacitors
Find the size and number of capacitors required to reduce the supply voltage noise to an acceptable level
Study the slide 48 to 57 of the first lecture
i

## Slide 9: Imp.: Task 4 : Parasitic capacitive coupling
a) Coupling the signal from a noise source to an object due to the parasitic cap.
b) How does shielding reduce the coupling?
Source
Object
C1
{
Load
Shield

## Slide 10: Task 5: Artificial sources of transient analysis
Generating different noise source “bv”:
  RAND, RANDOM: Uniform within [0, 1)
  WHITE: Semi gaussian distribution within (-0.5, 0.5)
  PWL signal
*Datafile and example schematic are available on the web-site
Uniform
Gaussian

## Slide 11: Random Noise Source