## Slide 1: Operating Systems: Introduction
Pål Halvorsen
Wednesday 16 September 15
INF1060: Introduction to Operating Systems and Data Communication

## Slide 2: Overview
Basic execution environment – an Intel example
What is an operating system (OS)?
OS components and services (extended in later lectures)
Interrupts
Booting, protection, kernel organization

## Slide 3: Hardware
Central Processing Units (CPUs)
Memory (cache(s), RAM, ROM, Flash, …)
I/O Devices (network cards, disks, CD, keyboard, mouse, …)
Links (interconnects, busses, …)

## Slide 4: An easy, old example: Intel Hub Architecture (850 Chipset)
Intel D850MD Motherboard: Source: Intel® Desktop Board D850MD/D850MV Technical Product Specification

## Slide 5: An easy, old example: Intel Hub Architecture (850 Chipset)
Intel D850MD Motherboard: Source: Intel® Desktop Board D850MD/D850MV Technical Product Specification
Pentium 4 socket
RAMBUS RDRAM – 2 banks (4 slots)
Memory Controller Hub
PCI Connectors (slots)
I/O Controller Hub
system bus
RDRAM
interface
hub
interface
PCI
bus
Firmware Hub – including BIOS
Battery
Speaker
Power connector
Diskette connector
IDE drive connectors
AGP slot
Video
mouse, keyboard, parallel, serial, network and USB connectors

## Slide 6: An easy, old example: Intel Hub Architecture (850 Chipset)
Pentium 4
Processor
registers
cache(s)
I/O
controller
hub
memory
controller
hub
RDRAM
RDRAM
RDRAM
RDRAM
PCI slots
PCI slots
PCI slots
system bus
(64-bit, 400/533 MHz ~24-32 Gbps)
hub interface
(four 8-bit, 66 MHz  2 Gbps)
PCI bus
(32-bit, 33 MHz  1 Gbps)
RAM interface
(two 64-bit, 200 MHz  ~24 Gbps)
disk
file system
application
disk
Notes: Talk about bottlenecks

## Slide 7: A slightly newer example: Intel Platform Controller Hub Architecture
Flexible Display Interface (FDI)
Pentium 4
Processor
registers
cache(s)
PCI slots
PCI slots
PCI slots
Core i7
registers
cache(s)
PCIe
iGraphics
RDRAM
RDRAM
I/O
controller
hub
PCH
Platform
Controller
Hub
PCIe slots
PCIe slots
PCIe slots
Direct Media Interface (DMI) / QuickPath Interconnect (QPI)
Peripherals
Sandy Bridge, Core i7
RDRAM
RDRAM
integrated
memory
controller
memory
controller
hub
Notes: PCIe – ×1, ×4, ×8, ×16, ×32 , version1 = 2 Gb/s, v2 = 4Gb, v3 = 8Gb, v4 = 16Gb per lane, both directions
QPI = 12.8 GBytes/s each way (26.6)  100 Gb/s each way

## Slide 8: Other examples: AMD Opteron & Intel Xeon
Intel Xeon MP Processor-based 4P
Different hardware may have different bottlenecks ==> nice to have an operating system to control the HW?

## Slide 9: Different Hardware
Hardware X
Hardware Y
Operating System
Application program
Operating System
Application program
Application
Application

## Slide 10: Intel 32-bit Architecture (IA32): Basic Execution Environment
Address space: 1 – 236 (64 GB), each process may have a linear address space of 4 GB (232)
Basic program execution registers:
  8 general purpose registers (data: EAX, EBX, ECX, EDX, address: ESI, EDI, EBP, ESP)
  6 segment registers (CS, DS, SS, ES, FS and GS)
  1 flag register (EFLAGS)
  1 instruction pointer register (EIP)
Stack – a continuous array of memory locations
  Current stack is referenced by the SS register
  ESP register – stack pointer
  EBP register – stack frame base pointer (fixed reference)
  PUSH – stack grows, add item (ESP decrement)
  POP – remove item, stack shrinks (ESP increment)
Several other registers like Control, MMX/FPU (MM/R), Memory Type Range Registers (MTRRs), SSEx (XMM), AVX (YMM), performance monitoring, …
...
STACK:
PUSH %eax
ESP pointer:
X
Y
PUSH %ebx
EAX:
EBX:
ECX:
EDX:
ESI:
EDI:
EBP:
ESP: see arrow
GPRs:
X
Y
POP %ebx
POP %eax
<do something>
0xfff...
0x0...
Notes: General data registers
All of the four following registers may be used as general purpose registers. However each has some specialized purpose as well. Each of these registers also have 16-bit or 8-bit subset names.
EAX (At 000) Dedicated accumulator which is used for all major calculations.
ECX (At 001) The universal loop counter which has a special interpretation for loops.
EDX (At 010) The data register, which is an extension to the accumulator, stores data relevant to the operation applied to the accumulator.
EBX (At 011) Currently used for free storage but was originally used as a pointer in 16-bit mode
General address registers
Used only for address pointing. They have 16-bit subset names, but no 8-bit subsets.
ESP (At 100) Stack pointer. Is used to hold the top address of the stack.
EBP (At 101) Base pointer. Is used to hold the address of the current stack frame. It is also sometimes used as free storage.
ESI (At 110) Source index. Commonly used for string operations. It has a one-byte opcode for loading data from memory to the accumulator.
EDI (At 111) Destination index. Commonly used for string operations. Has a one-byte STOS instruction to write data out of the accumulator.
EIP Instruction pointer. Holds the current instruction address
STACK-FRAME BASE POINTER
The stack is typically divided into frames. Each stack frame can then contain local variables,
parameters to be passed to another procedure, and procedure linking information. The stackframe
base pointer (contained in the EBP register) identifies a fixed reference point within the
stack frame for the called procedure. To use the stack-frame base pointer, the called procedure
typically copies the contents of the ESP register into the EBP register prior to pushing any local
variables on the stack. The stack-frame base pointer then permits easy access to data structures
passed on the stack, to the return instruction pointer, and to local variables added to the stack by
the called procedure.

## Slide 11: Intel 32-bit Architecture (IA32): Basic Execution Environment
insert value 4 in variable a on stack:
0xfffffffc = -(0xffffffff – 0xfffffffc) = -0x4
a’s memory address = EBP - 4
Example:
main (void)
{
int a = 4, b = 2, c = 0;
c = a + b;
}
…
…
code segment:
8048314 <main>:
8048314: push %ebp
8048315: mov %esp,%ebp
8048317: sub $0x18,%esp
804831a: and $0xfffffff0,%esp
804831c: mov $0x0,%eax
8048322: sub %eax,%esp
8048324: movl $0x4,0xfffffffc(%ebp)
804832b: movl $0x2,0xfffffff8(%ebp)
8048332: movl $0x0,0xfffffff4(%ebp)
8048339: mov 0xfffffff8(%ebp),%eax
804833c: add 0xfffffffc(%ebp),%eax
804833f: mov %eax,0xfffffff4(%ebp)
8048342: leave
8048343: ret
objdump -d
...
...
...
stack:
0
2
4
6
0xfff...
0x0...
ESP:
EBP:
EPI:
EAX:
Accumulator for operands and results data
Stack pointer
Pointer to data on stack (base)
Pointer to next instruction to be executed
8048314
old EBP
8048315
8048317
804831a
804831c
8048322
8048324
804832b
8048332
8048339
804833c
804833f
8048342
0xfffffff4
???
0xfffffff0
0xfffffff0
0xffffffd8
0xffffffd0
0
2
6
…
sub 24 (0x18) bytes (add space for 24 bytes)
alignment – sub "X" (here 8) bytes
8048343

## Slide 12: C Function Calls & Stack
A calling function does
  push the parameters into stack in reverse order
  push return address (current EIP value) onto stack
When called, a C function does
  push frame pointer (EBP) into stack - saves frame pointer register and gives easy return if necessary
  let frame pointer point at the stack top, i.e., point at the saved stack pointer (EBP = ESP)
  shift stack pointer (ESP) upward (to lower addresses) to allocate space for local variables
When returning, a C function does
  put return value in the return value register (EAX)
  copy frame pointer into stack pointer - stack top now contains the saved frame pointer
  pop stack into frame pointer (restore), leaving the return program pointer on top of the stack
  the RET instruction pops the stack top into the program counter register (EIP), causing the CPU to execute from the "return address" saved earlier
When returned to calling function, it does
  copy the return value (EAX) into right place
  pop parameters – restore the stack
int add (int a, int b)
{
return a + b;
}
main (void)
{
int c = 0;
c = add(4 , 2);
}

## Slide 13: C Function Calls & Stack
…
...
Example:
int add (int a, int b)
{
return a + b;
}
main (void)
{
int c = 0;
c = add(4 , 2);
}
code segment:
objdump -d
...
...
0
2
4
804834a
6
stack:
0xfff...
0x0...
old EBP
Push EIP register
Loads the offset of the called procedure in the EIP register
Begin execution
“main” EBP
Pop return instruction pointer into the EIP register
Release parameters (ESP)
Resume caller execution
8048314 <add>:
8048314: push %ebp
8048315: mov %esp,%ebp
8048317: mov 0xc(%ebp),%eax
804831a: add 0x8(%ebp),%eax
804831d: pop %ebp
804831e: ret
804831f <main>:
804831f: push %ebp
8048320: mov %esp,%ebp
8048322: sub $0x18,%esp
8048325: and $0xfffffff0,%esp
8048328: mov $0x0,%eax
804832d: sub %eax,%esp
804832f: movl $0x0,0xfffffffc(%ebp)
8048336: movl $0x2,0x4(%esp)
804833e: movl $0x4,(%esp)
8048345: call 8048314 <add>
804834a: mov %eax,0xfffffffc(%ebp)
804834d: leave
804834e: ret
804834f: nop
insert value 0 in variable a on stack:
0xfffffffc = -(0xffffffff – 0xfffffffc) = -0x4
c’s memory address = EBP - 4
Wouldn't it be nice if this could be automatically managed!!??  operating system

## Slide 14: C Function Calls & Stack
…
...
int add (int a, int b)
{
return a + b;
}
main (void)
{
int c = 0;
c = add(4 , 2);
}
code segment:
...
...
0
2
4
804834a
6
stack:
0xfff...
0x0...
old EBP
Push EIP register
Loads the offset of the called procedure in the EIP register
Begin execution
“main” EBP
Pop return instruction pointer into the EIP register
Release parameters (ESP)
Resume caller execution
8048314 <add>:
8048314: push %ebp
8048315: mov %esp,%ebp
8048317: mov 0xc(%ebp),%eax
804831a: add 0x8(%ebp),%eax
804831d: pop %ebp
804831e: ret
804831f <main>:
804831f: push %ebp
8048320: mov %esp,%ebp
8048322: sub $0x18,%esp
8048325: and $0xfffffff0,%esp
8048328: mov $0x0,%eax
804832d: sub %eax,%esp
804832f: movl $0x0,0xfffffffc(%ebp)
8048336: movl $0x2,0x4(%esp)
804833e: movl $0x4,(%esp)
8048345: call 8048314 <add>
804834a: mov %eax,0xfffffffc(%ebp)
804834d: leave
804834e: ret
804834f: nop
extra copy
for handout
insert value 0 in variable a on stack:
0xfffffffc = -(0xffffffff – 0xfffffffc) = -0x4
c’s memory address = EBP - 4

## Slide 15: Many Concurrent Tasks
Better use & utilization
  many concurrent processes
    performing different tasks
    using different parts of the machine
  many concurrent users
Challenges
  “concurrent” access
  protection/security
  fairness
  …
Operating System Layer
Notes: Bedre utnyttelse av maskinen ved at
  Man kjører flere programmer samtidig
    Skriver i en teksteditor samtidig som
    mailsystemet sjekker om det er mail til deg, og
    Klokken på skjermen oppdateres hvert sekund
    ...
  Flere brukere på samme maskin
    Flere kan være logget inn på ”mjollnir” samtidig
    Hver av disse kan kjøre flere programmer
  Flere prosesser på samme maskin
    En som trenger mye diskIO (Web-server), og
    en som trenger mye CPU-kapasitet (f.eks. vitenskapelige beregninger)
De forskjellige former for samtidighet gir tilleggsproblemer
  Hvordan kjøre flere programmer ”samtidig” på en CPU?
  Hvordan sørge for at de forskjellige programmene ikke går i bena på hverandre (overskriver hverandres data f.eks.)
  Hvordan kontrollere de forskjellige programmenes tilgang til skjerm, disk, skriver, nettverk?

## Slide 16: Many Concurrent Tasks
Better use & utilization
  many concurrent processes
    performing different tasks
    using different parts of the machine
  many concurrent users
Challenges
  “concurrent” access
  protection/security
  fairness
  …
Operating System Layer
extra copy
for handout

## Slide 17: What is an Operating System (OS)?
“An operating system (OS) is a collection of programs that acts as an intermediary between the hardware and its user(s), providing a high-level interface to low level hardware resources, such as the CPU, memory, and I/O devices. The operating system provides various facilities and services that make the use of the hardware convenient, efficient and safe” Lazowska, E. D.: Contemporary Issues in Operating Systems , in: Encyclopedia of Computer Science, Ralston, A., Reilly, E. D. (Editors), IEEE Press, 1993, pp.980
It is an extended machine (top-down view)
  Hides the messy details
  Presents a virtual machine, easier to use
It is a resource manager (bottom-up view)
  Each program gets time/space on the resource
hardware
user
application
operating system

## Slide 18: Where do we find OSes?
Computers
Cars
cameras,
other vehicles/crafts,
set-top boxes,
watches,
sensors,
…  EVERYWHERE
Phones
Game Boxes

## Slide 19: Operating System Categories
Single-user, single-task: historic, and rare (only a few PDAs use this)
Single-user, multi-tasking: PCs and workstations may be configured like this
Multi-user, multi-tasking: used on large, old mainframes; and handhelds, PCs, workstations and servers today
Distributed OSes: support for administration of distributed resources
Real-time OSes: support for systems with real-time requirements like cars, nuclear reactors, etc.
Embedded OSes: built into a device to control a specific type of equipment like cellular phones, micro waves, washing machines, etc.

## Slide 20: History
OSes have evolved over the last 60 years
Early history (’40s and early ’50s):
  first machines did not include OSes
  programmed using mechanical switches or wires
Second generation (’50s and ’60s):
  transistors introduced in mid-’50s
  batch systems
  card readers

## Slide 21: History
Third generation (mid-’60s to the ’80s)
  integrated circuits and simple multiprogramming
  timesharing
  graphical user interface
  UNIX (’69-’70)
  BSD (’77)
Newer times (’80s to present)
  personal computers & workstations
  MS-DOS (’82), SunOS (’82), Mac System Software (’84), Win (’85), Minix (’87), OS/2 (’87)
  Linux (’91), Solaris (’92), WinNT (’93), Win95, MacOS (’96), MacOS 9 (’99)
  Linux 2.4 (’01), Mac OS X (’01), Linux 2.6 (’03), WinVista (’06), Win7 (’09)
  Linux 3.0 (’11), Win8 (’12), , MacOS X Yosemite (’14), Win10 (’15) , Linux 4.0 (’15), MacOS X El Capitan (’15?)

## Slide 22: So, why study OSes?
“I will never write an operating system from scratch, nor even touch a line of code in the kernel”
“Operating systems have existed for decades, what more can be added?”
“I just need to know the API to give the system commands in order to store my data and run my programs”
“Writing programs in Java is very easy and I do not need to know anything about operating systems to make it work”
Consider the following example, does it matter which one to use?:
int data[32768][32768];
for (j = 0; j < 32768; j++)
for (i = 0; i < 32768; i++) data[i,j] = i*j;
int data[32768][32768];
for (i = 0; i < 32768; i++)
for (j = 0; j < 32768; j++) data[i,j] = i*j;
Notes: Example: same result – YES
same number of loops – YES
same speed – NO, memory operations
Yes the program wil segfault since the array is larger than the max array size in C…

## Slide 23: So, why study OSes?
To do things right and efficient, one must know how computers and operating systems work
  operating systems provide magic to provide “infinite” CPU cycles, “endless” memory, transparent access to devices, networked computing, etc.
  operating systems manage concurrency and sharing
  understand the tradeoffs between performance and functionality, division of labor between HW and SW
OSes are found everywhere and are therefore key components in many systems

## Slide 24: Primary Components
User interface
(shell)
Device
management
File
management
Memory
management
Processor
(or process)
management
Communication
services
Operating system layer
Application program layer
Hardware layer
"Visible" to user
  Shell
  File system
  Device management
"(Semi)Transparent"
  Processor management
  Memory management
  Communication services
Notes: Visible / transparent depend on the level…

## Slide 25: Primary Components
User interface
(shell)
Device
management
File
management
Memory
management
Processor
(or process)
management
Communication
services
Operating system layer
Application program layer
Hardware layer
File Management (file system):
provides a mechanism for the user to create, delete, modify and manipulate files
Memory Management:
provides a mechanism for the system to efficiently manage the system’s
memory recourses – allocating space to processes
User Interface:
provides a mechanism for user and
application to communicate with OS
and use the machine resources
Management of processes:
provides a mechanism for the system to efficiently and fair manage the
machine CPU cycles for the running
processes
Communication:
provides a mechanism for the system communicate with other processes (on
same or another machine)
Device Management:
provides the system with means to
control the systems peripheral devices like keyboard, display, printer and disk

## Slide 26: Device Management
The OS must be able to control pheripal devices such as disks, keyboard, network cards, screen, speakers, mouse, memory sticks, camera, DVD, michrophone, printers, joysticks, ...
  large diversity
  varying speeds
  different access modes
Rest of the
operating
system
Device
driver
Device
driver
.
.
.
Device
driver
Device
controller
Device
controller
.
.
.
Device
controller
Device
Device
Device
Device

## Slide 27: Device Management
Rest of the
operating
system
Device
driver
Device
driver
.
.
.
Device
driver
Device
controller
Device
controller
.
.
.
Device
controller
Device
Device
Device
Device
Device controllers often have registers to hold status, give commands, …
  port I/O – special instructions to talk to device memory
  memory mapped I/O – registers mapped into regular memory
Each device may be different and require device-spesific software
The software talking to the controller and giving commands is often called a device driver
  usually running within the kernel
  usually provided by the device vendors
  translating device-independent commands, e.g., read from file on disk: logical block number  device interface (device, cylinder, head, sector)
A huge amount of code (95% of the Linux code!!??)
Notes: https://www.linuxcounter.net/statistics/kernel:
2003 - Linux 2.6.0 had 4.700.000lines of code
2015 – Linux 4 has 15.500.000 lines of code

## Slide 28: Device Management
Device controllers often have registers to hold status, give commands, …
  port I/O – special instructions to talk to device memory
  memory mapped I/O – registers mapped into regular memory
Each device may be different and require device-spesific software
The software talking to the controller and giving commands is often called a device driver
  usually running within the kernel
  usually provided by the device vendors
  translating device-independent commands, e.g., read from file on disk: logical block number  device, cylinder, head, sector(s)
A huge amount of code (95% of the Linux code!!??)
extra copy
for handout

## Slide 29: Interfaces
A point of connection between components
The OS incorporates logic that support interfaces with both hardware and applications, e.g.,
  command line interface, e.g., a shell
  graphical user interface (GUI)
    interface consisting of windows, icons, menus and pointers
    often not part of the OS (at least not kernel), but an own program
  …
Example: X (see man X)
  network transparent window system running on most ANSI C and POSIX (portable OS interface for UNIX) compliant systems
  uses inter-process communication to get input from and send output to various client programs
  xdm (X Display Manager) – usually set by administrator to run automatically at boot time
  xinit – manually starting X (startx, x11, xstart, …)

## Slide 30: Windows Interfaces
The GUI incorporates a
command line shell similar to the MS-DOS interface
Applications access HW
through the API consisting of
a set of routines, protocols and
other tools

## Slide 31: The WinXP Desktop Interface
Taskbar
Start button
Notification area

## Slide 32: UNIX Interfaces
Applications are accessed HW through the API consisting of a set of routines, protocols and other tools (e.g., POSIX – portable OS interface for UNIX)
A user can interact with the system through the application interface or using a command line prosessed by a shell (not really a part of the OS)
A plain command line interface may be hard to use. Many UNIX systems therefore have a standard graphical interface (X Windows) which can run a desktop system (like KDE, Gnome, Fvwm, Afterstep, …)
Windows is more or less similar…

## Slide 33: A Linux (KDE) Desktop Interface
Application Starter
Virtual Desktops
Panel
Taskbar
Desktop

## Slide 34: Typical (UNIX) Line Commands

## Slide 35: System Calls
The interface between the OS and users is defined by a set of system calls
Making a system call is similar to a procedure/function call, but system calls enter the kernel:
application
application
application
user space
kernel space
system call interface
OS components
Linux:
x86 v2.4.19 entry.S  242
x86 v3.0-rc4 syscall_table_32.S  347
x86 v3.16.2 syscall_32.tbl  353
FreeBSD:
v9 syscalls.c  531

## Slide 36: System Calls: read
C example: count = read(fd,buffer,nbyte)
push parameters on stack
call library code
put system call number in register
call kernel (TRAP)
  kernel examines system call number
  finds requested system call handler
  execute requested operation
return to library and clean up
  increase instruction pointer
  remove parameters from stack
resume process
application
user space
kernel space
count = read (fd , buffer , nbytes)
read library
procedure
register
memory (stack)
buffer
nbytes
buffer
fd
X (read)
system call
handler
X
sys_read()

## Slide 37: Interrupt Program Execution
CPU
We may use “polling”…!?

## Slide 38: Interrupts
Interrupts are electronic signals that (usually) result in a forced transfer of control to an interrupt handling routine
  alternative to polling
  caused by asynchronous events like finished disk operations, incoming network packets, expired timers, …
  an interrupt descriptor table (IDT) associates each interrupt with a code descriptor (pointer to code segment)
  can be disabled or masked out

## Slide 39: Exceptions
Another way for the processor to interrupt program execution is exceptions
  caused by synchronous events generated when the processor detects a predefined condition while executing an instruction
  TRAPS: the processor reaches a condition the exception handler can handle (e.g., overflow, break point in code like making a system call, …)
  FAULTS: the processor reaches a fault the exception handler can correct (e.g., division by zero, wrong data format, …)
  ABORTS: terminate the process due to an unrecoverable error (e.g., hardware failure) which the process itself cannot correct
  the processor responds to exceptions (i.e., traps and faults) essentially as for interrupts

## Slide 40: Interrupt (and Exception) Handling
The IA-32 has an interrupt description table (IDT) with 256 entries for interrupts and exceptions
  32 (0 - 31) predefined and reserved
  224 (32 - 255) is "user" (operating system) defined
Each interrupt is associated with a code segment through the IDT and a unique index value giving management like this:
  process running while interrupt occur
  capture state, switch control and find right interrupt handler
  execute the interrupt handler
  restore interrupted process
  continue execution
user
kernel
IDT:
disk interrupt (x)
Interrupt routines:

## Slide 41: Booting
Memory is a volatile, limited resource: OS usually on disk
Most motherboards contain a basic input/output system (BIOS) chip (often flash RAM) – stores instructions for basic HW initialization and management, and initiates the …
... bootstrap: loads the OS into memory
  read the boot program from a known location on secondary storage typically first sector(s), often called master boot record (MBR)
  run boot program
    read root file system and locate file with OS kernel
    load kernel into memory
    run kernel

## Slide 42: Booting
boot
OS
boot
OS
Gather HW information and set up system
Load data from boot sector
Execute boot program an CPU
Load OS from disk
Run OS

## Slide 43: User Level vs. Kernel Level (Protection)
Many OSes distinguish user and kernel level, i.e., due to security and protection
Usually, applications and many sub-systems run in user mode (pentium level 3)
  protected mode
  not allowed to access HW or device drivers directly, only through an API
  access to assigned memory only
  limited instruction set
OSes run in kernel mode (under the virtual machine abstraction, pentium level 0)
  real mode
  access to the entire memory
  all instructions can be executed
  bypass security

## Slide 44: OS Organization
No standard describing how to organize a kernel (as it is for compilers, communication protocols, etc.) and several approaches exist, e.g.:
Monolithic kernels (“the big mess”):
  written as a collection of functions linked into a single object
  usually efficient (no boundaries to cross)
  large, complex, easy to crash
  UNIX, Linux, …
Micro kernels
  kernel with minimal functionality (managing interrupts, memory, processor)
  other services are implemented in server processes running in user space used in a client-server model
  lot of message passing (inefficient)
  small, modular, extensible, portable, …
  MACH, L4, Chorus, …

## Slide 45: Virtualization
People would like to save money, save energy, reduce the number of machines, be secure, easily move services, etc.… and still run multiple OSes, applications, etc…
Virtualization
  many types of virtualization – server/machine virtualization
  partitioning a physical server into several virtual servers, or machines
  interact independently/isolated with other devices, applications, data and users
Sandboxing scfss
Hardware
Hypervisor
Guest OS
Guest OS
Guest OS
App
App
App
Type 1 Hypervisor
VMWare ESX, XEN, Hyper-V
Hardware
Host OS
App
Guest OS
Guest OS
App
App
Hypervisor
Type 2 Hypervisor
KVM, VirtualBox, VMWare Workstation
Hardware
Host OS
App
App
App
Sandboxing
Sandboxing
sandboxie, bufferzone, libcontainer, runc, cgroups
App
App
App
Notes: Type 1 hypervisor interacts directly with hardware, independent from OS, boots before the OS, full control of HW – often called “native” or “bare-metal” hypervisors
Type 2 sits on top of OS, dependent on OS, boots after OS, if OS crash – all users are affected, not full control of HW
a sandbox is a security mechanism for separating running programs - executing the software in a restricted operating system environment, thus controlling the resources
These concepts address different problems: When we virtualize, we are hiding physical limitations of the machine. Sandboxing, on the other hand, sets artificial limits on access across a machine. Sandboxing means isolation only, when virtualization usually means simulating of some sort of hardware (virtual machine). Virtualization can happen with our without sandboxing.

## Slide 46: Summary
OSes are found “everywhere” and provide virtual machines and work as a resource managers
Many components providing different services
Users access the services using an interface like system calls
In the next lectures, we look closer at some of the main components and abstractions in an OS
  processes management
  memory management
  storage management
  local inter-process communication
  inter-computer network communication is covered in the last part of the course